## Slide 1: Amateur Radio General License Exam (valid July 1, 2015 – June 30, 2019)
Copyright © 2017 Herb Weiner
herbw@wiskit.com
http://www.herbweiner.com
Notes: Presentation generated using SlideMight: https://slidemight.com

## Slide 2
Subelement |  | Groups | Questions
G1 | Commission's Rules | 5 | 60
G2 | Operating Procedures | 5 | 59
G3 | Radio Wave Propagation | 3 | 41
G4 | Amateur Radio Practices | 5 | 65
G5 | Electrical Principles | 3 | 44
G6 | Circuit Components | 2 | 36
G7 | Practical Circuits | 3 | 37
G8 | Signals and Emissions | 3 | 32
G9 | Antennas and Feed Lines | 4 | 58
G0 | Electrical and RF Safety | 2 | 27
Notes: This slide lists all Subelements. The first column contains clickable hyperlinks for easy access to each Subelement.

## Slide 3
Group |  | Questions
G1A | General Class control operator frequency privileges; primary and secondary allocations | 14
G1B | Antenna structure limitations; good engineering and good amateur practice; beacon operation; prohibited transmissions; retransmitting radio signals | 12
G1C | Transmitter power regulations; data emission standards | 11
G1D | Volunteer Examiners and Volunteer Examiner Coordinators; temporary identification | 11
G1E | Control categories; repeater regulations; harmful interference; third party rules; ITU regions; automatically controlled digital station | 12
5 | Total | 60
Subelement G1 Commission's Rules
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 4
G1A01
G1A02
G1A03
G1A04
G1A05
G1A06
G1A07
G1A08
G1A09
G1A10
G1A11
G1A12
G1A13
G1A14
Commission's Rules
Group G1A (14 Questions)
General Class control operator frequency privileges; primary and secondary allocations
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 5
 | G1A01 ~ On which of the following bands is a General Class license holder granted all amateur frequency privileges? | 
 |  | 60, 20, 17, and 12 meters
 |  | 160, 80, 40, and 10 meters
 |  | 160, 60, 30, 17, 12, and 10 meters
 |  | 160, 30, 17, 15, 12, and 10 meters
 | FCC | 97.301(d)
 | G1A01 ~ On which of the following bands is a General Class license holder granted all amateur frequency privileges? | 
 |  | 60, 20, 17, and 12 meters
 |  | 160, 80, 40, and 10 meters
 |  | 160, 30, 17, 15, 12, and 10 meters
 | G1A01 ~ On which of the following bands is a General Class license holder granted all amateur frequency privileges? | 
 | A. | 60, 20, 17, and 12 meters
 | B. | 160, 80, 40, and 10 meters
 | C. | 160, 60, 30, 17, 12, and 10 meters
 | D. | 160, 30, 17, 15, 12, and 10 meters
Commission's Rules
Group G1A

## Slide 6
 | G1A02 ~ On which of the following bands is phone operation prohibited? | 
 |  | 160 meters
 |  | 30 meters
 |  | 17 meters
 |  | 12 meters
 | FCC | 97.305
 | G1A02 ~ On which of the following bands is phone operation prohibited? | 
 |  | 160 meters
 |  | 17 meters
 |  | 12 meters
 | G1A02 ~ On which of the following bands is phone operation prohibited? | 
 | A. | 160 meters
 | B. | 30 meters
 | C. | 17 meters
 | D. | 12 meters
Commission's Rules
Group G1A

## Slide 7
 | G1A03 ~ On which of the following bands is image transmission prohibited? | 
 |  | 160 meters
 |  | 30 meters
 |  | 20 meters
 |  | 12 meters
 | FCC | 97.305
 | G1A03 ~ On which of the following bands is image transmission prohibited? | 
 |  | 160 meters
 |  | 20 meters
 |  | 12 meters
 | G1A03 ~ On which of the following bands is image transmission prohibited? | 
 | A. | 160 meters
 | B. | 30 meters
 | C. | 20 meters
 | D. | 12 meters
Commission's Rules
Group G1A

## Slide 8
 | G1A04 ~ Which of the following amateur bands is restricted to communication on only specific channels, rather than frequency ranges? | 
 |  | 11 meters
 |  | 12 meters
 |  | 30 meters
 |  | 60 meters
 | FCC | 97.303 (h)
 | G1A04 ~ Which of the following amateur bands is restricted to communication on only specific channels, rather than frequency ranges? | 
 |  | 11 meters
 |  | 12 meters
 |  | 30 meters
 | G1A04 ~ Which of the following amateur bands is restricted to communication on only specific channels, rather than frequency ranges? | 
 | A. | 11 meters
 | B. | 12 meters
 | C. | 30 meters
 | D. | 60 meters
Commission's Rules
Group G1A

## Slide 9
 | G1A05 ~ Which of the following frequencies is in the General Class portion of the 40-meter band? | 
 |  | 7.250 MHz
 |  | 7.500 MHz
 |  | 40.200 MHz
 |  | 40.500 MHz
 | FCC | 97.301(d)
 | G1A05 ~ Which of the following frequencies is in the General Class portion of the 40-meter band? | 
 |  | 7.500 MHz
 |  | 40.200 MHz
 |  | 40.500 MHz
 | G1A05 ~ Which of the following frequencies is in the General Class portion of the 40-meter band? | 
 | A. | 7.250 MHz
 | B. | 7.500 MHz
 | C. | 40.200 MHz
 | D. | 40.500 MHz
Commission's Rules
Group G1A

## Slide 10
 | G1A06 ~ Which of the following frequencies is within the General Class portion of the 75-meter phone band? | 
 |  | 1875 kHz
 |  | 3750 kHz
 |  | 3900 kHz
 |  | 4005 kHz
 | FCC | 97.301(d)
 | G1A06 ~ Which of the following frequencies is within the General Class portion of the 75-meter phone band? | 
 |  | 1875 kHz
 |  | 3750 kHz
 |  | 4005 kHz
 | G1A06 ~ Which of the following frequencies is within the General Class portion of the 75-meter phone band? | 
 | A. | 1875 kHz
 | B. | 3750 kHz
 | C. | 3900 kHz
 | D. | 4005 kHz
Commission's Rules
Group G1A

## Slide 11
 | G1A07 ~ Which of the following frequencies is within the General Class portion of the 20-meter phone band? | 
 |  | 14005 kHz
 |  | 14105 kHz
 |  | 14305 kHz
 |  | 14405 kHz
 | FCC | 97.301(d)
 | G1A07 ~ Which of the following frequencies is within the General Class portion of the 20-meter phone band? | 
 |  | 14005 kHz
 |  | 14105 kHz
 |  | 14405 kHz
 | G1A07 ~ Which of the following frequencies is within the General Class portion of the 20-meter phone band? | 
 | A. | 14005 kHz
 | B. | 14105 kHz
 | C. | 14305 kHz
 | D. | 14405 kHz
Commission's Rules
Group G1A

## Slide 12
 | G1A08 ~ Which of the following frequencies is within the General Class portion of the 80-meter band? | 
 |  | 1855 kHz
 |  | 2560 kHz
 |  | 3560 kHz
 |  | 3650 kHz
 | FCC | 97.301(d)
 | G1A08 ~ Which of the following frequencies is within the General Class portion of the 80-meter band? | 
 |  | 1855 kHz
 |  | 2560 kHz
 |  | 3650 kHz
 | G1A08 ~ Which of the following frequencies is within the General Class portion of the 80-meter band? | 
 | A. | 1855 kHz
 | B. | 2560 kHz
 | C. | 3560 kHz
 | D. | 3650 kHz
Commission's Rules
Group G1A

## Slide 13
 | G1A09 ~ Which of the following frequencies is within the General Class portion of the 15-meter band? | 
 |  | 14250 kHz
 |  | 18155 kHz
 |  | 21300 kHz
 |  | 24900 kHz
 | FCC | 97.301(d)
 | G1A09 ~ Which of the following frequencies is within the General Class portion of the 15-meter band? | 
 |  | 14250 kHz
 |  | 18155 kHz
 |  | 24900 kHz
 | G1A09 ~ Which of the following frequencies is within the General Class portion of the 15-meter band? | 
 | A. | 14250 kHz
 | B. | 18155 kHz
 | C. | 21300 kHz
 | D. | 24900 kHz
Commission's Rules
Group G1A

## Slide 14
 | G1A10 ~ Which of the following frequencies is available to a control operator holding a General Class license? | 
 |  | 28.020 MHz
 |  | 28.350 MHz
 |  | 28.550 MHz
 |  | All of these choices are correct
 | FCC | 97.301(d)
 | G1A10 ~ Which of the following frequencies is available to a control operator holding a General Class license? | 
 |  | 28.020 MHz
 |  | 28.350 MHz
 |  | 28.550 MHz
 | G1A10 ~ Which of the following frequencies is available to a control operator holding a General Class license? | 
 | A. | 28.020 MHz
 | B. | 28.350 MHz
 | C. | 28.550 MHz
 | D. | All of these choices are correct
Commission's Rules
Group G1A

## Slide 15
 | G1A11 ~ When General Class licensees are not permitted to use the entire voice portion of a particular band, which portion of the voice segment is generally available to them? | 
 |  | The lower frequency end
 |  | The upper frequency end
 |  | The lower frequency end on frequencies below 7.3 MHz and the upper end on frequencies above 14.150 MHz
 |  | The upper frequency end on frequencies below 7.3 MHz and the lower end on frequencies above 14.150 MHz
 | FCC | 97.301
 | G1A11 ~ When General Class licensees are not permitted to use the entire voice portion of a particular band, which portion of the voice segment is generally available to them? | 
 |  | The lower frequency end
 |  | The lower frequency end on frequencies below 7.3 MHz and the upper end on frequencies above 14.150 MHz
 |  | The upper frequency end on frequencies below 7.3 MHz and the lower end on frequencies above 14.150 MHz
 | G1A11 ~ When General Class licensees are not permitted to use the entire voice portion of a particular band, which portion of the voice segment is generally available to them? | 
 | A. | The lower frequency end
 | B. | The upper frequency end
 | C. | The lower frequency end on frequencies below 7.3 MHz and the upper end on frequencies above 14.150 MHz
 | D. | The upper frequency end on frequencies below 7.3 MHz and the lower end on frequencies above 14.150 MHz
Commission's Rules
Group G1A

## Slide 16
 | G1A12 ~ Which of the following applies when the FCC rules designate the Amateur Service as a secondary user on a band? | 
 |  | Amateur stations must record the call sign of the primary service station before operating on a frequency assigned to that station
 |  | Amateur stations are allowed to use the band only during emergencies
 |  | Amateur stations are allowed to use the band only if they do not cause harmful interference to primary users
 |  | Amateur stations may only operate during specific hours of the day, while primary users are permitted 24 hour use of the band
 | FCC | 97.303
 | G1A12 ~ Which of the following applies when the FCC rules designate the Amateur Service as a secondary user on a band? | 
 |  | Amateur stations must record the call sign of the primary service station before operating on a frequency assigned to that station
 |  | Amateur stations are allowed to use the band only during emergencies
 |  | Amateur stations may only operate during specific hours of the day, while primary users are permitted 24 hour use of the band
 | G1A12 ~ Which of the following applies when the FCC rules designate the Amateur Service as a secondary user on a band? | 
 | A. | Amateur stations must record the call sign of the primary service station before operating on a frequency assigned to that station
 | B. | Amateur stations are allowed to use the band only during emergencies
 | C. | Amateur stations are allowed to use the band only if they do not cause harmful interference to primary users
 | D. | Amateur stations may only operate during specific hours of the day, while primary users are permitted 24 hour use of the band
Commission's Rules
Group G1A

## Slide 17
 | G1A13 ~ What is the appropriate action if, when operating on either the 30-meter or 60-meter bands, a station in the primary service interferes with your contact? | 
 |  | Notify the FCCs regional Engineer in Charge of the interference
 |  | Increase your transmitter's power to overcome the interference
 |  | Attempt to contact the station and request that it stop the interference
 |  | Move to a clear frequency or stop transmitting
 | FCC | 97.303(h)(2)(j)
 | G1A13 ~ What is the appropriate action if, when operating on either the 30-meter or 60-meter bands, a station in the primary service interferes with your contact? | 
 |  | Notify the FCCs regional Engineer in Charge of the interference
 |  | Increase your transmitter's power to overcome the interference
 |  | Attempt to contact the station and request that it stop the interference
 | G1A13 ~ What is the appropriate action if, when operating on either the 30-meter or 60-meter bands, a station in the primary service interferes with your contact? | 
 | A. | Notify the FCCs regional Engineer in Charge of the interference
 | B. | Increase your transmitter's power to overcome the interference
 | C. | Attempt to contact the station and request that it stop the interference
 | D. | Move to a clear frequency or stop transmitting
Commission's Rules
Group G1A

## Slide 18
 | G1A14 ~ In what ITU region is operation in the 7.175 to 7.300 MHz band permitted for a control operator holding an FCC issued General Class license? | 
 |  | Region 1
 |  | Region 2
 |  | Region 3
 |  | All three regions
 | FCC | 97.301(d)
 | G1A14 ~ In what ITU region is operation in the 7.175 to 7.300 MHz band permitted for a control operator holding an FCC issued General Class license? | 
 |  | Region 1
 |  | Region 3
 |  | All three regions
 | G1A14 ~ In what ITU region is operation in the 7.175 to 7.300 MHz band permitted for a control operator holding an FCC issued General Class license? | 
 | A. | Region 1
 | B. | Region 2
 | C. | Region 3
 | D. | All three regions
Commission's Rules
Group G1A

## Slide 19
G1B01
G1B02
G1B03
G1B04
G1B05
G1B06
G1B07
G1B08
G1B09
G1B10
G1B11
G1B12
Commission's Rules
Group G1B (12 Questions)
Antenna structure limitations; good engineering and good amateur practice; beacon operation; prohibited transmissions; retransmitting radio signals
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 20
 | G1B01 ~ What is the maximum height above ground to which an antenna structure may be erected without requiring notification to the FAA and registration with the FCC, provided it is not at or near a public use airport? | 
 |  | 50 feet
 |  | 100 feet
 |  | 200 feet
 |  | 300 feet
 | FCC | 97.15(a)
 | G1B01 ~ What is the maximum height above ground to which an antenna structure may be erected without requiring notification to the FAA and registration with the FCC, provided it is not at or near a public use airport? | 
 |  | 50 feet
 |  | 100 feet
 |  | 300 feet
 | G1B01 ~ What is the maximum height above ground to which an antenna structure may be erected without requiring notification to the FAA and registration with the FCC, provided it is not at or near a public use airport? | 
 | A. | 50 feet
 | B. | 100 feet
 | C. | 200 feet
 | D. | 300 feet
Commission's Rules
Group G1B

## Slide 21
 | G1B02 ~ With which of the following conditions must beacon stations comply? | 
 |  | A beacon station may not use automatic control
 |  | The frequency must be coordinated with the National Beacon Organization
 |  | The frequency must be posted on the Internet or published in a national periodical
 |  | There must be no more than one beacon signal transmitting in the same band from the same station location
 | FCC | 97.203(b)
 | G1B02 ~ With which of the following conditions must beacon stations comply? | 
 |  | A beacon station may not use automatic control
 |  | The frequency must be coordinated with the National Beacon Organization
 |  | The frequency must be posted on the Internet or published in a national periodical
 | G1B02 ~ With which of the following conditions must beacon stations comply? | 
 | A. | A beacon station may not use automatic control
 | B. | The frequency must be coordinated with the National Beacon Organization
 | C. | The frequency must be posted on the Internet or published in a national periodical
 | D. | There must be no more than one beacon signal transmitting in the same band from the same station location
Commission's Rules
Group G1B

## Slide 22
 | G1B03 ~ Which of the following is a purpose of a beacon station as identified in the FCC rules? | 
 |  | Observation of propagation and reception
 |  | Automatic identification of repeaters
 |  | Transmission of bulletins of general interest to Amateur Radio licensees
 |  | Identifying net frequencies
 | FCC | 97.3(a)(9)
 | G1B03 ~ Which of the following is a purpose of a beacon station as identified in the FCC rules? | 
 |  | Automatic identification of repeaters
 |  | Transmission of bulletins of general interest to Amateur Radio licensees
 |  | Identifying net frequencies
 | G1B03 ~ Which of the following is a purpose of a beacon station as identified in the FCC rules? | 
 | A. | Observation of propagation and reception
 | B. | Automatic identification of repeaters
 | C. | Transmission of bulletins of general interest to Amateur Radio licensees
 | D. | Identifying net frequencies
Commission's Rules
Group G1B

## Slide 23
 | G1B04 ~ Which of the following must be true before amateur stations may provide communications to broadcasters for dissemination to the public? | 
 |  | The communications must directly relate to the immediate safety of human life or protection of property and there must be no other means of communication reasonably available before or at the time of the event
 |  | The communications must be approved by a local emergency preparedness official and conducted on officially designated frequencies
 |  | The FCC must have declared a state of emergency
 |  | All of these choices are correct
 | FCC | 97.113(b)
 | G1B04 ~ Which of the following must be true before amateur stations may provide communications to broadcasters for dissemination to the public? | 
 |  | The communications must be approved by a local emergency preparedness official and conducted on officially designated frequencies
 |  | The FCC must have declared a state of emergency
 |  | All of these choices are correct
 | G1B04 ~ Which of the following must be true before amateur stations may provide communications to broadcasters for dissemination to the public? | 
 | A. | The communications must directly relate to the immediate safety of human life or protection of property and there must be no other means of communication reasonably available before or at the time of the event
 | B. | The communications must be approved by a local emergency preparedness official and conducted on officially designated frequencies
 | C. | The FCC must have declared a state of emergency
 | D. | All of these choices are correct
Commission's Rules
Group G1B

## Slide 24
 | G1B05 ~ When may music be transmitted by an amateur station? | 
 |  | At any time, as long as it produces no spurious emissions
 |  | When it is unintentionally transmitted from the background at the transmitter
 |  | When it is transmitted on frequencies above 1215 MHz
 |  | When it is an incidental part of a manned space craft retransmission
 | FCC | 97.113(c)
 | G1B05 ~ When may music be transmitted by an amateur station? | 
 |  | At any time, as long as it produces no spurious emissions
 |  | When it is unintentionally transmitted from the background at the transmitter
 |  | When it is transmitted on frequencies above 1215 MHz
 | G1B05 ~ When may music be transmitted by an amateur station? | 
 | A. | At any time, as long as it produces no spurious emissions
 | B. | When it is unintentionally transmitted from the background at the transmitter
 | C. | When it is transmitted on frequencies above 1215 MHz
 | D. | When it is an incidental part of a manned space craft retransmission
Commission's Rules
Group G1B

## Slide 25
 | G1B06 ~ When is an amateur station permitted to transmit secret codes? | 
 |  | During a declared communications emergency
 |  | To control a space station
 |  | Only when the information is of a routine, personal nature
 |  | Only with Special Temporary Authorization from the FCC
 | FCC | 97.113(a)(4) and 97.207(f)
 | G1B06 ~ When is an amateur station permitted to transmit secret codes? | 
 |  | During a declared communications emergency
 |  | Only when the information is of a routine, personal nature
 |  | Only with Special Temporary Authorization from the FCC
 | G1B06 ~ When is an amateur station permitted to transmit secret codes? | 
 | A. | During a declared communications emergency
 | B. | To control a space station
 | C. | Only when the information is of a routine, personal nature
 | D. | Only with Special Temporary Authorization from the FCC
Commission's Rules
Group G1B

## Slide 26
 | G1B07 ~ What are the restrictions on the use of abbreviations or procedural signals in the Amateur Service? | 
 |  | Only "Q" signals are permitted
 |  | They may be used if they do not obscure the meaning of a message
 |  | They are not permitted
 |  | Only "10 codes" are permitted
 | FCC | 97.113(a)(4)
 | G1B07 ~ What are the restrictions on the use of abbreviations or procedural signals in the Amateur Service? | 
 |  | Only "Q" signals are permitted
 |  | They are not permitted
 |  | Only "10 codes" are permitted
 | G1B07 ~ What are the restrictions on the use of abbreviations or procedural signals in the Amateur Service? | 
 | A. | Only "Q" signals are permitted
 | B. | They may be used if they do not obscure the meaning of a message
 | C. | They are not permitted
 | D. | Only "10 codes" are permitted
Commission's Rules
Group G1B

## Slide 27
 | G1B08 ~ When choosing a transmitting frequency, what should you do to comply with good amateur practice? | 
 |  | Insure that the frequency and mode selected are within your license class privileges
 |  | Follow generally accepted band plans agreed to by the Amateur Radio community
 |  | Monitor the frequency before transmitting
 |  | All of these choices are correct
 | FCC | 97.101(a)
 | G1B08 ~ When choosing a transmitting frequency, what should you do to comply with good amateur practice? | 
 |  | Insure that the frequency and mode selected are within your license class privileges
 |  | Follow generally accepted band plans agreed to by the Amateur Radio community
 |  | Monitor the frequency before transmitting
 | G1B08 ~ When choosing a transmitting frequency, what should you do to comply with good amateur practice? | 
 | A. | Insure that the frequency and mode selected are within your license class privileges
 | B. | Follow generally accepted band plans agreed to by the Amateur Radio community
 | C. | Monitor the frequency before transmitting
 | D. | All of these choices are correct
Commission's Rules
Group G1B

## Slide 28
 | G1B09 ~ When may an amateur station transmit communications in which the licensee or control operator has a pecuniary (monetary) interest? | 
 |  | When other amateurs are being notified of the sale of apparatus normally used in an amateur station and such activity is not done on a regular basis
 |  | Only when there is no other means of communications readily available
 |  | When other amateurs are being notified of the sale of any item with a monetary value less than $200 and such activity is not done on a regular basis
 |  | Never
 | FCC | 97.113(a)(3)
 | G1B09 ~ When may an amateur station transmit communications in which the licensee or control operator has a pecuniary (monetary) interest? | 
 |  | Only when there is no other means of communications readily available
 |  | When other amateurs are being notified of the sale of any item with a monetary value less than $200 and such activity is not done on a regular basis
 |  | Never
 | G1B09 ~ When may an amateur station transmit communications in which the licensee or control operator has a pecuniary (monetary) interest? | 
 | A. | When other amateurs are being notified of the sale of apparatus normally used in an amateur station and such activity is not done on a regular basis
 | B. | Only when there is no other means of communications readily available
 | C. | When other amateurs are being notified of the sale of any item with a monetary value less than $200 and such activity is not done on a regular basis
 | D. | Never
Commission's Rules
Group G1B

## Slide 29
 | G1B10 ~ What is the power limit for beacon stations? | 
 |  | 10 watts PEP output
 |  | 20 watts PEP output
 |  | 100 watts PEP output
 |  | 200 watts PEP output
 | FCC | 97.203(c)
 | G1B10 ~ What is the power limit for beacon stations? | 
 |  | 10 watts PEP output
 |  | 20 watts PEP output
 |  | 200 watts PEP output
 | G1B10 ~ What is the power limit for beacon stations? | 
 | A. | 10 watts PEP output
 | B. | 20 watts PEP output
 | C. | 100 watts PEP output
 | D. | 200 watts PEP output
Commission's Rules
Group G1B

## Slide 30
 | G1B11 ~ How does the FCC require an amateur station to be operated in all respects not specifically covered by the Part 97 rules? | 
 |  | In conformance with the rules of the IARU
 |  | In conformance with Amateur Radio custom
 |  | In conformance with good engineering and good amateur practice
 |  | All of these choices are correct
 | FCC | 97.101(a)
 | G1B11 ~ How does the FCC require an amateur station to be operated in all respects not specifically covered by the Part 97 rules? | 
 |  | In conformance with the rules of the IARU
 |  | In conformance with Amateur Radio custom
 |  | All of these choices are correct
 | G1B11 ~ How does the FCC require an amateur station to be operated in all respects not specifically covered by the Part 97 rules? | 
 | A. | In conformance with the rules of the IARU
 | B. | In conformance with Amateur Radio custom
 | C. | In conformance with good engineering and good amateur practice
 | D. | All of these choices are correct
Commission's Rules
Group G1B

## Slide 31
 | G1B12 ~ Who or what determines "good engineering and good amateur practice" as applied to the operation of an amateur station in all respects not covered by the Part 97 rules? | 
 |  | The FCC
 |  | The Control Operator
 |  | The IEEE
 |  | The ITU
 | FCC | 97.101(a)
 | G1B12 ~ Who or what determines "good engineering and good amateur practice" as applied to the operation of an amateur station in all respects not covered by the Part 97 rules? | 
 |  | The Control Operator
 |  | The IEEE
 |  | The ITU
 | G1B12 ~ Who or what determines "good engineering and good amateur practice" as applied to the operation of an amateur station in all respects not covered by the Part 97 rules? | 
 | A. | The FCC
 | B. | The Control Operator
 | C. | The IEEE
 | D. | The ITU
Commission's Rules
Group G1B

## Slide 32
G1C01
G1C02
G1C03
G1C04
G1C05
G1C06
G1C07
G1C08
G1C09
G1C10
G1C11
Commission's Rules
Group G1C (11 Questions)
Transmitter power regulations; data emission standards
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 33
 | G1C01 ~ What is the maximum transmitting power an amateur station may use on 10.140 MHz? | 
 |  | 200 watts PEP output
 |  | 1000 watts PEP output
 |  | 1500 watts PEP output
 |  | 2000 watts PEP output
 | FCC | 97.313(c)(1)
 | G1C01 ~ What is the maximum transmitting power an amateur station may use on 10.140 MHz? | 
 |  | 1000 watts PEP output
 |  | 1500 watts PEP output
 |  | 2000 watts PEP output
 | G1C01 ~ What is the maximum transmitting power an amateur station may use on 10.140 MHz? | 
 | A. | 200 watts PEP output
 | B. | 1000 watts PEP output
 | C. | 1500 watts PEP output
 | D. | 2000 watts PEP output
Commission's Rules
Group G1C

## Slide 34
 | G1C02 ~ What is the maximum transmitting power an amateur station may use on the 12-meter band? | 
 |  | 50 watts PEP output
 |  | 200 watts PEP output
 |  | 1500 watts PEP output
 |  | An effective radiated power equivalent to 100 watts from a half-wave dipole
 | FCC | 97.313(a),(b)
 | G1C02 ~ What is the maximum transmitting power an amateur station may use on the 12-meter band? | 
 |  | 50 watts PEP output
 |  | 200 watts PEP output
 |  | An effective radiated power equivalent to 100 watts from a half-wave dipole
 | G1C02 ~ What is the maximum transmitting power an amateur station may use on the 12-meter band? | 
 | A. | 50 watts PEP output
 | B. | 200 watts PEP output
 | C. | 1500 watts PEP output
 | D. | An effective radiated power equivalent to 100 watts from a half-wave dipole
Commission's Rules
Group G1C

## Slide 35
 | G1C03 ~ What is the maximum bandwidth permitted by FCC rules for Amateur Radio stations transmitting on USB frequencies in the 60-meter band? | 
 |  | 2.8 kHz
 |  | 5.6 kHz
 |  | 1.8 kHz
 |  | 3 kHz
 | FCC | 97.303(h)(1)
 | G1C03 ~ What is the maximum bandwidth permitted by FCC rules for Amateur Radio stations transmitting on USB frequencies in the 60-meter band? | 
 |  | 5.6 kHz
 |  | 1.8 kHz
 |  | 3 kHz
 | G1C03 ~ What is the maximum bandwidth permitted by FCC rules for Amateur Radio stations transmitting on USB frequencies in the 60-meter band? | 
 | A. | 2.8 kHz
 | B. | 5.6 kHz
 | C. | 1.8 kHz
 | D. | 3 kHz
Commission's Rules
Group G1C

## Slide 36
 | G1C04 ~ Which of the following limitations apply to transmitter power on every amateur band? | 
 |  | Only the minimum power necessary to carry out the desired communications should be used
 |  | Power must be limited to 200 watts when transmitting between 14.100 MHz and 14.150 MHz
 |  | Power should be limited as necessary to avoid interference to another radio service on the frequency
 |  | Effective radiated power cannot exceed 1500 watts
 | FCC | 97.313(a)
 | G1C04 ~ Which of the following limitations apply to transmitter power on every amateur band? | 
 |  | Power must be limited to 200 watts when transmitting between 14.100 MHz and 14.150 MHz
 |  | Power should be limited as necessary to avoid interference to another radio service on the frequency
 |  | Effective radiated power cannot exceed 1500 watts
 | G1C04 ~ Which of the following limitations apply to transmitter power on every amateur band? | 
 | A. | Only the minimum power necessary to carry out the desired communications should be used
 | B. | Power must be limited to 200 watts when transmitting between 14.100 MHz and 14.150 MHz
 | C. | Power should be limited as necessary to avoid interference to another radio service on the frequency
 | D. | Effective radiated power cannot exceed 1500 watts
Commission's Rules
Group G1C

## Slide 37
 | G1C05 ~ Which of the following is a limitation on transmitter power on the 28 MHz band for a General Class control operator? | 
 |  | 100 watts PEP output
 |  | 1000 watts PEP output
 |  | 1500 watts PEP output
 |  | 2000 watts PEP output
 | FCC | 97.313(c)(2)
 | G1C05 ~ Which of the following is a limitation on transmitter power on the 28 MHz band for a General Class control operator? | 
 |  | 100 watts PEP output
 |  | 1000 watts PEP output
 |  | 2000 watts PEP output
 | G1C05 ~ Which of the following is a limitation on transmitter power on the 28 MHz band for a General Class control operator? | 
 | A. | 100 watts PEP output
 | B. | 1000 watts PEP output
 | C. | 1500 watts PEP output
 | D. | 2000 watts PEP output
Commission's Rules
Group G1C

## Slide 38
 | G1C06 ~ Which of the following is a limitation on transmitter power on the 1.8 MHz band? | 
 |  | 200 watts PEP output
 |  | 1000 watts PEP output
 |  | 1200 watts PEP output
 |  | 1500 watts PEP output
 | FCC | 97.313
 | G1C06 ~ Which of the following is a limitation on transmitter power on the 1.8 MHz band? | 
 |  | 200 watts PEP output
 |  | 1000 watts PEP output
 |  | 1200 watts PEP output
 | G1C06 ~ Which of the following is a limitation on transmitter power on the 1.8 MHz band? | 
 | A. | 200 watts PEP output
 | B. | 1000 watts PEP output
 | C. | 1200 watts PEP output
 | D. | 1500 watts PEP output
Commission's Rules
Group G1C

## Slide 39
 | G1C07 ~ What is the maximum symbol rate permitted for RTTY or data emission transmission on the 20-meter band? | 
 |  | 56 kilobaud
 |  | 19.6 kilobaud
 |  | 1200 baud
 |  | 300 baud
 | FCC | 97.305(c), 97.307(f)(3)
 | G1C07 ~ What is the maximum symbol rate permitted for RTTY or data emission transmission on the 20-meter band? | 
 |  | 56 kilobaud
 |  | 19.6 kilobaud
 |  | 1200 baud
 | G1C07 ~ What is the maximum symbol rate permitted for RTTY or data emission transmission on the 20-meter band? | 
 | A. | 56 kilobaud
 | B. | 19.6 kilobaud
 | C. | 1200 baud
 | D. | 300 baud
Commission's Rules
Group G1C

## Slide 40
 | G1C08 ~ What is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz? | 
 |  | 56 kilobaud
 |  | 19.6 kilobaud
 |  | 1200 baud
 |  | 300 baud
 | FCC | 97.307(f)(3)
 | G1C08 ~ What is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz? | 
 |  | 56 kilobaud
 |  | 19.6 kilobaud
 |  | 1200 baud
 | G1C08 ~ What is the maximum symbol rate permitted for RTTY or data emission transmitted at frequencies below 28 MHz? | 
 | A. | 56 kilobaud
 | B. | 19.6 kilobaud
 | C. | 1200 baud
 | D. | 300 baud
Commission's Rules
Group G1C

## Slide 41
 | G1C09 ~ What is the maximum symbol rate permitted for RTTY or data emission transmitted on the 1.25-meter and 70-centimeter bands? | 
 |  | 56 kilobaud
 |  | 19.6 kilobaud
 |  | 1200 baud
 |  | 300 baud
 | FCC | 97.305(c) and 97.307(f)(5)
 | G1C09 ~ What is the maximum symbol rate permitted for RTTY or data emission transmitted on the 1.25-meter and 70-centimeter bands? | 
 |  | 19.6 kilobaud
 |  | 1200 baud
 |  | 300 baud
 | G1C09 ~ What is the maximum symbol rate permitted for RTTY or data emission transmitted on the 1.25-meter and 70-centimeter bands? | 
 | A. | 56 kilobaud
 | B. | 19.6 kilobaud
 | C. | 1200 baud
 | D. | 300 baud
Commission's Rules
Group G1C

## Slide 42
 | G1C10 ~ What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10-meter band? | 
 |  | 56 kilobaud
 |  | 19.6 kilobaud
 |  | 1200 baud
 |  | 300 baud
 | FCC | 97.305(c) and 97.307(f)(4)
 | G1C10 ~ What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10-meter band? | 
 |  | 56 kilobaud
 |  | 19.6 kilobaud
 |  | 300 baud
 | G1C10 ~ What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 10-meter band? | 
 | A. | 56 kilobaud
 | B. | 19.6 kilobaud
 | C. | 1200 baud
 | D. | 300 baud
Commission's Rules
Group G1C

## Slide 43
 | G1C11 ~ What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 2-meter band? | 
 |  | 56 kilobaud
 |  | 19.6 kilobaud
 |  | 1200 baud
 |  | 300 baud
 | FCC | 97.305(c) and 97.307(f)(5)
 | G1C11 ~ What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 2-meter band? | 
 |  | 56 kilobaud
 |  | 1200 baud
 |  | 300 baud
 | G1C11 ~ What is the maximum symbol rate permitted for RTTY or data emission transmissions on the 2-meter band? | 
 | A. | 56 kilobaud
 | B. | 19.6 kilobaud
 | C. | 1200 baud
 | D. | 300 baud
Commission's Rules
Group G1C

## Slide 44
G1D01
G1D02
G1D03
G1D04
G1D05
G1D06
G1D07
G1D08
G1D09
G1D10
G1D11
Commission's Rules
Group G1D (11 Questions)
Volunteer Examiners and Volunteer Examiner Coordinators; temporary identification
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 45
 | G1D01 ~ Who may receive credit for the elements represented by an expired amateur radio license? | 
 |  | Any person who can demonstrate that they once held an FCC issued General, Advanced, or Amateur Extra class license that was not revoked by the FCC
 |  | Anyone who held an FCC issued amateur radio license that has been expired for not less than 5 years and not more than 15 years
 |  | Any person who previously held an amateur license issued by another country, but only if that country has a current reciprocal licensing agreement with the FCC
 |  | Only persons who once held an FCC issued Novice, Technician, or Technician Plus license
 | FCC | 97.501, 97.505(a)
 | G1D01 ~ Who may receive credit for the elements represented by an expired amateur radio license? | 
 |  | Anyone who held an FCC issued amateur radio license that has been expired for not less than 5 years and not more than 15 years
 |  | Any person who previously held an amateur license issued by another country, but only if that country has a current reciprocal licensing agreement with the FCC
 |  | Only persons who once held an FCC issued Novice, Technician, or Technician Plus license
 | G1D01 ~ Who may receive credit for the elements represented by an expired amateur radio license? | 
 | A. | Any person who can demonstrate that they once held an FCC issued General, Advanced, or Amateur Extra class license that was not revoked by the FCC
 | B. | Anyone who held an FCC issued amateur radio license that has been expired for not less than 5 years and not more than 15 years
 | C. | Any person who previously held an amateur license issued by another country, but only if that country has a current reciprocal licensing agreement with the FCC
 | D. | Only persons who once held an FCC issued Novice, Technician, or Technician Plus license
Commission's Rules
Group G1D

## Slide 46
 | G1D02 ~ What license examinations may you administer when you are an accredited VE holding a General Class operator license? | 
 |  | General and Technician
 |  | General only
 |  | Technician only
 |  | Extra, General and Technician
 | FCC | 97.509(b)(3)(i)
 | G1D02 ~ What license examinations may you administer when you are an accredited VE holding a General Class operator license? | 
 |  | General and Technician
 |  | General only
 |  | Extra, General and Technician
 | G1D02 ~ What license examinations may you administer when you are an accredited VE holding a General Class operator license? | 
 | A. | General and Technician
 | B. | General only
 | C. | Technician only
 | D. | Extra, General and Technician
Commission's Rules
Group G1D

## Slide 47
 | G1D03 ~ On which of the following band segments may you operate if you are a Technician Class operator and have a CSCE for General Class privileges? | 
 |  | Only the Technician band segments until your upgrade is posted in the FCC database
 |  | Only on the Technician band segments until your license arrives in the mail
 |  | On any General or Technician Class band segment
 |  | On any General or Technician Class band segment except 30-meters and 60-meters
 | FCC | 97.9(b)
 | G1D03 ~ On which of the following band segments may you operate if you are a Technician Class operator and have a CSCE for General Class privileges? | 
 |  | Only the Technician band segments until your upgrade is posted in the FCC database
 |  | Only on the Technician band segments until your license arrives in the mail
 |  | On any General or Technician Class band segment except 30-meters and 60-meters
 | G1D03 ~ On which of the following band segments may you operate if you are a Technician Class operator and have a CSCE for General Class privileges? | 
 | A. | Only the Technician band segments until your upgrade is posted in the FCC database
 | B. | Only on the Technician band segments until your license arrives in the mail
 | C. | On any General or Technician Class band segment
 | D. | On any General or Technician Class band segment except 30-meters and 60-meters
Commission's Rules
Group G1D

## Slide 48
 | G1D04 ~ Which of the following is a requirement for administering a Technician Class license examination? | 
 |  | At least three General Class or higher VEs must observe the examination
 |  | At least two General Class or higher VEs must be present
 |  | At least two General Class or higher VEs must be present, but only one need be Extra Class
 |  | At least three VEs of Technician Class or higher must observe the examination
 | FCC | 97.509(3)(i)(c)
 | G1D04 ~ Which of the following is a requirement for administering a Technician Class license examination? | 
 |  | At least two General Class or higher VEs must be present
 |  | At least two General Class or higher VEs must be present, but only one need be Extra Class
 |  | At least three VEs of Technician Class or higher must observe the examination
 | G1D04 ~ Which of the following is a requirement for administering a Technician Class license examination? | 
 | A. | At least three General Class or higher VEs must observe the examination
 | B. | At least two General Class or higher VEs must be present
 | C. | At least two General Class or higher VEs must be present, but only one need be Extra Class
 | D. | At least three VEs of Technician Class or higher must observe the examination
Commission's Rules
Group G1D

## Slide 49
 | G1D05 ~ Which of the following must a person have before they can be an administering VE for a Technician Class license examination? | 
 |  | Notification to the FCC that you want to give an examination
 |  | Receipt of a CSCE for General Class
 |  | Possession of a properly obtained telegraphy license
 |  | An FCC General Class or higher license and VEC accreditation
 | FCC | 97.509(b)(3)(i)
 | G1D05 ~ Which of the following must a person have before they can be an administering VE for a Technician Class license examination? | 
 |  | Notification to the FCC that you want to give an examination
 |  | Receipt of a CSCE for General Class
 |  | Possession of a properly obtained telegraphy license
 | G1D05 ~ Which of the following must a person have before they can be an administering VE for a Technician Class license examination? | 
 | A. | Notification to the FCC that you want to give an examination
 | B. | Receipt of a CSCE for General Class
 | C. | Possession of a properly obtained telegraphy license
 | D. | An FCC General Class or higher license and VEC accreditation
Commission's Rules
Group G1D

## Slide 50
 | G1D06 ~ When must you add the special identifier "AG" after your call sign if you are a Technician Class licensee and have a CSCE for General Class operator privileges, but the FCC has not yet posted your upgrade on its website ? | 
 |  | Whenever you operate using General Class frequency privileges
 |  | Whenever you operate on any amateur frequency
 |  | Whenever you operate using Technician frequency privileges
 |  | A special identifier is not required as long as your General Class license application has been filed with the FCC
 | FCC | 97.119(f)(2)
 | G1D06 ~ When must you add the special identifier "AG" after your call sign if you are a Technician Class licensee and have a CSCE for General Class operator privileges, but the FCC has not yet posted your upgrade on its website ? | 
 |  | Whenever you operate on any amateur frequency
 |  | Whenever you operate using Technician frequency privileges
 |  | A special identifier is not required as long as your General Class license application has been filed with the FCC
 | G1D06 ~ When must you add the special identifier "AG" after your call sign if you are a Technician Class licensee and have a CSCE for General Class operator privileges, but the FCC has not yet posted your upgrade on its website ? | 
 | A. | Whenever you operate using General Class frequency privileges
 | B. | Whenever you operate on any amateur frequency
 | C. | Whenever you operate using Technician frequency privileges
 | D. | A special identifier is not required as long as your General Class license application has been filed with the FCC
Commission's Rules
Group G1D

## Slide 51
 | G1D07 ~ Volunteer Examiners are accredited by what organization? | 
 |  | The Federal Communications Commission
 |  | The Universal Licensing System
 |  | A Volunteer Examiner Coordinator
 |  | The Wireless Telecommunications Bureau
 | FCC | 97.509(b)(1)
 | G1D07 ~ Volunteer Examiners are accredited by what organization? | 
 |  | The Federal Communications Commission
 |  | The Universal Licensing System
 |  | The Wireless Telecommunications Bureau
 | G1D07 ~ Volunteer Examiners are accredited by what organization? | 
 | A. | The Federal Communications Commission
 | B. | The Universal Licensing System
 | C. | A Volunteer Examiner Coordinator
 | D. | The Wireless Telecommunications Bureau
Commission's Rules
Group G1D

## Slide 52
 | G1D08 ~ Which of the following criteria must be met for a non-U.S. citizen to be an accredited Volunteer Examiner? | 
 |  | The person must be a resident of the U.S. for a minimum of 5 years
 |  | The person must hold an FCC granted Amateur Radio license of General Class or above
 |  | The person's home citizenship must be in ITU region 2
 |  | None of these choices is correct; a non-U.S. citizen cannot be a Volunteer Examiner
 | FCC | 97.509(b)(3)
 | G1D08 ~ Which of the following criteria must be met for a non-U.S. citizen to be an accredited Volunteer Examiner? | 
 |  | The person must be a resident of the U.S. for a minimum of 5 years
 |  | The person's home citizenship must be in ITU region 2
 |  | None of these choices is correct; a non-U.S. citizen cannot be a Volunteer Examiner
 | G1D08 ~ Which of the following criteria must be met for a non-U.S. citizen to be an accredited Volunteer Examiner? | 
 | A. | The person must be a resident of the U.S. for a minimum of 5 years
 | B. | The person must hold an FCC granted Amateur Radio license of General Class or above
 | C. | The person's home citizenship must be in ITU region 2
 | D. | None of these choices is correct; a non-U.S. citizen cannot be a Volunteer Examiner
Commission's Rules
Group G1D

## Slide 53
 | G1D09 ~ How long is a Certificate of Successful Completion of Examination (CSCE) valid for exam element credit? | 
 |  | 30 days
 |  | 180 days
 |  | 365 days
 |  | For as long as your current license is valid
 | FCC | 97.9(b)
 | G1D09 ~ How long is a Certificate of Successful Completion of Examination (CSCE) valid for exam element credit? | 
 |  | 30 days
 |  | 180 days
 |  | For as long as your current license is valid
 | G1D09 ~ How long is a Certificate of Successful Completion of Examination (CSCE) valid for exam element credit? | 
 | A. | 30 days
 | B. | 180 days
 | C. | 365 days
 | D. | For as long as your current license is valid
Commission's Rules
Group G1D

## Slide 54
 | G1D10 ~ What is the minimum age that one must be to qualify as an accredited Volunteer Examiner? | 
 |  | 12 years
 |  | 18 years
 |  | 21 years
 |  | There is no age limit
 | FCC | 97.509(b)(2)
 | G1D10 ~ What is the minimum age that one must be to qualify as an accredited Volunteer Examiner? | 
 |  | 12 years
 |  | 21 years
 |  | There is no age limit
 | G1D10 ~ What is the minimum age that one must be to qualify as an accredited Volunteer Examiner? | 
 | A. | 12 years
 | B. | 18 years
 | C. | 21 years
 | D. | There is no age limit
Commission's Rules
Group G1D

## Slide 55
 | G1D11 ~ If a person has an expired FCC issued amateur radio license of General Class or higher, what is required before they can receive a new license? | 
 |  | They must have a letter from the FCC showing they once held an amateur or commercial license
 |  | There are no requirements other than being able to show a copy of the expired license
 |  | The applicant must be able to produce a copy of a page from a call book published in the USA showing his or her name and address
 |  | The applicant must pass the current element 2 exam
 | G1D11 ~ If a person has an expired FCC issued amateur radio license of General Class or higher, what is required before they can receive a new license? | 
 |  | They must have a letter from the FCC showing they once held an amateur or commercial license
 |  | There are no requirements other than being able to show a copy of the expired license
 |  | The applicant must be able to produce a copy of a page from a call book published in the USA showing his or her name and address
 | G1D11 ~ If a person has an expired FCC issued amateur radio license of General Class or higher, what is required before they can receive a new license? | 
 | A. | They must have a letter from the FCC showing they once held an amateur or commercial license
 | B. | There are no requirements other than being able to show a copy of the expired license
 | C. | The applicant must be able to produce a copy of a page from a call book published in the USA showing his or her name and address
 | D. | The applicant must pass the current element 2 exam
Commission's Rules
Group G1D

## Slide 56
G1E01
G1E02
G1E03
G1E04
G1E05
G1E06
G1E07
G1E08
G1E09
G1E11
G1E12
G1E13
Commission's Rules
Group G1E (12 Questions)
Control categories; repeater regulations; harmful interference; third party rules; ITU regions; automatically controlled digital station
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 57
 | G1E01 ~ Which of the following would disqualify a third party from participating in stating a message over an amateur station? | 
 |  | The third party's amateur license has been revoked and not reinstated
 |  | The third party is not a U.S. citizen
 |  | The third party is a licensed amateur
 |  | The third party is speaking in a language other than English
 | FCC | 97.115(b)(2)
 | G1E01 ~ Which of the following would disqualify a third party from participating in stating a message over an amateur station? | 
 |  | The third party is not a U.S. citizen
 |  | The third party is a licensed amateur
 |  | The third party is speaking in a language other than English
 | G1E01 ~ Which of the following would disqualify a third party from participating in stating a message over an amateur station? | 
 | A. | The third party's amateur license has been revoked and not reinstated
 | B. | The third party is not a U.S. citizen
 | C. | The third party is a licensed amateur
 | D. | The third party is speaking in a language other than English
Commission's Rules
Group G1E

## Slide 58
 | G1E02 ~ When may a 10-meter repeater retransmit the 2-meter signal from a station having a Technician Class control operator? | 
 |  | Under no circumstances
 |  | Only if the station on 10-meters is operating under a Special Temporary Authorization allowing such retransmission
 |  | Only during an FCC declared general state of communications emergency
 |  | Only if the 10-meter repeater control operator holds at least a General Class license
 | FCC | 97.205(b)
 | G1E02 ~ When may a 10-meter repeater retransmit the 2-meter signal from a station having a Technician Class control operator? | 
 |  | Under no circumstances
 |  | Only if the station on 10-meters is operating under a Special Temporary Authorization allowing such retransmission
 |  | Only during an FCC declared general state of communications emergency
 | G1E02 ~ When may a 10-meter repeater retransmit the 2-meter signal from a station having a Technician Class control operator? | 
 | A. | Under no circumstances
 | B. | Only if the station on 10-meters is operating under a Special Temporary Authorization allowing such retransmission
 | C. | Only during an FCC declared general state of communications emergency
 | D. | Only if the 10-meter repeater control operator holds at least a General Class license
Commission's Rules
Group G1E

## Slide 59
 | G1E03 ~ What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments? | 
 |  | The station initiating the contact must be under local or remote control
 |  | The interrogating transmission must be made by another automatically controlled station
 |  | No third party traffic maybe be transmitted
 |  | The control operator of the interrogating station must hold an Extra
 | FCC | 97.221
 | G1E03 ~ What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments? | 
 |  | The interrogating transmission must be made by another automatically controlled station
 |  | No third party traffic maybe be transmitted
 |  | The control operator of the interrogating station must hold an Extra
 | G1E03 ~ What is required to conduct communications with a digital station operating under automatic control outside the automatic control band segments? | 
 | A. | The station initiating the contact must be under local or remote control
 | B. | The interrogating transmission must be made by another automatically controlled station
 | C. | No third party traffic maybe be transmitted
 | D. | The control operator of the interrogating station must hold an Extra
Commission's Rules
Group G1E

## Slide 60
 | G1E04 ~ Which of the following conditions require a licensed Amateur Radio operator to take specific steps to avoid harmful interference to other users or facilities? | 
 |  | When operating within one mile of an FCC Monitoring Station
 |  | When using a band where the Amateur Service is secondary
 |  | When a station is transmitting spread spectrum emissions
 |  | All of these choices are correct
 | FCC | 97.13(b), 97.303, 97.311(b)
 | G1E04 ~ Which of the following conditions require a licensed Amateur Radio operator to take specific steps to avoid harmful interference to other users or facilities? | 
 |  | When operating within one mile of an FCC Monitoring Station
 |  | When using a band where the Amateur Service is secondary
 |  | When a station is transmitting spread spectrum emissions
 | G1E04 ~ Which of the following conditions require a licensed Amateur Radio operator to take specific steps to avoid harmful interference to other users or facilities? | 
 | A. | When operating within one mile of an FCC Monitoring Station
 | B. | When using a band where the Amateur Service is secondary
 | C. | When a station is transmitting spread spectrum emissions
 | D. | All of these choices are correct
Commission's Rules
Group G1E

## Slide 61
 | G1E05 ~ What types of messages for a third party in another country may be transmitted by an amateur station? | 
 |  | Any message, as long as the amateur operator is not paid
 |  | Only messages for other licensed amateurs
 |  | Only messages relating to Amateur Radio or remarks of a personal character, or messages relating to emergencies or disaster relief
 |  | Any messages, as long as the text of the message is recorded in the station log
 | FCC | 97.115(a)(2),97.117
 | G1E05 ~ What types of messages for a third party in another country may be transmitted by an amateur station? | 
 |  | Any message, as long as the amateur operator is not paid
 |  | Only messages for other licensed amateurs
 |  | Any messages, as long as the text of the message is recorded in the station log
 | G1E05 ~ What types of messages for a third party in another country may be transmitted by an amateur station? | 
 | A. | Any message, as long as the amateur operator is not paid
 | B. | Only messages for other licensed amateurs
 | C. | Only messages relating to Amateur Radio or remarks of a personal character, or messages relating to emergencies or disaster relief
 | D. | Any messages, as long as the text of the message is recorded in the station log
Commission's Rules
Group G1E

## Slide 62
 | G1E06 ~ Which of the following applies in the event of interference between a coordinated repeater and an uncoordinated repeater? | 
 |  | The licensee of the uncoordinated repeater has primary responsibility to resolve the interference
 |  | The licensee of the coordinated repeater has primary responsibility to resolve the interference
 |  | Both repeater licensees share equal responsibility to resolve the interference
 |  | The frequency coordinator bears primary responsibility to resolve the interference
 | FCC | 97.205(c)
 | G1E06 ~ Which of the following applies in the event of interference between a coordinated repeater and an uncoordinated repeater? | 
 |  | The licensee of the coordinated repeater has primary responsibility to resolve the interference
 |  | Both repeater licensees share equal responsibility to resolve the interference
 |  | The frequency coordinator bears primary responsibility to resolve the interference
 | G1E06 ~ Which of the following applies in the event of interference between a coordinated repeater and an uncoordinated repeater? | 
 | A. | The licensee of the uncoordinated repeater has primary responsibility to resolve the interference
 | B. | The licensee of the coordinated repeater has primary responsibility to resolve the interference
 | C. | Both repeater licensees share equal responsibility to resolve the interference
 | D. | The frequency coordinator bears primary responsibility to resolve the interference
Commission's Rules
Group G1E

## Slide 63
 | G1E07 ~ With which foreign countries is third party traffic prohibited, except for messages directly involving emergencies or disaster relief communications? | 
 |  | Countries in ITU Region 2
 |  | Countries in ITU Region 1
 |  | Every foreign country, unless there is a third party agreement in effect with that country
 |  | Any country which is not a member of the International Amateur Radio Union (IARU)
 | FCC | 97.115(a)(2)
 | G1E07 ~ With which foreign countries is third party traffic prohibited, except for messages directly involving emergencies or disaster relief communications? | 
 |  | Countries in ITU Region 2
 |  | Countries in ITU Region 1
 |  | Any country which is not a member of the International Amateur Radio Union (IARU)
 | G1E07 ~ With which foreign countries is third party traffic prohibited, except for messages directly involving emergencies or disaster relief communications? | 
 | A. | Countries in ITU Region 2
 | B. | Countries in ITU Region 1
 | C. | Every foreign country, unless there is a third party agreement in effect with that country
 | D. | Any country which is not a member of the International Amateur Radio Union (IARU)
Commission's Rules
Group G1E

## Slide 64
 | G1E08 ~ Which of the following is a requirement for a non-licensed person to communicate with a foreign Amateur Radio station from a station with an FCC-granted license at which an FCC licensed control operator is present? | 
 |  | Information must be exchanged in English
 |  | The foreign amateur station must be in a country with which the United States has a third party agreement
 |  | The control operator must have at least a General Class license
 |  | All of these choices are correct
 | FCC | 97.115(a)(b)
 | G1E08 ~ Which of the following is a requirement for a non-licensed person to communicate with a foreign Amateur Radio station from a station with an FCC-granted license at which an FCC licensed control operator is present? | 
 |  | Information must be exchanged in English
 |  | The control operator must have at least a General Class license
 |  | All of these choices are correct
 | G1E08 ~ Which of the following is a requirement for a non-licensed person to communicate with a foreign Amateur Radio station from a station with an FCC-granted license at which an FCC licensed control operator is present? | 
 | A. | Information must be exchanged in English
 | B. | The foreign amateur station must be in a country with which the United States has a third party agreement
 | C. | The control operator must have at least a General Class license
 | D. | All of these choices are correct
Commission's Rules
Group G1E

## Slide 65
 | G1E09 ~ What language must be used when identifying your station if you are using a language other than English in making a contact using phone emission? | 
 |  | The language being used for the contact
 |  | Any language recognized by the United Nations
 |  | English only
 |  | English, Spanish, French, or German
 | FCC | 97.119(b)(2)
 | G1E09 ~ What language must be used when identifying your station if you are using a language other than English in making a contact using phone emission? | 
 |  | The language being used for the contact
 |  | Any language recognized by the United Nations
 |  | English, Spanish, French, or German
 | G1E09 ~ What language must be used when identifying your station if you are using a language other than English in making a contact using phone emission? | 
 | A. | The language being used for the contact
 | B. | Any language recognized by the United Nations
 | C. | English only
 | D. | English, Spanish, French, or German
Commission's Rules
Group G1E

## Slide 66
 | G1E11 ~ Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet? | 
 |  | Locally controlled station
 |  | Robotically controlled station
 |  | Automatically controlled digital station
 |  | Fail-safe digital station
 | FCC | 97.221
 | G1E11 ~ Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet? | 
 |  | Locally controlled station
 |  | Robotically controlled station
 |  | Fail-safe digital station
 | G1E11 ~ Which of the following is the FCC term for an unattended digital station that transfers messages to and from the Internet? | 
 | A. | Locally controlled station
 | B. | Robotically controlled station
 | C. | Automatically controlled digital station
 | D. | Fail-safe digital station
Commission's Rules
Group G1E

## Slide 67
 | G1E12 ~ Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication? | 
 |  | Under no circumstances
 |  | When messages are encrypted
 |  | When messages are not encrypted
 |  | When under automatic control
 | FCC | 97.115
 | G1E12 ~ Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication? | 
 |  | When messages are encrypted
 |  | When messages are not encrypted
 |  | When under automatic control
 | G1E12 ~ Under what circumstances are messages that are sent via digital modes exempt from Part 97 third party rules that apply to other modes of communication? | 
 | A. | Under no circumstances
 | B. | When messages are encrypted
 | C. | When messages are not encrypted
 | D. | When under automatic control
Commission's Rules
Group G1E

## Slide 68
 | G1E13 ~ On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations? | 
 |  | On any band segment where digital operation is permitted
 |  | Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
 |  | Only in the non-phone Extra Class segments of the bands
 |  | Anywhere in the 1.25-meter or shorter wavelength bands, and in specified segments of the 80-meter through 2-meter bands
 | FCC | 97.221, 97.305
 | G1E13 ~ On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations? | 
 |  | On any band segment where digital operation is permitted
 |  | Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
 |  | Only in the non-phone Extra Class segments of the bands
 | G1E13 ~ On what bands may automatically controlled stations transmitting RTTY or data emissions communicate with other automatically controlled digital stations? | 
 | A. | On any band segment where digital operation is permitted
 | B. | Anywhere in the non-phone segments of the 10-meter or shorter wavelength bands
 | C. | Only in the non-phone Extra Class segments of the bands
 | D. | Anywhere in the 1.25-meter or shorter wavelength bands, and in specified segments of the 80-meter through 2-meter bands
Commission's Rules
Group G1E

## Slide 69
Group |  | Questions
G2A | Phone operating procedures; USB/LSB conventions; procedural signals; breaking into a contact; VOX operation | 11
G2B | Operating courtesy; band plans; emergencies, including drills and emergency communications | 12
G2C | CW operating procedures and procedural signals; Q signals and common abbreviations: full break in | 11
G2D | Amateur Auxiliary; minimizing interference; HF operations | 11
G2E | Digital operating: procedures, procedural signals and common abbreviations | 14
5 | Total | 59
Subelement G2 Operating Procedures
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 70
G2A01
G2A02
G2A03
G2A04
G2A05
G2A06
G2A07
G2A08
G2A09
G2A10
G2A11
Operating Procedures
Group G2A (11 Questions)
Phone operating procedures; USB/LSB conventions; procedural signals; breaking into a contact; VOX operation
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 71
 | G2A01 ~ Which sideband is most commonly used for voice communications on frequencies of 14 MHz or higher? | 
 |  | Upper sideband
 |  | Lower sideband
 |  | Vestigial sideband
 |  | Double sideband
 | G2A01 ~ Which sideband is most commonly used for voice communications on frequencies of 14 MHz or higher? | 
 |  | Lower sideband
 |  | Vestigial sideband
 |  | Double sideband
 | G2A01 ~ Which sideband is most commonly used for voice communications on frequencies of 14 MHz or higher? | 
 | A. | Upper sideband
 | B. | Lower sideband
 | C. | Vestigial sideband
 | D. | Double sideband
Operating Procedures
Group G2A

## Slide 72
 | G2A02 ~ Which of the following modes is most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands? | 
 |  | Upper sideband
 |  | Lower sideband
 |  | Vestigial sideband
 |  | Double sideband
 | G2A02 ~ Which of the following modes is most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands? | 
 |  | Upper sideband
 |  | Vestigial sideband
 |  | Double sideband
 | G2A02 ~ Which of the following modes is most commonly used for voice communications on the 160-meter, 75-meter, and 40-meter bands? | 
 | A. | Upper sideband
 | B. | Lower sideband
 | C. | Vestigial sideband
 | D. | Double sideband
Operating Procedures
Group G2A

## Slide 73
 | G2A03 ~ Which of the following is most commonly used for SSB voice communications in the VHF and UHF bands? | 
 |  | Upper sideband
 |  | Lower sideband
 |  | Vestigial sideband
 |  | Double sideband
 | G2A03 ~ Which of the following is most commonly used for SSB voice communications in the VHF and UHF bands? | 
 |  | Lower sideband
 |  | Vestigial sideband
 |  | Double sideband
 | G2A03 ~ Which of the following is most commonly used for SSB voice communications in the VHF and UHF bands? | 
 | A. | Upper sideband
 | B. | Lower sideband
 | C. | Vestigial sideband
 | D. | Double sideband
Operating Procedures
Group G2A

## Slide 74
 | G2A04 ~ Which mode is most commonly used for voice communications on the 17-meter and 12-meter bands? | 
 |  | Upper sideband
 |  | Lower sideband
 |  | Vestigial sideband
 |  | Double sideband
 | G2A04 ~ Which mode is most commonly used for voice communications on the 17-meter and 12-meter bands? | 
 |  | Lower sideband
 |  | Vestigial sideband
 |  | Double sideband
 | G2A04 ~ Which mode is most commonly used for voice communications on the 17-meter and 12-meter bands? | 
 | A. | Upper sideband
 | B. | Lower sideband
 | C. | Vestigial sideband
 | D. | Double sideband
Operating Procedures
Group G2A

## Slide 75
 | G2A05 ~ Which mode of voice communication is most commonly used on the HF amateur bands? | 
 |  | Frequency modulation
 |  | Double sideband
 |  | Single sideband
 |  | Phase modulation
 | G2A05 ~ Which mode of voice communication is most commonly used on the HF amateur bands? | 
 |  | Frequency modulation
 |  | Double sideband
 |  | Phase modulation
 | G2A05 ~ Which mode of voice communication is most commonly used on the HF amateur bands? | 
 | A. | Frequency modulation
 | B. | Double sideband
 | C. | Single sideband
 | D. | Phase modulation
Operating Procedures
Group G2A

## Slide 76
 | G2A06 ~ Which of the following is an advantage when using single sideband as compared to other analog voice modes on the HF amateur bands? | 
 |  | Very high fidelity voice modulation
 |  | Less bandwidth used and greater power efficiency
 |  | Ease of tuning on receive and immunity to impulse noise
 |  | Less subject to interference from atmospheric static crashes
 | G2A06 ~ Which of the following is an advantage when using single sideband as compared to other analog voice modes on the HF amateur bands? | 
 |  | Very high fidelity voice modulation
 |  | Ease of tuning on receive and immunity to impulse noise
 |  | Less subject to interference from atmospheric static crashes
 | G2A06 ~ Which of the following is an advantage when using single sideband as compared to other analog voice modes on the HF amateur bands? | 
 | A. | Very high fidelity voice modulation
 | B. | Less bandwidth used and greater power efficiency
 | C. | Ease of tuning on receive and immunity to impulse noise
 | D. | Less subject to interference from atmospheric static crashes
Operating Procedures
Group G2A

## Slide 77
 | G2A07 ~ Which of the following statements is true of the single sideband voice mode? | 
 |  | Only one sideband and the carrier are transmitted; the other sideband is suppressed
 |  | Only one sideband is transmitted; the other sideband and carrier are suppressed
 |  | SSB is the only voice mode that is authorized on the 20-meter, 15-meter, and 10-meter amateur bands
 |  | SSB is the only voice mode that is authorized on the 160-meter, 75-meter and 40-meter amateur bands
 | G2A07 ~ Which of the following statements is true of the single sideband voice mode? | 
 |  | Only one sideband and the carrier are transmitted; the other sideband is suppressed
 |  | SSB is the only voice mode that is authorized on the 20-meter, 15-meter, and 10-meter amateur bands
 |  | SSB is the only voice mode that is authorized on the 160-meter, 75-meter and 40-meter amateur bands
 | G2A07 ~ Which of the following statements is true of the single sideband voice mode? | 
 | A. | Only one sideband and the carrier are transmitted; the other sideband is suppressed
 | B. | Only one sideband is transmitted; the other sideband and carrier are suppressed
 | C. | SSB is the only voice mode that is authorized on the 20-meter, 15-meter, and 10-meter amateur bands
 | D. | SSB is the only voice mode that is authorized on the 160-meter, 75-meter and 40-meter amateur bands
Operating Procedures
Group G2A

## Slide 78
 | G2A08 ~ Which of the following is a recommended way to break into a contact when using phone? | 
 |  | Say "QRZ" several times followed by your call sign
 |  | Say your call sign during a break between transmissions by the other stations
 |  | Say "Break Break Break" and wait for a response
 |  | Say "CQ" followed by the call sign of either station
 | G2A08 ~ Which of the following is a recommended way to break into a contact when using phone? | 
 |  | Say "QRZ" several times followed by your call sign
 |  | Say "Break Break Break" and wait for a response
 |  | Say "CQ" followed by the call sign of either station
 | G2A08 ~ Which of the following is a recommended way to break into a contact when using phone? | 
 | A. | Say "QRZ" several times followed by your call sign
 | B. | Say your call sign during a break between transmissions by the other stations
 | C. | Say "Break Break Break" and wait for a response
 | D. | Say "CQ" followed by the call sign of either station
Operating Procedures
Group G2A

## Slide 79
 | G2A09 ~ Why do most amateur stations use lower sideband on the 160-meter, 75-meter and 40-meter bands? | 
 |  | Lower sideband is more efficient than upper sideband at these frequencies
 |  | Lower sideband is the only sideband legal on these frequency bands
 |  | Because it is fully compatible with an AM detector
 |  | Current amateur practice is to use lower sideband on these frequency bands
 | G2A09 ~ Why do most amateur stations use lower sideband on the 160-meter, 75-meter and 40-meter bands? | 
 |  | Lower sideband is more efficient than upper sideband at these frequencies
 |  | Lower sideband is the only sideband legal on these frequency bands
 |  | Because it is fully compatible with an AM detector
 | G2A09 ~ Why do most amateur stations use lower sideband on the 160-meter, 75-meter and 40-meter bands? | 
 | A. | Lower sideband is more efficient than upper sideband at these frequencies
 | B. | Lower sideband is the only sideband legal on these frequency bands
 | C. | Because it is fully compatible with an AM detector
 | D. | Current amateur practice is to use lower sideband on these frequency bands
Operating Procedures
Group G2A

## Slide 80
 | G2A10 ~ Which of the following statements is true of voice VOX operation versus PTT operation? | 
 |  | The received signal is more natural sounding
 |  | It allows "hands free" operation
 |  | It occupies less bandwidth
 |  | It provides more power output
 | G2A10 ~ Which of the following statements is true of voice VOX operation versus PTT operation? | 
 |  | The received signal is more natural sounding
 |  | It occupies less bandwidth
 |  | It provides more power output
 | G2A10 ~ Which of the following statements is true of voice VOX operation versus PTT operation? | 
 | A. | The received signal is more natural sounding
 | B. | It allows "hands free" operation
 | C. | It occupies less bandwidth
 | D. | It provides more power output
Operating Procedures
Group G2A

## Slide 81
 | G2A11 ~ What does the expression "CQ DX" usually indicate? | 
 |  | A general call for any station
 |  | The caller is listening for a station in Germany
 |  | The caller is looking for any station outside their own country
 |  | A distress call
 | G2A11 ~ What does the expression "CQ DX" usually indicate? | 
 |  | A general call for any station
 |  | The caller is listening for a station in Germany
 |  | A distress call
 | G2A11 ~ What does the expression "CQ DX" usually indicate? | 
 | A. | A general call for any station
 | B. | The caller is listening for a station in Germany
 | C. | The caller is looking for any station outside their own country
 | D. | A distress call
Operating Procedures
Group G2A

## Slide 82
G2B01
G2B02
G2B03
G2B04
G2B05
G2B06
G2B07
G2B08
G2B09
G2B10
G2B11
G2B12
Operating Procedures
Group G2B (12 Questions)
Operating courtesy; band plans; emergencies, including drills and emergency communications
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 83
 | G2B01 ~ Which of the following is true concerning access to frequencies in non-emergency situations? | 
 |  | Nets always have priority
 |  | QSOs in progress always have priority
 |  | Except during FCC declared emergencies, no one has priority access to frequencies
 |  | Contest operations must always yield to non-contest use of frequencies
 | G2B01 ~ Which of the following is true concerning access to frequencies in non-emergency situations? | 
 |  | Nets always have priority
 |  | QSOs in progress always have priority
 |  | Contest operations must always yield to non-contest use of frequencies
 | G2B01 ~ Which of the following is true concerning access to frequencies in non-emergency situations? | 
 | A. | Nets always have priority
 | B. | QSOs in progress always have priority
 | C. | Except during FCC declared emergencies, no one has priority access to frequencies
 | D. | Contest operations must always yield to non-contest use of frequencies
Operating Procedures
Group G2B

## Slide 84
 | G2B02 ~ What is the first thing you should do if you are communicating with another amateur station and hear a station in distress break in? | 
 |  | Continue your communication because you were on the frequency first
 |  | Acknowledge the station in distress and determine what assistance may be needed
 |  | Change to a different frequency
 |  | Immediately cease all transmissions
 | G2B02 ~ What is the first thing you should do if you are communicating with another amateur station and hear a station in distress break in? | 
 |  | Continue your communication because you were on the frequency first
 |  | Change to a different frequency
 |  | Immediately cease all transmissions
 | G2B02 ~ What is the first thing you should do if you are communicating with another amateur station and hear a station in distress break in? | 
 | A. | Continue your communication because you were on the frequency first
 | B. | Acknowledge the station in distress and determine what assistance may be needed
 | C. | Change to a different frequency
 | D. | Immediately cease all transmissions
Operating Procedures
Group G2B

## Slide 85
 | G2B03 ~ If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, what should you do? | 
 |  | Tell the interfering stations to change frequency
 |  | Report the interference to your local Amateur Auxiliary Coordinator
 |  | As a common courtesy, move your contact to another frequency
 |  | Increase power to overcome interference
 | G2B03 ~ If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, what should you do? | 
 |  | Tell the interfering stations to change frequency
 |  | Report the interference to your local Amateur Auxiliary Coordinator
 |  | Increase power to overcome interference
 | G2B03 ~ If propagation changes during your contact and you notice increasing interference from other activity on the same frequency, what should you do? | 
 | A. | Tell the interfering stations to change frequency
 | B. | Report the interference to your local Amateur Auxiliary Coordinator
 | C. | As a common courtesy, move your contact to another frequency
 | D. | Increase power to overcome interference
Operating Procedures
Group G2B

## Slide 86
 | G2B04 ~ When selecting a CW transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies? | 
 |  | 5 to 50 Hz
 |  | 150 to 500 Hz
 |  | 1 to 3 kHz
 |  | 3 to 6 kHz
 | G2B04 ~ When selecting a CW transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies? | 
 |  | 5 to 50 Hz
 |  | 1 to 3 kHz
 |  | 3 to 6 kHz
 | G2B04 ~ When selecting a CW transmitting frequency, what minimum separation should be used to minimize interference to stations on adjacent frequencies? | 
 | A. | 5 to 50 Hz
 | B. | 150 to 500 Hz
 | C. | 1 to 3 kHz
 | D. | 3 to 6 kHz
Operating Procedures
Group G2B

## Slide 87
 | G2B05 ~ What is the customary minimum frequency separation between SSB signals under normal conditions? | 
 |  | Between 150 and 500 Hz
 |  | Approximately 3 kHz
 |  | Approximately 6 kHz
 |  | Approximately 10 kHz
 | G2B05 ~ What is the customary minimum frequency separation between SSB signals under normal conditions? | 
 |  | Between 150 and 500 Hz
 |  | Approximately 6 kHz
 |  | Approximately 10 kHz
 | G2B05 ~ What is the customary minimum frequency separation between SSB signals under normal conditions? | 
 | A. | Between 150 and 500 Hz
 | B. | Approximately 3 kHz
 | C. | Approximately 6 kHz
 | D. | Approximately 10 kHz
Operating Procedures
Group G2B

## Slide 88
 | G2B06 ~ What is a practical way to avoid harmful interference on an apparently clear frequency before calling CQ on CW or phone? | 
 |  | Send "QRL?" on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign
 |  | Listen for 2 minutes before calling CQ
 |  | Send the letter "V" in Morse code several times and listen for a response or say "test" several times and listen for a response
 |  | Send "QSY" on CW or if using phone, announce "the frequency is in use", then give your call and listen for a response
 | G2B06 ~ What is a practical way to avoid harmful interference on an apparently clear frequency before calling CQ on CW or phone? | 
 |  | Listen for 2 minutes before calling CQ
 |  | Send the letter "V" in Morse code several times and listen for a response or say "test" several times and listen for a response
 |  | Send "QSY" on CW or if using phone, announce "the frequency is in use", then give your call and listen for a response
 | G2B06 ~ What is a practical way to avoid harmful interference on an apparently clear frequency before calling CQ on CW or phone? | 
 | A. | Send "QRL?" on CW, followed by your call sign; or, if using phone, ask if the frequency is in use, followed by your call sign
 | B. | Listen for 2 minutes before calling CQ
 | C. | Send the letter "V" in Morse code several times and listen for a response or say "test" several times and listen for a response
 | D. | Send "QSY" on CW or if using phone, announce "the frequency is in use", then give your call and listen for a response
Operating Procedures
Group G2B

## Slide 89
 | G2B07 ~ Which of the following complies with good amateur practice when choosing a frequency on which to initiate a call? | 
 |  | Check to see if the channel is assigned to another station
 |  | Identify your station by transmitting your call sign at least 3 times
 |  | Follow the voluntary band plan for the operating mode you intend to use
 |  | All of these choices are correct
 | G2B07 ~ Which of the following complies with good amateur practice when choosing a frequency on which to initiate a call? | 
 |  | Check to see if the channel is assigned to another station
 |  | Identify your station by transmitting your call sign at least 3 times
 |  | All of these choices are correct
 | G2B07 ~ Which of the following complies with good amateur practice when choosing a frequency on which to initiate a call? | 
 | A. | Check to see if the channel is assigned to another station
 | B. | Identify your station by transmitting your call sign at least 3 times
 | C. | Follow the voluntary band plan for the operating mode you intend to use
 | D. | All of these choices are correct
Operating Procedures
Group G2B

## Slide 90
 | G2B08 ~ What is the "DX window" in a voluntary band plan? | 
 |  | A portion of the band that should not be used for contacts between stations within the 48 contiguous United States
 |  | An FCC rule that prohibits contacts between stations within the United States and possessions in that portion of the band
 |  | An FCC rule that allows only digital contacts in that portion of the band
 |  | A portion of the band that has been voluntarily set aside for digital contacts only
 | G2B08 ~ What is the "DX window" in a voluntary band plan? | 
 |  | An FCC rule that prohibits contacts between stations within the United States and possessions in that portion of the band
 |  | An FCC rule that allows only digital contacts in that portion of the band
 |  | A portion of the band that has been voluntarily set aside for digital contacts only
 | G2B08 ~ What is the "DX window" in a voluntary band plan? | 
 | A. | A portion of the band that should not be used for contacts between stations within the 48 contiguous United States
 | B. | An FCC rule that prohibits contacts between stations within the United States and possessions in that portion of the band
 | C. | An FCC rule that allows only digital contacts in that portion of the band
 | D. | A portion of the band that has been voluntarily set aside for digital contacts only
Operating Procedures
Group G2B

## Slide 91
 | G2B09 ~ Who may be the control operator of an amateur station transmitting in RACES to assist relief operations during a disaster? | 
 |  | Only a person holding an FCC issued amateur operator license
 |  | Only a RACES net control operator
 |  | A person holding an FCC issued amateur operator license or an appropriate government official
 |  | Any control operator when normal communication systems are operational
 | FCC | 97.407(a)
 | G2B09 ~ Who may be the control operator of an amateur station transmitting in RACES to assist relief operations during a disaster? | 
 |  | Only a RACES net control operator
 |  | A person holding an FCC issued amateur operator license or an appropriate government official
 |  | Any control operator when normal communication systems are operational
 | G2B09 ~ Who may be the control operator of an amateur station transmitting in RACES to assist relief operations during a disaster? | 
 | A. | Only a person holding an FCC issued amateur operator license
 | B. | Only a RACES net control operator
 | C. | A person holding an FCC issued amateur operator license or an appropriate government official
 | D. | Any control operator when normal communication systems are operational
Operating Procedures
Group G2B

## Slide 92
 | G2B10 ~ When may the FCC restrict normal frequency operations of amateur stations participating in RACES? | 
 |  | When they declare a temporary state of communication emergency
 |  | When they seize your equipment for use in disaster communications
 |  | Only when all amateur stations are instructed to stop transmitting
 |  | When the President's War Emergency Powers have been invoked
 | FCC | 97.407(b)
 | G2B10 ~ When may the FCC restrict normal frequency operations of amateur stations participating in RACES? | 
 |  | When they declare a temporary state of communication emergency
 |  | When they seize your equipment for use in disaster communications
 |  | Only when all amateur stations are instructed to stop transmitting
 | G2B10 ~ When may the FCC restrict normal frequency operations of amateur stations participating in RACES? | 
 | A. | When they declare a temporary state of communication emergency
 | B. | When they seize your equipment for use in disaster communications
 | C. | Only when all amateur stations are instructed to stop transmitting
 | D. | When the President's War Emergency Powers have been invoked
Operating Procedures
Group G2B

## Slide 93
 | G2B11 ~ What frequency should be used to send a distress call? | 
 |  | Whichever frequency has the best chance of communicating the distress message
 |  | Only frequencies authorized for RACES or ARES stations
 |  | Only frequencies that are within your operating privileges
 |  | Only frequencies used by police, fire or emergency medical services
 | FCC | 97.405
 | G2B11 ~ What frequency should be used to send a distress call? | 
 |  | Only frequencies authorized for RACES or ARES stations
 |  | Only frequencies that are within your operating privileges
 |  | Only frequencies used by police, fire or emergency medical services
 | G2B11 ~ What frequency should be used to send a distress call? | 
 | A. | Whichever frequency has the best chance of communicating the distress message
 | B. | Only frequencies authorized for RACES or ARES stations
 | C. | Only frequencies that are within your operating privileges
 | D. | Only frequencies used by police, fire or emergency medical services
Operating Procedures
Group G2B

## Slide 94
 | G2B12 ~ When is an amateur station allowed to use any means at its disposal to assist another station in distress? | 
 |  | Only when transmitting in RACES
 |  | At any time when transmitting in an organized net
 |  | At any time during an actual emergency
 |  | Only on authorized HF frequencies
 | FCC | 97.405(b)
 | G2B12 ~ When is an amateur station allowed to use any means at its disposal to assist another station in distress? | 
 |  | Only when transmitting in RACES
 |  | At any time when transmitting in an organized net
 |  | Only on authorized HF frequencies
 | G2B12 ~ When is an amateur station allowed to use any means at its disposal to assist another station in distress? | 
 | A. | Only when transmitting in RACES
 | B. | At any time when transmitting in an organized net
 | C. | At any time during an actual emergency
 | D. | Only on authorized HF frequencies
Operating Procedures
Group G2B

## Slide 95
G2C01
G2C02
G2C03
G2C04
G2C05
G2C06
G2C07
G2C08
G2C09
G2C10
G2C11
Operating Procedures
Group G2C (11 Questions)
CW operating procedures and procedural signals; Q signals and common abbreviations: full break in
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 96
 | G2C01 ~ Which of the following describes full break-in telegraphy (QSK)? | 
 |  | Breaking stations send the Morse code prosign BK
 |  | Automatic keyers are used to send Morse code instead of hand keys
 |  | An operator must activate a manual send/receive switch before and after every transmission
 |  | Transmitting stations can receive between code characters and elements
 | G2C01 ~ Which of the following describes full break-in telegraphy (QSK)? | 
 |  | Breaking stations send the Morse code prosign BK
 |  | Automatic keyers are used to send Morse code instead of hand keys
 |  | An operator must activate a manual send/receive switch before and after every transmission
 | G2C01 ~ Which of the following describes full break-in telegraphy (QSK)? | 
 | A. | Breaking stations send the Morse code prosign BK
 | B. | Automatic keyers are used to send Morse code instead of hand keys
 | C. | An operator must activate a manual send/receive switch before and after every transmission
 | D. | Transmitting stations can receive between code characters and elements
Operating Procedures
Group G2C

## Slide 97
 | G2C02 ~ What should you do if a CW station sends "QRS"? | 
 |  | Send slower
 |  | Change frequency
 |  | Increase your power
 |  | Repeat everything twice
 | G2C02 ~ What should you do if a CW station sends "QRS"? | 
 |  | Change frequency
 |  | Increase your power
 |  | Repeat everything twice
 | G2C02 ~ What should you do if a CW station sends "QRS"? | 
 | A. | Send slower
 | B. | Change frequency
 | C. | Increase your power
 | D. | Repeat everything twice
Operating Procedures
Group G2C

## Slide 98
 | G2C03 ~ What does it mean when a CW operator sends "KN" at the end of a transmission? | 
 |  | Listening for novice stations
 |  | Operating full break-in
 |  | Listening only for a specific station or stations
 |  | Closing station now
 | G2C03 ~ What does it mean when a CW operator sends "KN" at the end of a transmission? | 
 |  | Listening for novice stations
 |  | Operating full break-in
 |  | Closing station now
 | G2C03 ~ What does it mean when a CW operator sends "KN" at the end of a transmission? | 
 | A. | Listening for novice stations
 | B. | Operating full break-in
 | C. | Listening only for a specific station or stations
 | D. | Closing station now
Operating Procedures
Group G2C

## Slide 99
 | G2C04 ~ What does the Q signal "QRL?" mean? | 
 |  | "Will you keep the frequency clear?"
 |  | "Are you operating full break-in" or "Can you operate full break-in?"
 |  | "Are you listening only for a specific station?"
 |  | "Are you busy?", or "Is this frequency in use?"
 | G2C04 ~ What does the Q signal "QRL?" mean? | 
 |  | "Will you keep the frequency clear?"
 |  | "Are you operating full break-in" or "Can you operate full break-in?"
 |  | "Are you listening only for a specific station?"
 | G2C04 ~ What does the Q signal "QRL?" mean? | 
 | A. | "Will you keep the frequency clear?"
 | B. | "Are you operating full break-in" or "Can you operate full break-in?"
 | C. | "Are you listening only for a specific station?"
 | D. | "Are you busy?", or "Is this frequency in use?"
Operating Procedures
Group G2C

## Slide 100
 | G2C05 ~ What is the best speed to use when answering a CQ in Morse code? | 
 |  | The fastest speed at which you are comfortable copying
 |  | The speed at which the CQ was sent
 |  | A slow speed until contact is established
 |  | At the standard calling speed of 5 wpm
 | G2C05 ~ What is the best speed to use when answering a CQ in Morse code? | 
 |  | The fastest speed at which you are comfortable copying
 |  | A slow speed until contact is established
 |  | At the standard calling speed of 5 wpm
 | G2C05 ~ What is the best speed to use when answering a CQ in Morse code? | 
 | A. | The fastest speed at which you are comfortable copying
 | B. | The speed at which the CQ was sent
 | C. | A slow speed until contact is established
 | D. | At the standard calling speed of 5 wpm
Operating Procedures
Group G2C

## Slide 101
 | G2C06 ~ What does the term "zero beat" mean in CW operation? | 
 |  | Matching the speed of the transmitting station
 |  | Operating split to avoid interference on frequency
 |  | Sending without error
 |  | Matching your transmit frequency to the frequency of a received signal
 | G2C06 ~ What does the term "zero beat" mean in CW operation? | 
 |  | Matching the speed of the transmitting station
 |  | Operating split to avoid interference on frequency
 |  | Sending without error
 | G2C06 ~ What does the term "zero beat" mean in CW operation? | 
 | A. | Matching the speed of the transmitting station
 | B. | Operating split to avoid interference on frequency
 | C. | Sending without error
 | D. | Matching your transmit frequency to the frequency of a received signal
Operating Procedures
Group G2C

## Slide 102
 | G2C07 ~ When sending CW, what does a "C" mean when added to the RST report? | 
 |  | Chirpy or unstable signal
 |  | Report was read from an S meter rather than estimated
 |  | 100 percent copy
 |  | Key clicks
 | G2C07 ~ When sending CW, what does a "C" mean when added to the RST report? | 
 |  | Report was read from an S meter rather than estimated
 |  | 100 percent copy
 |  | Key clicks
 | G2C07 ~ When sending CW, what does a "C" mean when added to the RST report? | 
 | A. | Chirpy or unstable signal
 | B. | Report was read from an S meter rather than estimated
 | C. | 100 percent copy
 | D. | Key clicks
Operating Procedures
Group G2C

## Slide 103
 | G2C08 ~ What prosign is sent to indicate the end of a formal message when using CW? | 
 |  | SK
 |  | BK
 |  | AR
 |  | KN
 | G2C08 ~ What prosign is sent to indicate the end of a formal message when using CW? | 
 |  | SK
 |  | BK
 |  | KN
 | G2C08 ~ What prosign is sent to indicate the end of a formal message when using CW? | 
 | A. | SK
 | B. | BK
 | C. | AR
 | D. | KN
Operating Procedures
Group G2C

## Slide 104
 | G2C09 ~ What does the Q signal "QSL" mean? | 
 |  | Send slower
 |  | We have already confirmed by card
 |  | I acknowledge receipt
 |  | We have worked before
 | G2C09 ~ What does the Q signal "QSL" mean? | 
 |  | Send slower
 |  | We have already confirmed by card
 |  | We have worked before
 | G2C09 ~ What does the Q signal "QSL" mean? | 
 | A. | Send slower
 | B. | We have already confirmed by card
 | C. | I acknowledge receipt
 | D. | We have worked before
Operating Procedures
Group G2C

## Slide 105
 | G2C10 ~ What does the Q signal "QRN" mean? | 
 |  | Send more slowly
 |  | I am troubled by static
 |  | Zero beat my signal
 |  | Stop sending
 | G2C10 ~ What does the Q signal "QRN" mean? | 
 |  | Send more slowly
 |  | Zero beat my signal
 |  | Stop sending
 | G2C10 ~ What does the Q signal "QRN" mean? | 
 | A. | Send more slowly
 | B. | I am troubled by static
 | C. | Zero beat my signal
 | D. | Stop sending
Operating Procedures
Group G2C

## Slide 106
 | G2C11 ~ What does the Q signal "QRV" mean? | 
 |  | You are sending too fast
 |  | There is interference on the frequency
 |  | I am quitting for the day
 |  | I am ready to receive messages
 | G2C11 ~ What does the Q signal "QRV" mean? | 
 |  | You are sending too fast
 |  | There is interference on the frequency
 |  | I am quitting for the day
 | G2C11 ~ What does the Q signal "QRV" mean? | 
 | A. | You are sending too fast
 | B. | There is interference on the frequency
 | C. | I am quitting for the day
 | D. | I am ready to receive messages
Operating Procedures
Group G2C

## Slide 107
G2D01
G2D02
G2D03
G2D04
G2D05
G2D06
G2D07
G2D08
G2D09
G2D10
G2D11
Operating Procedures
Group G2D (11 Questions)
Amateur Auxiliary; minimizing interference; HF operations
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 108
 | G2D01 ~ What is the Amateur Auxiliary to the FCC? | 
 |  | Amateur volunteers who are formally enlisted to monitor the airwaves for rules violations
 |  | Amateur volunteers who conduct amateur licensing examinations
 |  | Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
 |  | Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency
 | G2D01 ~ What is the Amateur Auxiliary to the FCC? | 
 |  | Amateur volunteers who conduct amateur licensing examinations
 |  | Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
 |  | Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency
 | G2D01 ~ What is the Amateur Auxiliary to the FCC? | 
 | A. | Amateur volunteers who are formally enlisted to monitor the airwaves for rules violations
 | B. | Amateur volunteers who conduct amateur licensing examinations
 | C. | Amateur volunteers who conduct frequency coordination for amateur VHF repeaters
 | D. | Amateur volunteers who use their station equipment to help civil defense organizations in times of emergency
Operating Procedures
Group G2D

## Slide 109
 | G2D02 ~ Which of the following are objectives of the Amateur Auxiliary? | 
 |  | To conduct efficient and orderly amateur licensing examinations
 |  | To encourage self-regulation and compliance with the rules by radio amateur operators
 |  | To coordinate repeaters for efficient and orderly spectrum usage
 |  | To provide emergency and public safety communications
 | G2D02 ~ Which of the following are objectives of the Amateur Auxiliary? | 
 |  | To conduct efficient and orderly amateur licensing examinations
 |  | To coordinate repeaters for efficient and orderly spectrum usage
 |  | To provide emergency and public safety communications
 | G2D02 ~ Which of the following are objectives of the Amateur Auxiliary? | 
 | A. | To conduct efficient and orderly amateur licensing examinations
 | B. | To encourage self-regulation and compliance with the rules by radio amateur operators
 | C. | To coordinate repeaters for efficient and orderly spectrum usage
 | D. | To provide emergency and public safety communications
Operating Procedures
Group G2D

## Slide 110
 | G2D03 ~ What skills learned during hidden transmitter hunts are of help to the Amateur Auxiliary? | 
 |  | Identification of out of band operation
 |  | Direction finding used to locate stations violating FCC Rules
 |  | Identification of different call signs
 |  | Hunters have an opportunity to transmit on non-amateur frequencies
 | G2D03 ~ What skills learned during hidden transmitter hunts are of help to the Amateur Auxiliary? | 
 |  | Identification of out of band operation
 |  | Identification of different call signs
 |  | Hunters have an opportunity to transmit on non-amateur frequencies
 | G2D03 ~ What skills learned during hidden transmitter hunts are of help to the Amateur Auxiliary? | 
 | A. | Identification of out of band operation
 | B. | Direction finding used to locate stations violating FCC Rules
 | C. | Identification of different call signs
 | D. | Hunters have an opportunity to transmit on non-amateur frequencies
Operating Procedures
Group G2D

## Slide 111
 | G2D04 ~ Which of the following describes an azimuthal projection map? | 
 |  | A map that shows accurate land masses
 |  | A map that shows true bearings and distances from a particular location
 |  | A map that shows the angle at which an amateur satellite crosses the equator
 |  | A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit
 | G2D04 ~ Which of the following describes an azimuthal projection map? | 
 |  | A map that shows accurate land masses
 |  | A map that shows the angle at which an amateur satellite crosses the equator
 |  | A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit
 | G2D04 ~ Which of the following describes an azimuthal projection map? | 
 | A. | A map that shows accurate land masses
 | B. | A map that shows true bearings and distances from a particular location
 | C. | A map that shows the angle at which an amateur satellite crosses the equator
 | D. | A map that shows the number of degrees longitude that an amateur satellite appears to move westward at the equator with each orbit
Operating Procedures
Group G2D

## Slide 112
 | G2D05 ~ When is it permissible to communicate with amateur stations in countries outside the areas administered by the Federal Communications Commission? | 
 |  | Only when the foreign country has a formal third party agreement filed with the FCC
 |  | When the contact is with amateurs in any country except those whose administrations have notified the ITU that they object to such communications
 |  | When the contact is with amateurs in any country as long as the communication is conducted in English
 |  | Only when the foreign country is a member of the International Amateur Radio Union
 | FCC | 97.111(a)(1)
 | G2D05 ~ When is it permissible to communicate with amateur stations in countries outside the areas administered by the Federal Communications Commission? | 
 |  | Only when the foreign country has a formal third party agreement filed with the FCC
 |  | When the contact is with amateurs in any country as long as the communication is conducted in English
 |  | Only when the foreign country is a member of the International Amateur Radio Union
 | G2D05 ~ When is it permissible to communicate with amateur stations in countries outside the areas administered by the Federal Communications Commission? | 
 | A. | Only when the foreign country has a formal third party agreement filed with the FCC
 | B. | When the contact is with amateurs in any country except those whose administrations have notified the ITU that they object to such communications
 | C. | When the contact is with amateurs in any country as long as the communication is conducted in English
 | D. | Only when the foreign country is a member of the International Amateur Radio Union
Operating Procedures
Group G2D

## Slide 113
 | G2D06 ~ How is a directional antenna pointed when making a "long-path" contact with another station? | 
 |  | Toward the rising Sun
 |  | Along the gray line
 |  | 180 degrees from its short-path heading
 |  | Toward the north
 | G2D06 ~ How is a directional antenna pointed when making a "long-path" contact with another station? | 
 |  | Toward the rising Sun
 |  | Along the gray line
 |  | Toward the north
 | G2D06 ~ How is a directional antenna pointed when making a "long-path" contact with another station? | 
 | A. | Toward the rising Sun
 | B. | Along the gray line
 | C. | 180 degrees from its short-path heading
 | D. | Toward the north
Operating Procedures
Group G2D

## Slide 114
 | G2D07 ~ Which of the following is required by the FCC rules when operating in the 60-meter band? | 
 |  | If you are using other than a dipole antenna, you must keep a record of the gain of your antenna
 |  | You must keep a record of the date, time, frequency, power level and stations worked
 |  | You must keep a record of all third party traffic
 |  | You must keep a record of the manufacturer of your equipment and the antenna used
 | FCC | 97.303(i)
 | G2D07 ~ Which of the following is required by the FCC rules when operating in the 60-meter band? | 
 |  | You must keep a record of the date, time, frequency, power level and stations worked
 |  | You must keep a record of all third party traffic
 |  | You must keep a record of the manufacturer of your equipment and the antenna used
 | G2D07 ~ Which of the following is required by the FCC rules when operating in the 60-meter band? | 
 | A. | If you are using other than a dipole antenna, you must keep a record of the gain of your antenna
 | B. | You must keep a record of the date, time, frequency, power level and stations worked
 | C. | You must keep a record of all third party traffic
 | D. | You must keep a record of the manufacturer of your equipment and the antenna used
Operating Procedures
Group G2D

## Slide 115
 | G2D08 ~ What is a reason why many amateurs keep a station log? | 
 |  | The ITU requires a log of all international contacts
 |  | The ITU requires a log of all international third party traffic
 |  | The log provides evidence of operation needed to renew a license without retest
 |  | To help with a reply if the FCC requests information
 | G2D08 ~ What is a reason why many amateurs keep a station log? | 
 |  | The ITU requires a log of all international contacts
 |  | The ITU requires a log of all international third party traffic
 |  | The log provides evidence of operation needed to renew a license without retest
 | G2D08 ~ What is a reason why many amateurs keep a station log? | 
 | A. | The ITU requires a log of all international contacts
 | B. | The ITU requires a log of all international third party traffic
 | C. | The log provides evidence of operation needed to renew a license without retest
 | D. | To help with a reply if the FCC requests information
Operating Procedures
Group G2D

## Slide 116
 | G2D09 ~ What information is traditionally contained in a station log? | 
 |  | Date and time of contact
 |  | Band and/or frequency of the contact
 |  | Call sign of station contacted and the signal report given
 |  | All of these choices are correct
 | G2D09 ~ What information is traditionally contained in a station log? | 
 |  | Date and time of contact
 |  | Band and/or frequency of the contact
 |  | Call sign of station contacted and the signal report given
 | G2D09 ~ What information is traditionally contained in a station log? | 
 | A. | Date and time of contact
 | B. | Band and/or frequency of the contact
 | C. | Call sign of station contacted and the signal report given
 | D. | All of these choices are correct
Operating Procedures
Group G2D

## Slide 117
 | G2D10 ~ What is QRP operation? | 
 |  | Remote piloted model control
 |  | Low power transmit operation
 |  | Transmission using Quick Response Protocol
 |  | Traffic relay procedure net operation
 | G2D10 ~ What is QRP operation? | 
 |  | Remote piloted model control
 |  | Transmission using Quick Response Protocol
 |  | Traffic relay procedure net operation
 | G2D10 ~ What is QRP operation? | 
 | A. | Remote piloted model control
 | B. | Low power transmit operation
 | C. | Transmission using Quick Response Protocol
 | D. | Traffic relay procedure net operation
Operating Procedures
Group G2D

## Slide 118
 | G2D11 ~ Which HF antenna would be the best to use for minimizing interference? | 
 |  | A quarter-wave vertical antenna
 |  | An isotropic antenna
 |  | A directional antenna
 |  | An omnidirectional antenna
 | G2D11 ~ Which HF antenna would be the best to use for minimizing interference? | 
 |  | A quarter-wave vertical antenna
 |  | An isotropic antenna
 |  | An omnidirectional antenna
 | G2D11 ~ Which HF antenna would be the best to use for minimizing interference? | 
 | A. | A quarter-wave vertical antenna
 | B. | An isotropic antenna
 | C. | A directional antenna
 | D. | An omnidirectional antenna
Operating Procedures
Group G2D

## Slide 119
G2E01
G2E02
G2E03
G2E04
G2E05
G2E06
G2E07
G2E08
G2E09
G2E10
G2E11
G2E12
G2E13
G2E14
Operating Procedures
Group G2E (14 Questions)
Digital operating: procedures, procedural signals and common abbreviations
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 120
 | G2E01 ~ Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter? | 
 |  | USB
 |  | DSB
 |  | CW
 |  | LSB
 | G2E01 ~ Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter? | 
 |  | USB
 |  | DSB
 |  | CW
 | G2E01 ~ Which mode is normally used when sending an RTTY signal via AFSK with an SSB transmitter? | 
 | A. | USB
 | B. | DSB
 | C. | CW
 | D. | LSB
Operating Procedures
Group G2E

## Slide 121
 | G2E02 ~ How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations? | 
 |  | Unplug the data connector temporarily and see if the channel-busy indication is turned off
 |  | Put the modem or controller in a mode which allows monitoring communications without a connection
 |  | Transmit UI packets several times and wait to see if there is a response from another PACTOR station
 |  | Send the message: "Is this frequency in use?"
 | G2E02 ~ How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations? | 
 |  | Unplug the data connector temporarily and see if the channel-busy indication is turned off
 |  | Transmit UI packets several times and wait to see if there is a response from another PACTOR station
 |  | Send the message: "Is this frequency in use?"
 | G2E02 ~ How can a PACTOR modem or controller be used to determine if the channel is in use by other PACTOR stations? | 
 | A. | Unplug the data connector temporarily and see if the channel-busy indication is turned off
 | B. | Put the modem or controller in a mode which allows monitoring communications without a connection
 | C. | Transmit UI packets several times and wait to see if there is a response from another PACTOR station
 | D. | Send the message: "Is this frequency in use?"
Operating Procedures
Group G2E

## Slide 122
 | G2E03 ~ What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission? | 
 |  | Frequent retries or timeouts
 |  | Long pauses in message transmission
 |  | Failure to establish a connection between stations
 |  | All of these choices are correct
 | G2E03 ~ What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission? | 
 |  | Frequent retries or timeouts
 |  | Long pauses in message transmission
 |  | Failure to establish a connection between stations
 | G2E03 ~ What symptoms may result from other signals interfering with a PACTOR or WINMOR transmission? | 
 | A. | Frequent retries or timeouts
 | B. | Long pauses in message transmission
 | C. | Failure to establish a connection between stations
 | D. | All of these choices are correct
Operating Procedures
Group G2E

## Slide 123
 | G2E04 ~ What segment of the 20-meter band is most often used for digital transmissions? | 
 |  | 14.000 - 14.050 MHz
 |  | 14.070 - 14.100 MHz
 |  | 14.150 - 14.225 MHz
 |  | 14.275 - 14.350 MHz
 | G2E04 ~ What segment of the 20-meter band is most often used for digital transmissions? | 
 |  | 14.000 - 14.050 MHz
 |  | 14.150 - 14.225 MHz
 |  | 14.275 - 14.350 MHz
 | G2E04 ~ What segment of the 20-meter band is most often used for digital transmissions? | 
 | A. | 14.000 - 14.050 MHz
 | B. | 14.070 - 14.100 MHz
 | C. | 14.150 - 14.225 MHz
 | D. | 14.275 - 14.350 MHz
Operating Procedures
Group G2E

## Slide 124
 | G2E05 ~ What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band? | 
 |  | LSB
 |  | USB
 |  | DSB
 |  | SSB
 | G2E05 ~ What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band? | 
 |  | LSB
 |  | DSB
 |  | SSB
 | G2E05 ~ What is the standard sideband used to generate a JT65 or JT9 digital signal when using AFSK in any amateur band? | 
 | A. | LSB
 | B. | USB
 | C. | DSB
 | D. | SSB
Operating Procedures
Group G2E

## Slide 125
 | G2E06 ~ What is the most common frequency shift for RTTY emissions in the amateur HF bands? | 
 |  | 85 Hz
 |  | 170 Hz
 |  | 425 Hz
 |  | 850 Hz
 | G2E06 ~ What is the most common frequency shift for RTTY emissions in the amateur HF bands? | 
 |  | 85 Hz
 |  | 425 Hz
 |  | 850 Hz
 | G2E06 ~ What is the most common frequency shift for RTTY emissions in the amateur HF bands? | 
 | A. | 85 Hz
 | B. | 170 Hz
 | C. | 425 Hz
 | D. | 850 Hz
Operating Procedures
Group G2E

## Slide 126
 | G2E07 ~ What segment of the 80-meter band is most commonly used for digital transmissions? | 
 |  | 3570 - 3600 kHz
 |  | 3500 - 3525 kHz
 |  | 3700 - 3750 kHz
 |  | 3775 - 3825 kHz
 | G2E07 ~ What segment of the 80-meter band is most commonly used for digital transmissions? | 
 |  | 3500 - 3525 kHz
 |  | 3700 - 3750 kHz
 |  | 3775 - 3825 kHz
 | G2E07 ~ What segment of the 80-meter band is most commonly used for digital transmissions? | 
 | A. | 3570 - 3600 kHz
 | B. | 3500 - 3525 kHz
 | C. | 3700 - 3750 kHz
 | D. | 3775 - 3825 kHz
Operating Procedures
Group G2E

## Slide 127
 | G2E08 ~ In what segment of the 20-meter band are most PSK31 operations commonly found? | 
 |  | At the bottom of the slow-scan TV segment, near 14.230 MHz
 |  | At the top of the SSB phone segment, near 14.325 MHz
 |  | In the middle of the CW segment, near 14.100 MHz
 |  | Below the RTTY segment, near 14.070 MHz
 | G2E08 ~ In what segment of the 20-meter band are most PSK31 operations commonly found? | 
 |  | At the bottom of the slow-scan TV segment, near 14.230 MHz
 |  | At the top of the SSB phone segment, near 14.325 MHz
 |  | In the middle of the CW segment, near 14.100 MHz
 | G2E08 ~ In what segment of the 20-meter band are most PSK31 operations commonly found? | 
 | A. | At the bottom of the slow-scan TV segment, near 14.230 MHz
 | B. | At the top of the SSB phone segment, near 14.325 MHz
 | C. | In the middle of the CW segment, near 14.100 MHz
 | D. | Below the RTTY segment, near 14.070 MHz
Operating Procedures
Group G2E

## Slide 128
 | G2E09 ~ How do you join a contact between two stations using the PACTOR protocol? | 
 |  | Send broadcast packets containing your call sign while in MONITOR mode
 |  | Transmit a steady carrier until the PACTOR protocol times out and disconnects
 |  | Joining an existing contact is not possible, PACTOR connections are limited to two stations
 |  | Send a NAK response continuously so that the sending station has to pause
 | G2E09 ~ How do you join a contact between two stations using the PACTOR protocol? | 
 |  | Send broadcast packets containing your call sign while in MONITOR mode
 |  | Transmit a steady carrier until the PACTOR protocol times out and disconnects
 |  | Send a NAK response continuously so that the sending station has to pause
 | G2E09 ~ How do you join a contact between two stations using the PACTOR protocol? | 
 | A. | Send broadcast packets containing your call sign while in MONITOR mode
 | B. | Transmit a steady carrier until the PACTOR protocol times out and disconnects
 | C. | Joining an existing contact is not possible, PACTOR connections are limited to two stations
 | D. | Send a NAK response continuously so that the sending station has to pause
Operating Procedures
Group G2E

## Slide 129
 | G2E10 ~ Which of the following is a way to establish contact with a digital messaging system gateway station? | 
 |  | Send an email to the system control operator
 |  | Send QRL in Morse code
 |  | Respond when the station broadcasts its SSID
 |  | Transmit a connect message on the station's published frequency
 | G2E10 ~ Which of the following is a way to establish contact with a digital messaging system gateway station? | 
 |  | Send an email to the system control operator
 |  | Send QRL in Morse code
 |  | Respond when the station broadcasts its SSID
 | G2E10 ~ Which of the following is a way to establish contact with a digital messaging system gateway station? | 
 | A. | Send an email to the system control operator
 | B. | Send QRL in Morse code
 | C. | Respond when the station broadcasts its SSID
 | D. | Transmit a connect message on the station's published frequency
Operating Procedures
Group G2E

## Slide 130
 | G2E11 ~ What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal? | 
 |  | Long Path propagation
 |  | Backscatter propagation
 |  | Insufficient modulation
 |  | Overmodulation
 | G2E11 ~ What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal? | 
 |  | Long Path propagation
 |  | Backscatter propagation
 |  | Insufficient modulation
 | G2E11 ~ What is indicated on a waterfall display by one or more vertical lines adjacent to a PSK31 signal? | 
 | A. | Long Path propagation
 | B. | Backscatter propagation
 | C. | Insufficient modulation
 | D. | Overmodulation
Operating Procedures
Group G2E

## Slide 131
 | G2E12 ~ Which of the following describes a waterfall display? | 
 |  | Frequency is horizontal, signal strength is vertical, time is intensity
 |  | Frequency is vertical, signal strength is intensity, time is horizontal
 |  | Frequency is horizontal, signal strength is intensity, time is vertical
 |  | Frequency is vertical, signal strength is horizontal, time is intensity
 | G2E12 ~ Which of the following describes a waterfall display? | 
 |  | Frequency is horizontal, signal strength is vertical, time is intensity
 |  | Frequency is vertical, signal strength is intensity, time is horizontal
 |  | Frequency is vertical, signal strength is horizontal, time is intensity
 | G2E12 ~ Which of the following describes a waterfall display? | 
 | A. | Frequency is horizontal, signal strength is vertical, time is intensity
 | B. | Frequency is vertical, signal strength is intensity, time is horizontal
 | C. | Frequency is horizontal, signal strength is intensity, time is vertical
 | D. | Frequency is vertical, signal strength is horizontal, time is intensity
Operating Procedures
Group G2E

## Slide 132
 | G2E13 ~ Which communication system sometimes uses the Internet to transfer messages? | 
 |  | Winlink
 |  | RTTY
 |  | ARES
 |  | Skywarn
 | G2E13 ~ Which communication system sometimes uses the Internet to transfer messages? | 
 |  | RTTY
 |  | ARES
 |  | Skywarn
 | G2E13 ~ Which communication system sometimes uses the Internet to transfer messages? | 
 | A. | Winlink
 | B. | RTTY
 | C. | ARES
 | D. | Skywarn
Operating Procedures
Group G2E

## Slide 133
 | G2E14 ~ What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly? | 
 |  | The mark and space frequencies may be reversed
 |  | You may have selected the wrong baud rate
 |  | You may be listening on the wrong sideband
 |  | All of these choices are correct
 | G2E14 ~ What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly? | 
 |  | The mark and space frequencies may be reversed
 |  | You may have selected the wrong baud rate
 |  | You may be listening on the wrong sideband
 | G2E14 ~ What could be wrong if you cannot decode an RTTY or other FSK signal even though it is apparently tuned in properly? | 
 | A. | The mark and space frequencies may be reversed
 | B. | You may have selected the wrong baud rate
 | C. | You may be listening on the wrong sideband
 | D. | All of these choices are correct
Operating Procedures
Group G2E

## Slide 134
Group |  | Questions
G3A | Sunspots and solar radiation; ionospheric disturbances; propagation forecasting and indices | 16
G3B | Maximum Usable Frequency; Lowest Usable Frequency; propagation | 12
G3C | Ionospheric layers; critical angle and frequency; HF scatter; Near Vertical Incidence Sky-wave | 13
3 | Total | 41
Subelement G3 Radio Wave Propagation
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 135
G3A01 | G3A15
G3A02 | G3A16
G3A03 | 
G3A04 | 
G3A05 | 
G3A06 | 
G3A07 | 
G3A08 | 
G3A09 | 
G3A10 | 
G3A11 | 
G3A12 | 
G3A13 | 
G3A14 | 
Radio Wave Propagation
Group G3A (16 Questions)
Sunspots and solar radiation; ionospheric disturbances; propagation forecasting and indices
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 136
 | G3A01 ~ What is the significance of the sunspot number with regard to HF propagation? | 
 |  | Higher sunspot numbers generally indicate a greater probability of good propagation at higher frequencies
 |  | Lower sunspot numbers generally indicate greater probability of sporadic E propagation
 |  | A zero sunspot number indicate radio propagation is not possible on any band
 |  | All of these choices are correct.
 | G3A01 ~ What is the significance of the sunspot number with regard to HF propagation? | 
 |  | Lower sunspot numbers generally indicate greater probability of sporadic E propagation
 |  | A zero sunspot number indicate radio propagation is not possible on any band
 |  | All of these choices are correct.
 | G3A01 ~ What is the significance of the sunspot number with regard to HF propagation? | 
 | A. | Higher sunspot numbers generally indicate a greater probability of good propagation at higher frequencies
 | B. | Lower sunspot numbers generally indicate greater probability of sporadic E propagation
 | C. | A zero sunspot number indicate radio propagation is not possible on any band
 | D. | All of these choices are correct.
Radio Wave Propagation
Group G3A

## Slide 137
 | G3A02 ~ What effect does a Sudden Ionospheric Disturbance have on the daytime ionospheric propagation of HF radio waves? | 
 |  | It enhances propagation on all HF frequencies
 |  | It disrupts signals on lower frequencies more than those on higher frequencies
 |  | It disrupts communications via satellite more than direct communications
 |  | None, because only areas on the night side of the Earth are affected
 | G3A02 ~ What effect does a Sudden Ionospheric Disturbance have on the daytime ionospheric propagation of HF radio waves? | 
 |  | It enhances propagation on all HF frequencies
 |  | It disrupts communications via satellite more than direct communications
 |  | None, because only areas on the night side of the Earth are affected
 | G3A02 ~ What effect does a Sudden Ionospheric Disturbance have on the daytime ionospheric propagation of HF radio waves? | 
 | A. | It enhances propagation on all HF frequencies
 | B. | It disrupts signals on lower frequencies more than those on higher frequencies
 | C. | It disrupts communications via satellite more than direct communications
 | D. | None, because only areas on the night side of the Earth are affected
Radio Wave Propagation
Group G3A

## Slide 138
 | G3A03 ~ Approximately how long does it take the increased ultraviolet and X-ray radiation from solar flares to affect radio propagation on the Earth? | 
 |  | 28 days
 |  | 1 to 2 hours
 |  | 8 minutes
 |  | 20 to 40 hours
 | G3A03 ~ Approximately how long does it take the increased ultraviolet and X-ray radiation from solar flares to affect radio propagation on the Earth? | 
 |  | 28 days
 |  | 1 to 2 hours
 |  | 20 to 40 hours
 | G3A03 ~ Approximately how long does it take the increased ultraviolet and X-ray radiation from solar flares to affect radio propagation on the Earth? | 
 | A. | 28 days
 | B. | 1 to 2 hours
 | C. | 8 minutes
 | D. | 20 to 40 hours
Radio Wave Propagation
Group G3A

## Slide 139
 | G3A04 ~ Which of the following are least reliable for long distance communications during periods of low solar activity? | 
 |  | 80 meters and 160 meters
 |  | 60 meters and 40 meters
 |  | 30 meters and 20 meters
 |  | 15 meters, 12 meters and 10 meters
 | G3A04 ~ Which of the following are least reliable for long distance communications during periods of low solar activity? | 
 |  | 80 meters and 160 meters
 |  | 60 meters and 40 meters
 |  | 30 meters and 20 meters
 | G3A04 ~ Which of the following are least reliable for long distance communications during periods of low solar activity? | 
 | A. | 80 meters and 160 meters
 | B. | 60 meters and 40 meters
 | C. | 30 meters and 20 meters
 | D. | 15 meters, 12 meters and 10 meters
Radio Wave Propagation
Group G3A

## Slide 140
 | G3A05 ~ What is the solar flux index? | 
 |  | A measure of the highest frequency that is useful for ionospheric propagation between two points on the Earth
 |  | A count of sunspots which is adjusted for solar emissions
 |  | Another name for the American sunspot number
 |  | A measure of solar radiation at 10.7 centimeters wavelength
 | G3A05 ~ What is the solar flux index? | 
 |  | A measure of the highest frequency that is useful for ionospheric propagation between two points on the Earth
 |  | A count of sunspots which is adjusted for solar emissions
 |  | Another name for the American sunspot number
 | G3A05 ~ What is the solar flux index? | 
 | A. | A measure of the highest frequency that is useful for ionospheric propagation between two points on the Earth
 | B. | A count of sunspots which is adjusted for solar emissions
 | C. | Another name for the American sunspot number
 | D. | A measure of solar radiation at 10.7 centimeters wavelength
Radio Wave Propagation
Group G3A

## Slide 141
 | G3A06 ~ What is a geomagnetic storm? | 
 |  | A sudden drop in the solar flux index
 |  | A thunderstorm which affects radio propagation
 |  | Ripples in the ionosphere
 |  | A temporary disturbance in the Earth's magnetosphere
 | G3A06 ~ What is a geomagnetic storm? | 
 |  | A sudden drop in the solar flux index
 |  | A thunderstorm which affects radio propagation
 |  | Ripples in the ionosphere
 | G3A06 ~ What is a geomagnetic storm? | 
 | A. | A sudden drop in the solar flux index
 | B. | A thunderstorm which affects radio propagation
 | C. | Ripples in the ionosphere
 | D. | A temporary disturbance in the Earth's magnetosphere
Radio Wave Propagation
Group G3A

## Slide 142
 | G3A07 ~ At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours? | 
 |  | At the summer solstice
 |  | Only at the maximum point of the solar cycle
 |  | Only at the minimum point of the solar cycle
 |  | At any point in the solar cycle
 | G3A07 ~ At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours? | 
 |  | At the summer solstice
 |  | Only at the maximum point of the solar cycle
 |  | Only at the minimum point of the solar cycle
 | G3A07 ~ At what point in the solar cycle does the 20-meter band usually support worldwide propagation during daylight hours? | 
 | A. | At the summer solstice
 | B. | Only at the maximum point of the solar cycle
 | C. | Only at the minimum point of the solar cycle
 | D. | At any point in the solar cycle
Radio Wave Propagation
Group G3A

## Slide 143
 | G3A08 ~ Which of the following effects can a geomagnetic storm have on radio propagation? | 
 |  | Improved high-latitude HF propagation
 |  | Degraded high-latitude HF propagation
 |  | Improved ground-wave propagation
 |  | Improved chances of UHF ducting
 | G3A08 ~ Which of the following effects can a geomagnetic storm have on radio propagation? | 
 |  | Improved high-latitude HF propagation
 |  | Improved ground-wave propagation
 |  | Improved chances of UHF ducting
 | G3A08 ~ Which of the following effects can a geomagnetic storm have on radio propagation? | 
 | A. | Improved high-latitude HF propagation
 | B. | Degraded high-latitude HF propagation
 | C. | Improved ground-wave propagation
 | D. | Improved chances of UHF ducting
Radio Wave Propagation
Group G3A

## Slide 144
 | G3A09 ~ What effect does a high sunspot number have on radio communications? | 
 |  | High-frequency radio signals become weak and distorted
 |  | Frequencies above 300 MHz become usable for long-distance communication
 |  | Long-distance communication in the upper HF and lower VHF range is enhanced
 |  | Microwave communications become unstable
 | G3A09 ~ What effect does a high sunspot number have on radio communications? | 
 |  | High-frequency radio signals become weak and distorted
 |  | Frequencies above 300 MHz become usable for long-distance communication
 |  | Microwave communications become unstable
 | G3A09 ~ What effect does a high sunspot number have on radio communications? | 
 | A. | High-frequency radio signals become weak and distorted
 | B. | Frequencies above 300 MHz become usable for long-distance communication
 | C. | Long-distance communication in the upper HF and lower VHF range is enhanced
 | D. | Microwave communications become unstable
Radio Wave Propagation
Group G3A

## Slide 145
 | G3A10 ~ What causes HF propagation conditions to vary periodically in a 28 day cycle? | 
 |  | Long term oscillations in the upper atmosphere
 |  | Cyclic variation in the Earth's radiation belts
 |  | The Sun's rotation on its axis
 |  | The position of the Moon in its orbit
 | G3A10 ~ What causes HF propagation conditions to vary periodically in a 28 day cycle? | 
 |  | Long term oscillations in the upper atmosphere
 |  | Cyclic variation in the Earth's radiation belts
 |  | The position of the Moon in its orbit
 | G3A10 ~ What causes HF propagation conditions to vary periodically in a 28 day cycle? | 
 | A. | Long term oscillations in the upper atmosphere
 | B. | Cyclic variation in the Earth's radiation belts
 | C. | The Sun's rotation on its axis
 | D. | The position of the Moon in its orbit
Radio Wave Propagation
Group G3A

## Slide 146
 | G3A11 ~ Approximately how long is the typical sunspot cycle? | 
 |  | 8 minutes
 |  | 40 hours
 |  | 28 days
 |  | 11 years
 | G3A11 ~ Approximately how long is the typical sunspot cycle? | 
 |  | 8 minutes
 |  | 40 hours
 |  | 28 days
 | G3A11 ~ Approximately how long is the typical sunspot cycle? | 
 | A. | 8 minutes
 | B. | 40 hours
 | C. | 28 days
 | D. | 11 years
Radio Wave Propagation
Group G3A

## Slide 147
 | G3A12 ~ What does the K-index indicate? | 
 |  | The relative position of sunspots on the surface of the Sun
 |  | The short term stability of the Earth's magnetic field
 |  | The stability of the Sun's magnetic field
 |  | The solar radio flux at Boulder, Colorado
 | G3A12 ~ What does the K-index indicate? | 
 |  | The relative position of sunspots on the surface of the Sun
 |  | The stability of the Sun's magnetic field
 |  | The solar radio flux at Boulder, Colorado
 | G3A12 ~ What does the K-index indicate? | 
 | A. | The relative position of sunspots on the surface of the Sun
 | B. | The short term stability of the Earth's magnetic field
 | C. | The stability of the Sun's magnetic field
 | D. | The solar radio flux at Boulder, Colorado
Radio Wave Propagation
Group G3A

## Slide 148
 | G3A13 ~ What does the A-index indicate? | 
 |  | The relative position of sunspots on the surface of the Sun
 |  | The amount of polarization of the Sun's electric field
 |  | The long term stability of the Earth's geomagnetic field
 |  | The solar radio flux at Boulder, Colorado
 | G3A13 ~ What does the A-index indicate? | 
 |  | The relative position of sunspots on the surface of the Sun
 |  | The amount of polarization of the Sun's electric field
 |  | The solar radio flux at Boulder, Colorado
 | G3A13 ~ What does the A-index indicate? | 
 | A. | The relative position of sunspots on the surface of the Sun
 | B. | The amount of polarization of the Sun's electric field
 | C. | The long term stability of the Earth's geomagnetic field
 | D. | The solar radio flux at Boulder, Colorado
Radio Wave Propagation
Group G3A

## Slide 149
 | G3A14 ~ How are radio communications usually affected by the charged particles that reach the Earth from solar coronal holes? | 
 |  | HF communications are improved
 |  | HF communications are disturbed
 |  | VHF/UHF ducting is improved
 |  | VHF/UHF ducting is disturbed
 | G3A14 ~ How are radio communications usually affected by the charged particles that reach the Earth from solar coronal holes? | 
 |  | HF communications are improved
 |  | VHF/UHF ducting is improved
 |  | VHF/UHF ducting is disturbed
 | G3A14 ~ How are radio communications usually affected by the charged particles that reach the Earth from solar coronal holes? | 
 | A. | HF communications are improved
 | B. | HF communications are disturbed
 | C. | VHF/UHF ducting is improved
 | D. | VHF/UHF ducting is disturbed
Radio Wave Propagation
Group G3A

## Slide 150
 | G3A15 ~ How long does it take charged particles from coronal mass ejections to affect radio propagation on the Earth? | 
 |  | 28 days
 |  | 14 days
 |  | 4 to 8 minutes
 |  | 20 to 40 hours
 | G3A15 ~ How long does it take charged particles from coronal mass ejections to affect radio propagation on the Earth? | 
 |  | 28 days
 |  | 14 days
 |  | 4 to 8 minutes
 | G3A15 ~ How long does it take charged particles from coronal mass ejections to affect radio propagation on the Earth? | 
 | A. | 28 days
 | B. | 14 days
 | C. | 4 to 8 minutes
 | D. | 20 to 40 hours
Radio Wave Propagation
Group G3A

## Slide 151
 | G3A16 ~ What is a possible benefit to radio communications resulting from periods of high geomagnetic activity? | 
 |  | Auroras that can reflect VHF signals
 |  | Higher signal strength for HF signals passing through the polar regions
 |  | Improved HF long path propagation
 |  | Reduced long delayed echoes
 | G3A16 ~ What is a possible benefit to radio communications resulting from periods of high geomagnetic activity? | 
 |  | Higher signal strength for HF signals passing through the polar regions
 |  | Improved HF long path propagation
 |  | Reduced long delayed echoes
 | G3A16 ~ What is a possible benefit to radio communications resulting from periods of high geomagnetic activity? | 
 | A. | Auroras that can reflect VHF signals
 | B. | Higher signal strength for HF signals passing through the polar regions
 | C. | Improved HF long path propagation
 | D. | Reduced long delayed echoes
Radio Wave Propagation
Group G3A

## Slide 152
G3B01
G3B02
G3B03
G3B04
G3B05
G3B06
G3B07
G3B08
G3B09
G3B10
G3B11
G3B12
Radio Wave Propagation
Group G3B (12 Questions)
Maximum Usable Frequency; Lowest Usable Frequency; propagation
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 153
 | G3B01 ~ How might a sky-wave signal sound if it arrives at your receiver by both short path and long path propagation? | 
 |  | Periodic fading approximately every 10 seconds
 |  | Signal strength increased by 3 dB
 |  | The signal might be cancelled causing severe attenuation
 |  | A well-defined echo might be heard
 | G3B01 ~ How might a sky-wave signal sound if it arrives at your receiver by both short path and long path propagation? | 
 |  | Periodic fading approximately every 10 seconds
 |  | Signal strength increased by 3 dB
 |  | The signal might be cancelled causing severe attenuation
 | G3B01 ~ How might a sky-wave signal sound if it arrives at your receiver by both short path and long path propagation? | 
 | A. | Periodic fading approximately every 10 seconds
 | B. | Signal strength increased by 3 dB
 | C. | The signal might be cancelled causing severe attenuation
 | D. | A well-defined echo might be heard
Radio Wave Propagation
Group G3B

## Slide 154
 | G3B02 ~ Which of the following is a good indicator of the possibility of sky-wave propagation on the 6-meter band? | 
 |  | Short skip sky-wave propagation on the 10-meter band
 |  | Long skip sky-wave propagation on the 10-meter band
 |  | Severe attenuation of signals on the 10-meter band
 |  | Long delayed echoes on the 10-meter band
 | G3B02 ~ Which of the following is a good indicator of the possibility of sky-wave propagation on the 6-meter band? | 
 |  | Long skip sky-wave propagation on the 10-meter band
 |  | Severe attenuation of signals on the 10-meter band
 |  | Long delayed echoes on the 10-meter band
 | G3B02 ~ Which of the following is a good indicator of the possibility of sky-wave propagation on the 6-meter band? | 
 | A. | Short skip sky-wave propagation on the 10-meter band
 | B. | Long skip sky-wave propagation on the 10-meter band
 | C. | Severe attenuation of signals on the 10-meter band
 | D. | Long delayed echoes on the 10-meter band
Radio Wave Propagation
Group G3B

## Slide 155
 | G3B03 ~ Which of the following applies when selecting a frequency for lowest attenuation when transmitting on HF? | 
 |  | Select a frequency just below the MUF
 |  | Select a frequency just above the LUF
 |  | Select a frequency just below the critical frequency
 |  | Select a frequency just above the critical frequency
 | G3B03 ~ Which of the following applies when selecting a frequency for lowest attenuation when transmitting on HF? | 
 |  | Select a frequency just above the LUF
 |  | Select a frequency just below the critical frequency
 |  | Select a frequency just above the critical frequency
 | G3B03 ~ Which of the following applies when selecting a frequency for lowest attenuation when transmitting on HF? | 
 | A. | Select a frequency just below the MUF
 | B. | Select a frequency just above the LUF
 | C. | Select a frequency just below the critical frequency
 | D. | Select a frequency just above the critical frequency
Radio Wave Propagation
Group G3B

## Slide 156
 | G3B04 ~ What is a reliable way to determine if the MUF is high enough to support skip propagation between your station and a distant location on frequencies between 14 and 30 MHz? | 
 |  | Listen for signals from an international beacon in the frequency range you plan to use
 |  | Send a series of dots on the band and listen for echoes from your signal
 |  | Check the strength of TV signals from Western Europe
 |  | Check the strength of signals in the MF AM broadcast band
 | G3B04 ~ What is a reliable way to determine if the MUF is high enough to support skip propagation between your station and a distant location on frequencies between 14 and 30 MHz? | 
 |  | Send a series of dots on the band and listen for echoes from your signal
 |  | Check the strength of TV signals from Western Europe
 |  | Check the strength of signals in the MF AM broadcast band
 | G3B04 ~ What is a reliable way to determine if the MUF is high enough to support skip propagation between your station and a distant location on frequencies between 14 and 30 MHz? | 
 | A. | Listen for signals from an international beacon in the frequency range you plan to use
 | B. | Send a series of dots on the band and listen for echoes from your signal
 | C. | Check the strength of TV signals from Western Europe
 | D. | Check the strength of signals in the MF AM broadcast band
Radio Wave Propagation
Group G3B

## Slide 157
 | G3B05 ~ What usually happens to radio waves with frequencies below the MUF and above the LUF when they are sent into the ionosphere? | 
 |  | They are bent back to the Earth
 |  | They pass through the ionosphere
 |  | They are amplified by interaction with the ionosphere
 |  | They are bent and trapped in the ionosphere to circle the Earth
 | G3B05 ~ What usually happens to radio waves with frequencies below the MUF and above the LUF when they are sent into the ionosphere? | 
 |  | They pass through the ionosphere
 |  | They are amplified by interaction with the ionosphere
 |  | They are bent and trapped in the ionosphere to circle the Earth
 | G3B05 ~ What usually happens to radio waves with frequencies below the MUF and above the LUF when they are sent into the ionosphere? | 
 | A. | They are bent back to the Earth
 | B. | They pass through the ionosphere
 | C. | They are amplified by interaction with the ionosphere
 | D. | They are bent and trapped in the ionosphere to circle the Earth
Radio Wave Propagation
Group G3B

## Slide 158
 | G3B06 ~ What usually happens to radio waves with frequencies below the LUF? | 
 |  | They are bent back to the Earth
 |  | They pass through the ionosphere
 |  | They are completely absorbed by the ionosphere
 |  | They are bent and trapped in the ionosphere to circle the Earth
 | G3B06 ~ What usually happens to radio waves with frequencies below the LUF? | 
 |  | They are bent back to the Earth
 |  | They pass through the ionosphere
 |  | They are bent and trapped in the ionosphere to circle the Earth
 | G3B06 ~ What usually happens to radio waves with frequencies below the LUF? | 
 | A. | They are bent back to the Earth
 | B. | They pass through the ionosphere
 | C. | They are completely absorbed by the ionosphere
 | D. | They are bent and trapped in the ionosphere to circle the Earth
Radio Wave Propagation
Group G3B

## Slide 159
 | G3B07 ~ What does LUF stand for? | 
 |  | The Lowest Usable Frequency for communications between two points
 |  | The Longest Universal Function for communications between two points
 |  | The Lowest Usable Frequency during a 24 hour period
 |  | The Longest Universal Function during a 24 hour period
 | G3B07 ~ What does LUF stand for? | 
 |  | The Longest Universal Function for communications between two points
 |  | The Lowest Usable Frequency during a 24 hour period
 |  | The Longest Universal Function during a 24 hour period
 | G3B07 ~ What does LUF stand for? | 
 | A. | The Lowest Usable Frequency for communications between two points
 | B. | The Longest Universal Function for communications between two points
 | C. | The Lowest Usable Frequency during a 24 hour period
 | D. | The Longest Universal Function during a 24 hour period
Radio Wave Propagation
Group G3B

## Slide 160
 | G3B08 ~ What does MUF stand for? | 
 |  | The Minimum Usable Frequency for communications between two points
 |  | The Maximum Usable Frequency for communications between two points
 |  | The Minimum Usable Frequency during a 24 hour period
 |  | The Maximum Usable Frequency during a 24 hour period
 | G3B08 ~ What does MUF stand for? | 
 |  | The Minimum Usable Frequency for communications between two points
 |  | The Minimum Usable Frequency during a 24 hour period
 |  | The Maximum Usable Frequency during a 24 hour period
 | G3B08 ~ What does MUF stand for? | 
 | A. | The Minimum Usable Frequency for communications between two points
 | B. | The Maximum Usable Frequency for communications between two points
 | C. | The Minimum Usable Frequency during a 24 hour period
 | D. | The Maximum Usable Frequency during a 24 hour period
Radio Wave Propagation
Group G3B

## Slide 161
 | G3B09 ~ What is the approximate maximum distance along the Earth's surface that is normally covered in one hop using the F2 region? | 
 |  | 180 miles
 |  | 1,200 miles
 |  | 2,500 miles
 |  | 12,000 miles
 | G3B09 ~ What is the approximate maximum distance along the Earth's surface that is normally covered in one hop using the F2 region? | 
 |  | 180 miles
 |  | 1,200 miles
 |  | 12,000 miles
 | G3B09 ~ What is the approximate maximum distance along the Earth's surface that is normally covered in one hop using the F2 region? | 
 | A. | 180 miles
 | B. | 1,200 miles
 | C. | 2,500 miles
 | D. | 12,000 miles
Radio Wave Propagation
Group G3B

## Slide 162
 | G3B10 ~ What is the approximate maximum distance along the Earth's surface that is normally covered in one hop using the E region? | 
 |  | 180 miles
 |  | 1,200 miles
 |  | 2,500 miles
 |  | 12,000 miles
 | G3B10 ~ What is the approximate maximum distance along the Earth's surface that is normally covered in one hop using the E region? | 
 |  | 180 miles
 |  | 2,500 miles
 |  | 12,000 miles
 | G3B10 ~ What is the approximate maximum distance along the Earth's surface that is normally covered in one hop using the E region? | 
 | A. | 180 miles
 | B. | 1,200 miles
 | C. | 2,500 miles
 | D. | 12,000 miles
Radio Wave Propagation
Group G3B

## Slide 163
 | G3B11 ~ What happens to HF propagation when the LUF exceeds the MUF? | 
 |  | No HF radio frequency will support ordinary sky-wave communications over the path
 |  | HF communications over the path are enhanced
 |  | Double hop propagation along the path is more common
 |  | Propagation over the path on all HF frequencies is enhanced
 | G3B11 ~ What happens to HF propagation when the LUF exceeds the MUF? | 
 |  | HF communications over the path are enhanced
 |  | Double hop propagation along the path is more common
 |  | Propagation over the path on all HF frequencies is enhanced
 | G3B11 ~ What happens to HF propagation when the LUF exceeds the MUF? | 
 | A. | No HF radio frequency will support ordinary sky-wave communications over the path
 | B. | HF communications over the path are enhanced
 | C. | Double hop propagation along the path is more common
 | D. | Propagation over the path on all HF frequencies is enhanced
Radio Wave Propagation
Group G3B

## Slide 164
 | G3B12 ~ What factor or factors affect the MUF? | 
 |  | Path distance and location
 |  | Time of day and season
 |  | Solar radiation and ionospheric disturbances
 |  | All of these choices are correct
 | G3B12 ~ What factor or factors affect the MUF? | 
 |  | Path distance and location
 |  | Time of day and season
 |  | Solar radiation and ionospheric disturbances
 | G3B12 ~ What factor or factors affect the MUF? | 
 | A. | Path distance and location
 | B. | Time of day and season
 | C. | Solar radiation and ionospheric disturbances
 | D. | All of these choices are correct
Radio Wave Propagation
Group G3B

## Slide 165
G3C01
G3C02
G3C03
G3C04
G3C05
G3C06
G3C07
G3C08
G3C09
G3C10
G3C11
G3C12
G3C13
Radio Wave Propagation
Group G3C (13 Questions)
Ionospheric layers; critical angle and frequency; HF scatter; Near Vertical Incidence Sky-wave
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 166
 | G3C01 ~ Which ionospheric layer is closest to the surface of the Earth? | 
 |  | The D layer
 |  | The E layer
 |  | The F1 layer
 |  | The F2 layer
 | G3C01 ~ Which ionospheric layer is closest to the surface of the Earth? | 
 |  | The E layer
 |  | The F1 layer
 |  | The F2 layer
 | G3C01 ~ Which ionospheric layer is closest to the surface of the Earth? | 
 | A. | The D layer
 | B. | The E layer
 | C. | The F1 layer
 | D. | The F2 layer
Radio Wave Propagation
Group G3C

## Slide 167
 | G3C02 ~ Where on the Earth do ionospheric layers reach their maximum height? | 
 |  | Where the Sun is overhead
 |  | Where the Sun is on the opposite side of the Earth
 |  | Where the Sun is rising
 |  | Where the Sun has just set
 | G3C02 ~ Where on the Earth do ionospheric layers reach their maximum height? | 
 |  | Where the Sun is on the opposite side of the Earth
 |  | Where the Sun is rising
 |  | Where the Sun has just set
 | G3C02 ~ Where on the Earth do ionospheric layers reach their maximum height? | 
 | A. | Where the Sun is overhead
 | B. | Where the Sun is on the opposite side of the Earth
 | C. | Where the Sun is rising
 | D. | Where the Sun has just set
Radio Wave Propagation
Group G3C

## Slide 168
 | G3C03 ~ Why is the F2 region mainly responsible for the longest distance radio wave propagation? | 
 |  | Because it is the densest ionospheric layer
 |  | Because it does not absorb radio waves as much as other ionospheric regions
 |  | Because it is the highest ionospheric region
 |  | All of these choices are correct
 | G3C03 ~ Why is the F2 region mainly responsible for the longest distance radio wave propagation? | 
 |  | Because it is the densest ionospheric layer
 |  | Because it does not absorb radio waves as much as other ionospheric regions
 |  | All of these choices are correct
 | G3C03 ~ Why is the F2 region mainly responsible for the longest distance radio wave propagation? | 
 | A. | Because it is the densest ionospheric layer
 | B. | Because it does not absorb radio waves as much as other ionospheric regions
 | C. | Because it is the highest ionospheric region
 | D. | All of these choices are correct
Radio Wave Propagation
Group G3C

## Slide 169
 | G3C04 ~ What does the term "critical angle" mean as used in radio wave propagation? | 
 |  | The long path azimuth of a distant station
 |  | The short path azimuth of a distant station
 |  | The lowest takeoff angle that will return a radio wave to the Earth under specific ionospheric conditions
 |  | The highest takeoff angle that will return a radio wave to the Earth under specific ionospheric conditions
 | G3C04 ~ What does the term "critical angle" mean as used in radio wave propagation? | 
 |  | The long path azimuth of a distant station
 |  | The short path azimuth of a distant station
 |  | The lowest takeoff angle that will return a radio wave to the Earth under specific ionospheric conditions
 | G3C04 ~ What does the term "critical angle" mean as used in radio wave propagation? | 
 | A. | The long path azimuth of a distant station
 | B. | The short path azimuth of a distant station
 | C. | The lowest takeoff angle that will return a radio wave to the Earth under specific ionospheric conditions
 | D. | The highest takeoff angle that will return a radio wave to the Earth under specific ionospheric conditions
Radio Wave Propagation
Group G3C

## Slide 170
 | G3C05 ~ Why is long distance communication on the 40-meter, 60-meter, 80-meter and 160-meter bands more difficult during the day? | 
 |  | The F layer absorbs signals at these frequencies during daylight hours
 |  | The F layer is unstable during daylight hours
 |  | The D layer absorbs signals at these frequencies during daylight hours
 |  | The E layer is unstable during daylight hours
 | G3C05 ~ Why is long distance communication on the 40-meter, 60-meter, 80-meter and 160-meter bands more difficult during the day? | 
 |  | The F layer absorbs signals at these frequencies during daylight hours
 |  | The F layer is unstable during daylight hours
 |  | The E layer is unstable during daylight hours
 | G3C05 ~ Why is long distance communication on the 40-meter, 60-meter, 80-meter and 160-meter bands more difficult during the day? | 
 | A. | The F layer absorbs signals at these frequencies during daylight hours
 | B. | The F layer is unstable during daylight hours
 | C. | The D layer absorbs signals at these frequencies during daylight hours
 | D. | The E layer is unstable during daylight hours
Radio Wave Propagation
Group G3C

## Slide 171
 | G3C06 ~ What is a characteristic of HF scatter signals? | 
 |  | They have high intelligibility
 |  | They have a wavering sound
 |  | They have very large swings in signal strength
 |  | All of these choices are correct
 | G3C06 ~ What is a characteristic of HF scatter signals? | 
 |  | They have high intelligibility
 |  | They have very large swings in signal strength
 |  | All of these choices are correct
 | G3C06 ~ What is a characteristic of HF scatter signals? | 
 | A. | They have high intelligibility
 | B. | They have a wavering sound
 | C. | They have very large swings in signal strength
 | D. | All of these choices are correct
Radio Wave Propagation
Group G3C

## Slide 172
 | G3C07 ~ What makes HF scatter signals often sound distorted? | 
 |  | The ionospheric layer involved is unstable
 |  | Ground waves are absorbing much of the signal
 |  | The E-region is not present
 |  | Energy is scattered into the skip zone through several different radio wave paths
 | G3C07 ~ What makes HF scatter signals often sound distorted? | 
 |  | The ionospheric layer involved is unstable
 |  | Ground waves are absorbing much of the signal
 |  | The E-region is not present
 | G3C07 ~ What makes HF scatter signals often sound distorted? | 
 | A. | The ionospheric layer involved is unstable
 | B. | Ground waves are absorbing much of the signal
 | C. | The E-region is not present
 | D. | Energy is scattered into the skip zone through several different radio wave paths
Radio Wave Propagation
Group G3C

## Slide 173
 | G3C08 ~ Why are HF scatter signals in the skip zone usually weak? | 
 |  | Only a small part of the signal energy is scattered into the skip zone
 |  | Signals are scattered from the magnetosphere which is not a good reflector
 |  | Propagation is through ground waves which absorb most of the signal energy
 |  | Propagations is through ducts in F region which absorb most of the energy
 | G3C08 ~ Why are HF scatter signals in the skip zone usually weak? | 
 |  | Signals are scattered from the magnetosphere which is not a good reflector
 |  | Propagation is through ground waves which absorb most of the signal energy
 |  | Propagations is through ducts in F region which absorb most of the energy
 | G3C08 ~ Why are HF scatter signals in the skip zone usually weak? | 
 | A. | Only a small part of the signal energy is scattered into the skip zone
 | B. | Signals are scattered from the magnetosphere which is not a good reflector
 | C. | Propagation is through ground waves which absorb most of the signal energy
 | D. | Propagations is through ducts in F region which absorb most of the energy
Radio Wave Propagation
Group G3C

## Slide 174
 | G3C09 ~ What type of radio wave propagation allows a signal to be detected at a distance too far for ground wave propagation but too near for normal sky-wave propagation? | 
 |  | Faraday rotation
 |  | Scatter
 |  | Sporadic-E skip
 |  | Short-path skip
 | G3C09 ~ What type of radio wave propagation allows a signal to be detected at a distance too far for ground wave propagation but too near for normal sky-wave propagation? | 
 |  | Faraday rotation
 |  | Sporadic-E skip
 |  | Short-path skip
 | G3C09 ~ What type of radio wave propagation allows a signal to be detected at a distance too far for ground wave propagation but too near for normal sky-wave propagation? | 
 | A. | Faraday rotation
 | B. | Scatter
 | C. | Sporadic-E skip
 | D. | Short-path skip
Radio Wave Propagation
Group G3C

## Slide 175
 | G3C10 ~ Which of the following might be an indication that signals heard on the HF bands are being received via scatter propagation? | 
 |  | The communication is during a sunspot maximum
 |  | The communication is during a sudden ionospheric disturbance
 |  | The signal is heard on a frequency below the Maximum Usable Frequency
 |  | The signal is heard on a frequency above the Maximum Usable Frequency
 | G3C10 ~ Which of the following might be an indication that signals heard on the HF bands are being received via scatter propagation? | 
 |  | The communication is during a sunspot maximum
 |  | The communication is during a sudden ionospheric disturbance
 |  | The signal is heard on a frequency below the Maximum Usable Frequency
 | G3C10 ~ Which of the following might be an indication that signals heard on the HF bands are being received via scatter propagation? | 
 | A. | The communication is during a sunspot maximum
 | B. | The communication is during a sudden ionospheric disturbance
 | C. | The signal is heard on a frequency below the Maximum Usable Frequency
 | D. | The signal is heard on a frequency above the Maximum Usable Frequency
Radio Wave Propagation
Group G3C

## Slide 176
 | G3C11 ~ Which of the following antenna types will be most effective for skip communications on 40-meters during the day? | 
 |  | A vertical antenna
 |  | A horizontal dipole placed between 1/8 and 1/4 wavelength above the ground
 |  | A left-hand circularly polarized antenna
 |  | A right-hand circularly polarized antenna
 | G3C11 ~ Which of the following antenna types will be most effective for skip communications on 40-meters during the day? | 
 |  | A vertical antenna
 |  | A left-hand circularly polarized antenna
 |  | A right-hand circularly polarized antenna
 | G3C11 ~ Which of the following antenna types will be most effective for skip communications on 40-meters during the day? | 
 | A. | A vertical antenna
 | B. | A horizontal dipole placed between 1/8 and 1/4 wavelength above the ground
 | C. | A left-hand circularly polarized antenna
 | D. | A right-hand circularly polarized antenna
Radio Wave Propagation
Group G3C

## Slide 177
 | G3C12 ~ Which ionospheric layer is the most absorbent of long skip signals during daylight hours on frequencies below 10 MHz? | 
 |  | The F2 layer
 |  | The F1 layer
 |  | The E layer
 |  | The D layer
 | G3C12 ~ Which ionospheric layer is the most absorbent of long skip signals during daylight hours on frequencies below 10 MHz? | 
 |  | The F2 layer
 |  | The F1 layer
 |  | The E layer
 | G3C12 ~ Which ionospheric layer is the most absorbent of long skip signals during daylight hours on frequencies below 10 MHz? | 
 | A. | The F2 layer
 | B. | The F1 layer
 | C. | The E layer
 | D. | The D layer
Radio Wave Propagation
Group G3C

## Slide 178
 | G3C13 ~ What is Near Vertical Incidence Sky-wave (NVIS) propagation? | 
 |  | Propagation near the MUF
 |  | Short distance MF or HF propagation using high elevation angles
 |  | Long path HF propagation at sunrise and sunset
 |  | Double hop propagation near the LUF
 | G3C13 ~ What is Near Vertical Incidence Sky-wave (NVIS) propagation? | 
 |  | Propagation near the MUF
 |  | Long path HF propagation at sunrise and sunset
 |  | Double hop propagation near the LUF
 | G3C13 ~ What is Near Vertical Incidence Sky-wave (NVIS) propagation? | 
 | A. | Propagation near the MUF
 | B. | Short distance MF or HF propagation using high elevation angles
 | C. | Long path HF propagation at sunrise and sunset
 | D. | Double hop propagation near the LUF
Radio Wave Propagation
Group G3C

## Slide 179
Group |  | Questions
G4A | Station Operation and set up | 15
G4B | Test and monitoring equipment; two-tone test | 15
G4C | Interference with consumer electronics; grounding; DSP | 13
G4D | Speech processors; S meters; sideband operation near band edges | 11
G4E | HF mobile radio installations; emergency and battery powered operation | 11
5 | Total | 65
Subelement G4 Amateur Radio Practices
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 180
G4A01 | G4A15
G4A02 | 
G4A03 | 
G4A04 | 
G4A05 | 
G4A06 | 
G4A07 | 
G4A08 | 
G4A09 | 
G4A10 | 
G4A11 | 
G4A12 | 
G4A13 | 
G4A14 | 
Amateur Radio Practices
Group G4A (15 Questions)
Station Operation and set up
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 181
 | G4A01 ~ What is the purpose of the "notch filter" found on many HF transceivers? | 
 |  | To restrict the transmitter voice bandwidth
 |  | To reduce interference from carriers in the receiver passband
 |  | To eliminate receiver interference from impulse noise sources
 |  | To enhance the reception of a specific frequency on a crowded band
 | G4A01 ~ What is the purpose of the "notch filter" found on many HF transceivers? | 
 |  | To restrict the transmitter voice bandwidth
 |  | To eliminate receiver interference from impulse noise sources
 |  | To enhance the reception of a specific frequency on a crowded band
 | G4A01 ~ What is the purpose of the "notch filter" found on many HF transceivers? | 
 | A. | To restrict the transmitter voice bandwidth
 | B. | To reduce interference from carriers in the receiver passband
 | C. | To eliminate receiver interference from impulse noise sources
 | D. | To enhance the reception of a specific frequency on a crowded band
Amateur Radio Practices
Group G4A

## Slide 182
 | G4A02 ~ What is one advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver? | 
 |  | Interference from impulse noise will be eliminated
 |  | More stations can be accommodated within a given signal passband
 |  | It may be possible to reduce or eliminate interference from other signals
 |  | Accidental out of band operation can be prevented
 | G4A02 ~ What is one advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver? | 
 |  | Interference from impulse noise will be eliminated
 |  | More stations can be accommodated within a given signal passband
 |  | Accidental out of band operation can be prevented
 | G4A02 ~ What is one advantage of selecting the opposite or "reverse" sideband when receiving CW signals on a typical HF transceiver? | 
 | A. | Interference from impulse noise will be eliminated
 | B. | More stations can be accommodated within a given signal passband
 | C. | It may be possible to reduce or eliminate interference from other signals
 | D. | Accidental out of band operation can be prevented
Amateur Radio Practices
Group G4A

## Slide 183
 | G4A03 ~ What is normally meant by operating a transceiver in "split" mode? | 
 |  | The radio is operating at half power
 |  | The transceiver is operating from an external power source
 |  | The transceiver is set to different transmit and receive frequencies
 |  | The transmitter is emitting an SSB signal, as opposed to DSB operation
 | G4A03 ~ What is normally meant by operating a transceiver in "split" mode? | 
 |  | The radio is operating at half power
 |  | The transceiver is operating from an external power source
 |  | The transmitter is emitting an SSB signal, as opposed to DSB operation
 | G4A03 ~ What is normally meant by operating a transceiver in "split" mode? | 
 | A. | The radio is operating at half power
 | B. | The transceiver is operating from an external power source
 | C. | The transceiver is set to different transmit and receive frequencies
 | D. | The transmitter is emitting an SSB signal, as opposed to DSB operation
Amateur Radio Practices
Group G4A

## Slide 184
 | G4A04 ~ What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control? | 
 |  | A pronounced peak
 |  | A pronounced dip
 |  | No change will be observed
 |  | A slow, rhythmic oscillation
 | G4A04 ~ What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control? | 
 |  | A pronounced peak
 |  | No change will be observed
 |  | A slow, rhythmic oscillation
 | G4A04 ~ What reading on the plate current meter of a vacuum tube RF power amplifier indicates correct adjustment of the plate tuning control? | 
 | A. | A pronounced peak
 | B. | A pronounced dip
 | C. | No change will be observed
 | D. | A slow, rhythmic oscillation
Amateur Radio Practices
Group G4A

## Slide 185
 | G4A05 ~ What is a reason to use Automatic Level Control (ALC) with an RF power amplifier? | 
 |  | To balance the transmitter audio frequency response
 |  | To reduce harmonic radiation
 |  | To reduce distortion due to excessive drive
 |  | To increase overall efficiency
 | G4A05 ~ What is a reason to use Automatic Level Control (ALC) with an RF power amplifier? | 
 |  | To balance the transmitter audio frequency response
 |  | To reduce harmonic radiation
 |  | To increase overall efficiency
 | G4A05 ~ What is a reason to use Automatic Level Control (ALC) with an RF power amplifier? | 
 | A. | To balance the transmitter audio frequency response
 | B. | To reduce harmonic radiation
 | C. | To reduce distortion due to excessive drive
 | D. | To increase overall efficiency
Amateur Radio Practices
Group G4A

## Slide 186
 | G4A06 ~ What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms? | 
 |  | Balanced modulator
 |  | SWR Bridge
 |  | Antenna coupler or antenna tuner
 |  | Q Multiplier
 | G4A06 ~ What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms? | 
 |  | Balanced modulator
 |  | SWR Bridge
 |  | Q Multiplier
 | G4A06 ~ What type of device is often used to match transmitter output impedance to an impedance not equal to 50 ohms? | 
 | A. | Balanced modulator
 | B. | SWR Bridge
 | C. | Antenna coupler or antenna tuner
 | D. | Q Multiplier
Amateur Radio Practices
Group G4A

## Slide 187
 | G4A07 ~ What condition can lead to permanent damage to a solid-state RF power amplifier? | 
 |  | Insufficient drive power
 |  | Low input SWR
 |  | Shorting the input signal to ground
 |  | Excessive drive power
 | G4A07 ~ What condition can lead to permanent damage to a solid-state RF power amplifier? | 
 |  | Insufficient drive power
 |  | Low input SWR
 |  | Shorting the input signal to ground
 | G4A07 ~ What condition can lead to permanent damage to a solid-state RF power amplifier? | 
 | A. | Insufficient drive power
 | B. | Low input SWR
 | C. | Shorting the input signal to ground
 | D. | Excessive drive power
Amateur Radio Practices
Group G4A

## Slide 188
 | G4A08 ~ What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier? | 
 |  | Minimum SWR on the antenna
 |  | Minimum plate current without exceeding maximum allowable grid current
 |  | Highest plate voltage while minimizing grid current
 |  | Maximum power output without exceeding maximum allowable plate current
 | G4A08 ~ What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier? | 
 |  | Minimum SWR on the antenna
 |  | Minimum plate current without exceeding maximum allowable grid current
 |  | Highest plate voltage while minimizing grid current
 | G4A08 ~ What is the correct adjustment for the load or coupling control of a vacuum tube RF power amplifier? | 
 | A. | Minimum SWR on the antenna
 | B. | Minimum plate current without exceeding maximum allowable grid current
 | C. | Highest plate voltage while minimizing grid current
 | D. | Maximum power output without exceeding maximum allowable plate current
Amateur Radio Practices
Group G4A

## Slide 189
 | G4A09 ~ Why is a time delay sometimes included in a transmitter keying circuit? | 
 |  | To prevent stations from interfering with one another
 |  | To allow the transmitter power regulators to charge properly
 |  | To allow time for transmit-receive changeover operations to complete properly before RF output is allowed
 |  | To allow time for a warning signal to be sent to other stations
 | G4A09 ~ Why is a time delay sometimes included in a transmitter keying circuit? | 
 |  | To prevent stations from interfering with one another
 |  | To allow the transmitter power regulators to charge properly
 |  | To allow time for a warning signal to be sent to other stations
 | G4A09 ~ Why is a time delay sometimes included in a transmitter keying circuit? | 
 | A. | To prevent stations from interfering with one another
 | B. | To allow the transmitter power regulators to charge properly
 | C. | To allow time for transmit-receive changeover operations to complete properly before RF output is allowed
 | D. | To allow time for a warning signal to be sent to other stations
Amateur Radio Practices
Group G4A

## Slide 190
 | G4A10 ~ What is the purpose of an electronic keyer? | 
 |  | Automatic transmit/receive switching
 |  | Automatic generation of strings of dots and dashes for CW operation
 |  | VOX operation
 |  | Computer interface for PSK and RTTY operation
 | G4A10 ~ What is the purpose of an electronic keyer? | 
 |  | Automatic transmit/receive switching
 |  | VOX operation
 |  | Computer interface for PSK and RTTY operation
 | G4A10 ~ What is the purpose of an electronic keyer? | 
 | A. | Automatic transmit/receive switching
 | B. | Automatic generation of strings of dots and dashes for CW operation
 | C. | VOX operation
 | D. | Computer interface for PSK and RTTY operation
Amateur Radio Practices
Group G4A

## Slide 191
 | G4A11 ~ Which of the following is a use for the IF shift control on a receiver? | 
 |  | To avoid interference from stations very close to the receive frequency
 |  | To change frequency rapidly
 |  | To permit listening on a different frequency from that on which you are transmitting
 |  | To tune in stations that are slightly off frequency without changing your transmit frequency
 | G4A11 ~ Which of the following is a use for the IF shift control on a receiver? | 
 |  | To change frequency rapidly
 |  | To permit listening on a different frequency from that on which you are transmitting
 |  | To tune in stations that are slightly off frequency without changing your transmit frequency
 | G4A11 ~ Which of the following is a use for the IF shift control on a receiver? | 
 | A. | To avoid interference from stations very close to the receive frequency
 | B. | To change frequency rapidly
 | C. | To permit listening on a different frequency from that on which you are transmitting
 | D. | To tune in stations that are slightly off frequency without changing your transmit frequency
Amateur Radio Practices
Group G4A

## Slide 192
 | G4A12 ~ Which of the following is a common use for the dual VFO feature on a transceiver? | 
 |  | To allow transmitting on two frequencies at once
 |  | To permit full duplex operation, that is transmitting and receiving at the same time
 |  | To permit monitoring of two different frequencies
 |  | To facilitate computer interface
 | G4A12 ~ Which of the following is a common use for the dual VFO feature on a transceiver? | 
 |  | To allow transmitting on two frequencies at once
 |  | To permit full duplex operation, that is transmitting and receiving at the same time
 |  | To facilitate computer interface
 | G4A12 ~ Which of the following is a common use for the dual VFO feature on a transceiver? | 
 | A. | To allow transmitting on two frequencies at once
 | B. | To permit full duplex operation, that is transmitting and receiving at the same time
 | C. | To permit monitoring of two different frequencies
 | D. | To facilitate computer interface
Amateur Radio Practices
Group G4A

## Slide 193
 | G4A13 ~ What is one reason to use the attenuator function that is present on many HF transceivers? | 
 |  | To reduce signal overload due to strong incoming signals
 |  | To reduce the transmitter power when driving a linear amplifier
 |  | To reduce power consumption when operating from batteries
 |  | To slow down received CW signals for better copy
 | G4A13 ~ What is one reason to use the attenuator function that is present on many HF transceivers? | 
 |  | To reduce the transmitter power when driving a linear amplifier
 |  | To reduce power consumption when operating from batteries
 |  | To slow down received CW signals for better copy
 | G4A13 ~ What is one reason to use the attenuator function that is present on many HF transceivers? | 
 | A. | To reduce signal overload due to strong incoming signals
 | B. | To reduce the transmitter power when driving a linear amplifier
 | C. | To reduce power consumption when operating from batteries
 | D. | To slow down received CW signals for better copy
Amateur Radio Practices
Group G4A

## Slide 194
 | G4A14 ~ What is likely to happen if a transceiver's ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode? | 
 |  | ALC will invert the modulation of the AFSK mode
 |  | Improper action of ALC distorts the signal and can cause spurious emissions
 |  | When using digital modes, too much ALC activity can cause the transmitter to overheat
 |  | All of these choices are correct
 | G4A14 ~ What is likely to happen if a transceiver's ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode? | 
 |  | ALC will invert the modulation of the AFSK mode
 |  | When using digital modes, too much ALC activity can cause the transmitter to overheat
 |  | All of these choices are correct
 | G4A14 ~ What is likely to happen if a transceiver's ALC system is not set properly when transmitting AFSK signals with the radio using single sideband mode? | 
 | A. | ALC will invert the modulation of the AFSK mode
 | B. | Improper action of ALC distorts the signal and can cause spurious emissions
 | C. | When using digital modes, too much ALC activity can cause the transmitter to overheat
 | D. | All of these choices are correct
Amateur Radio Practices
Group G4A

## Slide 195
 | G4A15 ~ Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver? | 
 |  | The VOX circuit does not un-key the transmitter
 |  | The transmitter signal is distorted
 |  | Frequent connection timeouts
 |  | All of these choices are correct
 | G4A15 ~ Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver? | 
 |  | The VOX circuit does not un-key the transmitter
 |  | The transmitter signal is distorted
 |  | Frequent connection timeouts
 | G4A15 ~ Which of the following can be a symptom of transmitted RF being picked up by an audio cable carrying AFSK data signals between a computer and a transceiver? | 
 | A. | The VOX circuit does not un-key the transmitter
 | B. | The transmitter signal is distorted
 | C. | Frequent connection timeouts
 | D. | All of these choices are correct
Amateur Radio Practices
Group G4A

## Slide 196
G4B01 | G4B15
G4B02 | 
G4B03 | 
G4B04 | 
G4B05 | 
G4B06 | 
G4B07 | 
G4B08 | 
G4B09 | 
G4B10 | 
G4B11 | 
G4B12 | 
G4B13 | 
G4B14 | 
Amateur Radio Practices
Group G4B (15 Questions)
Test and monitoring equipment; two-tone test
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 197
 | G4B01 ~ What item of test equipment contains horizontal and vertical channel amplifiers? | 
 |  | An ohmmeter
 |  | A signal generator
 |  | An ammeter
 |  | An oscilloscope
 | G4B01 ~ What item of test equipment contains horizontal and vertical channel amplifiers? | 
 |  | An ohmmeter
 |  | A signal generator
 |  | An ammeter
 | G4B01 ~ What item of test equipment contains horizontal and vertical channel amplifiers? | 
 | A. | An ohmmeter
 | B. | A signal generator
 | C. | An ammeter
 | D. | An oscilloscope
Amateur Radio Practices
Group G4B

## Slide 198
 | G4B02 ~ Which of the following is an advantage of an oscilloscope versus a digital voltmeter? | 
 |  | An oscilloscope uses less power
 |  | Complex impedances can be easily measured
 |  | Input impedance is much lower
 |  | Complex waveforms can be measured
 | G4B02 ~ Which of the following is an advantage of an oscilloscope versus a digital voltmeter? | 
 |  | An oscilloscope uses less power
 |  | Complex impedances can be easily measured
 |  | Input impedance is much lower
 | G4B02 ~ Which of the following is an advantage of an oscilloscope versus a digital voltmeter? | 
 | A. | An oscilloscope uses less power
 | B. | Complex impedances can be easily measured
 | C. | Input impedance is much lower
 | D. | Complex waveforms can be measured
Amateur Radio Practices
Group G4B

## Slide 199
 | G4B03 ~ Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter? | 
 |  | An oscilloscope
 |  | A field strength meter
 |  | A sidetone monitor
 |  | A wavemeter
 | G4B03 ~ Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter? | 
 |  | A field strength meter
 |  | A sidetone monitor
 |  | A wavemeter
 | G4B03 ~ Which of the following is the best instrument to use when checking the keying waveform of a CW transmitter? | 
 | A. | An oscilloscope
 | B. | A field strength meter
 | C. | A sidetone monitor
 | D. | A wavemeter
Amateur Radio Practices
Group G4B

## Slide 200
 | G4B04 ~ What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal? | 
 |  | The local oscillator of the transmitter
 |  | An external RF oscillator
 |  | The transmitter balanced mixer output
 |  | The attenuated RF output of the transmitter
 | G4B04 ~ What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal? | 
 |  | The local oscillator of the transmitter
 |  | An external RF oscillator
 |  | The transmitter balanced mixer output
 | G4B04 ~ What signal source is connected to the vertical input of an oscilloscope when checking the RF envelope pattern of a transmitted signal? | 
 | A. | The local oscillator of the transmitter
 | B. | An external RF oscillator
 | C. | The transmitter balanced mixer output
 | D. | The attenuated RF output of the transmitter
Amateur Radio Practices
Group G4B

## Slide 201
 | G4B05 ~ Why is high input impedance desirable for a voltmeter? | 
 |  | It improves the frequency response
 |  | It decreases battery consumption in the meter
 |  | It improves the resolution of the readings
 |  | It decreases the loading on circuits being measured
 | G4B05 ~ Why is high input impedance desirable for a voltmeter? | 
 |  | It improves the frequency response
 |  | It decreases battery consumption in the meter
 |  | It improves the resolution of the readings
 | G4B05 ~ Why is high input impedance desirable for a voltmeter? | 
 | A. | It improves the frequency response
 | B. | It decreases battery consumption in the meter
 | C. | It improves the resolution of the readings
 | D. | It decreases the loading on circuits being measured
Amateur Radio Practices
Group G4B

## Slide 202
 | G4B06 ~ What is an advantage of a digital voltmeter as compared to an analog voltmeter? | 
 |  | Better for measuring computer circuits
 |  | Better for RF measurements
 |  | Better precision for most uses
 |  | Faster response
 | G4B06 ~ What is an advantage of a digital voltmeter as compared to an analog voltmeter? | 
 |  | Better for measuring computer circuits
 |  | Better for RF measurements
 |  | Faster response
 | G4B06 ~ What is an advantage of a digital voltmeter as compared to an analog voltmeter? | 
 | A. | Better for measuring computer circuits
 | B. | Better for RF measurements
 | C. | Better precision for most uses
 | D. | Faster response
Amateur Radio Practices
Group G4B

## Slide 203
 | G4B07 ~ What signals are used to conduct a two-tone test? | 
 |  | Two audio signals of the same frequency shifted 90 degrees
 |  | Two non-harmonically related audio signals
 |  | Two swept frequency tones
 |  | Two audio frequency range square wave signals of equal amplitude
 | G4B07 ~ What signals are used to conduct a two-tone test? | 
 |  | Two audio signals of the same frequency shifted 90 degrees
 |  | Two swept frequency tones
 |  | Two audio frequency range square wave signals of equal amplitude
 | G4B07 ~ What signals are used to conduct a two-tone test? | 
 | A. | Two audio signals of the same frequency shifted 90 degrees
 | B. | Two non-harmonically related audio signals
 | C. | Two swept frequency tones
 | D. | Two audio frequency range square wave signals of equal amplitude
Amateur Radio Practices
Group G4B

## Slide 204
 | G4B08 ~ Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments? | 
 |  | A field strength meter
 |  | An antenna noise bridge
 |  | A multimeter
 |  | A Q meter
 | G4B08 ~ Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments? | 
 |  | An antenna noise bridge
 |  | A multimeter
 |  | A Q meter
 | G4B08 ~ Which of the following instruments may be used to monitor relative RF output when making antenna and transmitter adjustments? | 
 | A. | A field strength meter
 | B. | An antenna noise bridge
 | C. | A multimeter
 | D. | A Q meter
Amateur Radio Practices
Group G4B

## Slide 205
 | G4B09 ~ Which of the following can be determined with a field strength meter? | 
 |  | The radiation resistance of an antenna
 |  | The radiation pattern of an antenna
 |  | The presence and amount of phase distortion of a transmitter
 |  | The presence and amount of amplitude distortion of a transmitter
 | G4B09 ~ Which of the following can be determined with a field strength meter? | 
 |  | The radiation resistance of an antenna
 |  | The presence and amount of phase distortion of a transmitter
 |  | The presence and amount of amplitude distortion of a transmitter
 | G4B09 ~ Which of the following can be determined with a field strength meter? | 
 | A. | The radiation resistance of an antenna
 | B. | The radiation pattern of an antenna
 | C. | The presence and amount of phase distortion of a transmitter
 | D. | The presence and amount of amplitude distortion of a transmitter
Amateur Radio Practices
Group G4B

## Slide 206
 | G4B10 ~ Which of the following can be determined with a directional wattmeter? | 
 |  | Standing wave ratio
 |  | Antenna front-to-back ratio
 |  | RF interference
 |  | Radio wave propagation
 | G4B10 ~ Which of the following can be determined with a directional wattmeter? | 
 |  | Antenna front-to-back ratio
 |  | RF interference
 |  | Radio wave propagation
 | G4B10 ~ Which of the following can be determined with a directional wattmeter? | 
 | A. | Standing wave ratio
 | B. | Antenna front-to-back ratio
 | C. | RF interference
 | D. | Radio wave propagation
Amateur Radio Practices
Group G4B

## Slide 207
 | G4B11 ~ Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements? | 
 |  | Receiver
 |  | Transmitter
 |  | Antenna and feed line
 |  | All of these choices are correct
 | G4B11 ~ Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements? | 
 |  | Receiver
 |  | Transmitter
 |  | All of these choices are correct
 | G4B11 ~ Which of the following must be connected to an antenna analyzer when it is being used for SWR measurements? | 
 | A. | Receiver
 | B. | Transmitter
 | C. | Antenna and feed line
 | D. | All of these choices are correct
Amateur Radio Practices
Group G4B

## Slide 208
 | G4B12 ~ What problem can occur when making measurements on an antenna system with an antenna analyzer? | 
 |  | Permanent damage to the analyzer may occur if it is operated into a high SWR
 |  | Strong signals from nearby transmitters can affect the accuracy of measurements
 |  | The analyzer can be damaged if measurements outside the ham bands are attempted
 |  | Connecting the analyzer to an antenna can cause it to absorb harmonics
 | G4B12 ~ What problem can occur when making measurements on an antenna system with an antenna analyzer? | 
 |  | Permanent damage to the analyzer may occur if it is operated into a high SWR
 |  | The analyzer can be damaged if measurements outside the ham bands are attempted
 |  | Connecting the analyzer to an antenna can cause it to absorb harmonics
 | G4B12 ~ What problem can occur when making measurements on an antenna system with an antenna analyzer? | 
 | A. | Permanent damage to the analyzer may occur if it is operated into a high SWR
 | B. | Strong signals from nearby transmitters can affect the accuracy of measurements
 | C. | The analyzer can be damaged if measurements outside the ham bands are attempted
 | D. | Connecting the analyzer to an antenna can cause it to absorb harmonics
Amateur Radio Practices
Group G4B

## Slide 209
 | G4B13 ~ What is a use for an antenna analyzer other than measuring the SWR of an antenna system? | 
 |  | Measuring the front to back ratio of an antenna
 |  | Measuring the turns ratio of a power transformer
 |  | Determining the impedance of an unknown or unmarked coaxial cable
 |  | Determining the gain of a directional antenna
 | G4B13 ~ What is a use for an antenna analyzer other than measuring the SWR of an antenna system? | 
 |  | Measuring the front to back ratio of an antenna
 |  | Measuring the turns ratio of a power transformer
 |  | Determining the gain of a directional antenna
 | G4B13 ~ What is a use for an antenna analyzer other than measuring the SWR of an antenna system? | 
 | A. | Measuring the front to back ratio of an antenna
 | B. | Measuring the turns ratio of a power transformer
 | C. | Determining the impedance of an unknown or unmarked coaxial cable
 | D. | Determining the gain of a directional antenna
Amateur Radio Practices
Group G4B

## Slide 210
 | G4B14 ~ What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout? | 
 |  | When testing logic circuits
 |  | When high precision is desired
 |  | When measuring the frequency of an oscillator
 |  | When adjusting tuned circuits
 | G4B14 ~ What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout? | 
 |  | When testing logic circuits
 |  | When high precision is desired
 |  | When measuring the frequency of an oscillator
 | G4B14 ~ What is an instance in which the use of an instrument with analog readout may be preferred over an instrument with a digital readout? | 
 | A. | When testing logic circuits
 | B. | When high precision is desired
 | C. | When measuring the frequency of an oscillator
 | D. | When adjusting tuned circuits
Amateur Radio Practices
Group G4B

## Slide 211
 | G4B15 ~ What type of transmitter performance does a two-tone test analyze? | 
 |  | Linearity
 |  | Percentage of suppression of carrier and undesired sideband for SSB
 |  | Percentage of frequency modulation
 |  | Percentage of carrier phase shift
 | G4B15 ~ What type of transmitter performance does a two-tone test analyze? | 
 |  | Percentage of suppression of carrier and undesired sideband for SSB
 |  | Percentage of frequency modulation
 |  | Percentage of carrier phase shift
 | G4B15 ~ What type of transmitter performance does a two-tone test analyze? | 
 | A. | Linearity
 | B. | Percentage of suppression of carrier and undesired sideband for SSB
 | C. | Percentage of frequency modulation
 | D. | Percentage of carrier phase shift
Amateur Radio Practices
Group G4B

## Slide 212
G4C01
G4C02
G4C03
G4C04
G4C05
G4C06
G4C07
G4C08
G4C09
G4C10
G4C11
G4C12
G4C13
Amateur Radio Practices
Group G4C (13 Questions)
Interference with consumer electronics; grounding; DSP
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 213
 | G4C01 ~ Which of the following might be useful in reducing RF interference to audio frequency devices? | 
 |  | Bypass inductor
 |  | Bypass capacitor
 |  | Forward-biased diode
 |  | Reverse-biased diode
 | G4C01 ~ Which of the following might be useful in reducing RF interference to audio frequency devices? | 
 |  | Bypass inductor
 |  | Forward-biased diode
 |  | Reverse-biased diode
 | G4C01 ~ Which of the following might be useful in reducing RF interference to audio frequency devices? | 
 | A. | Bypass inductor
 | B. | Bypass capacitor
 | C. | Forward-biased diode
 | D. | Reverse-biased diode
Amateur Radio Practices
Group G4C

## Slide 214
 | G4C02 ~ Which of the following could be a cause of interference covering a wide range of frequencies? | 
 |  | Not using a balun or line isolator to feed balanced antennas
 |  | Lack of rectification of the transmitter's signal in power conductors
 |  | Arcing at a poor electrical connection
 |  | Using a balun to feed an unbalanced antenna
 | G4C02 ~ Which of the following could be a cause of interference covering a wide range of frequencies? | 
 |  | Not using a balun or line isolator to feed balanced antennas
 |  | Lack of rectification of the transmitter's signal in power conductors
 |  | Using a balun to feed an unbalanced antenna
 | G4C02 ~ Which of the following could be a cause of interference covering a wide range of frequencies? | 
 | A. | Not using a balun or line isolator to feed balanced antennas
 | B. | Lack of rectification of the transmitter's signal in power conductors
 | C. | Arcing at a poor electrical connection
 | D. | Using a balun to feed an unbalanced antenna
Amateur Radio Practices
Group G4C

## Slide 215
 | G4C03 ~ What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter? | 
 |  | A steady hum whenever the transmitter is on the air
 |  | On-and-off humming or clicking
 |  | Distorted speech
 |  | Clearly audible speech
 | G4C03 ~ What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter? | 
 |  | A steady hum whenever the transmitter is on the air
 |  | On-and-off humming or clicking
 |  | Clearly audible speech
 | G4C03 ~ What sound is heard from an audio device or telephone if there is interference from a nearby single sideband phone transmitter? | 
 | A. | A steady hum whenever the transmitter is on the air
 | B. | On-and-off humming or clicking
 | C. | Distorted speech
 | D. | Clearly audible speech
Amateur Radio Practices
Group G4C

## Slide 216
 | G4C04 ~ What is the effect on an audio device or telephone system if there is interference from a nearby CW transmitter? | 
 |  | On-and-off humming or clicking
 |  | A CW signal at a nearly pure audio frequency
 |  | A chirpy CW signal
 |  | Severely distorted audio
 | G4C04 ~ What is the effect on an audio device or telephone system if there is interference from a nearby CW transmitter? | 
 |  | A CW signal at a nearly pure audio frequency
 |  | A chirpy CW signal
 |  | Severely distorted audio
 | G4C04 ~ What is the effect on an audio device or telephone system if there is interference from a nearby CW transmitter? | 
 | A. | On-and-off humming or clicking
 | B. | A CW signal at a nearly pure audio frequency
 | C. | A chirpy CW signal
 | D. | Severely distorted audio
Amateur Radio Practices
Group G4C

## Slide 217
 | G4C05 ~ What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod? | 
 |  | Flat braid rather than round wire has been used for the ground wire
 |  | Insulated wire has been used for the ground wire
 |  | The ground rod is resonant
 |  | The ground wire has high impedance on that frequency
 | G4C05 ~ What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod? | 
 |  | Flat braid rather than round wire has been used for the ground wire
 |  | Insulated wire has been used for the ground wire
 |  | The ground rod is resonant
 | G4C05 ~ What might be the problem if you receive an RF burn when touching your equipment while transmitting on an HF band, assuming the equipment is connected to a ground rod? | 
 | A. | Flat braid rather than round wire has been used for the ground wire
 | B. | Insulated wire has been used for the ground wire
 | C. | The ground rod is resonant
 | D. | The ground wire has high impedance on that frequency
Amateur Radio Practices
Group G4C

## Slide 218
 | G4C06 ~ What effect can be caused by a resonant ground connection? | 
 |  | Overheating of ground straps
 |  | Corrosion of the ground rod
 |  | High RF voltages on the enclosures of station equipment
 |  | A ground loop
 | G4C06 ~ What effect can be caused by a resonant ground connection? | 
 |  | Overheating of ground straps
 |  | Corrosion of the ground rod
 |  | A ground loop
 | G4C06 ~ What effect can be caused by a resonant ground connection? | 
 | A. | Overheating of ground straps
 | B. | Corrosion of the ground rod
 | C. | High RF voltages on the enclosures of station equipment
 | D. | A ground loop
Amateur Radio Practices
Group G4C

## Slide 219
 | G4C07 ~ What is one good way to avoid unwanted effects of stray RF energy in an amateur station? | 
 |  | Connect all equipment grounds together
 |  | Install an RF filter in series with the ground wire
 |  | Use a ground loop for best conductivity
 |  | Install a few ferrite beads on the ground wire where it connects to your station
 | G4C07 ~ What is one good way to avoid unwanted effects of stray RF energy in an amateur station? | 
 |  | Install an RF filter in series with the ground wire
 |  | Use a ground loop for best conductivity
 |  | Install a few ferrite beads on the ground wire where it connects to your station
 | G4C07 ~ What is one good way to avoid unwanted effects of stray RF energy in an amateur station? | 
 | A. | Connect all equipment grounds together
 | B. | Install an RF filter in series with the ground wire
 | C. | Use a ground loop for best conductivity
 | D. | Install a few ferrite beads on the ground wire where it connects to your station
Amateur Radio Practices
Group G4C

## Slide 220
 | G4C08 ~ Which of the following would reduce RF interference caused by common-mode current on an audio cable? | 
 |  | Placing a ferrite choke around the cable
 |  | Adding series capacitors to the conductors
 |  | Adding shunt inductors to the conductors
 |  | Adding an additional insulating jacket to the cable
 | G4C08 ~ Which of the following would reduce RF interference caused by common-mode current on an audio cable? | 
 |  | Adding series capacitors to the conductors
 |  | Adding shunt inductors to the conductors
 |  | Adding an additional insulating jacket to the cable
 | G4C08 ~ Which of the following would reduce RF interference caused by common-mode current on an audio cable? | 
 | A. | Placing a ferrite choke around the cable
 | B. | Adding series capacitors to the conductors
 | C. | Adding shunt inductors to the conductors
 | D. | Adding an additional insulating jacket to the cable
Amateur Radio Practices
Group G4C

## Slide 221
 | G4C09 ~ How can a ground loop be avoided? | 
 |  | Connect all ground conductors in series
 |  | Connect the AC neutral conductor to the ground wire
 |  | Avoid using lock washers and star washers when making ground connections
 |  | Connect all ground conductors to a single point
 | G4C09 ~ How can a ground loop be avoided? | 
 |  | Connect all ground conductors in series
 |  | Connect the AC neutral conductor to the ground wire
 |  | Avoid using lock washers and star washers when making ground connections
 | G4C09 ~ How can a ground loop be avoided? | 
 | A. | Connect all ground conductors in series
 | B. | Connect the AC neutral conductor to the ground wire
 | C. | Avoid using lock washers and star washers when making ground connections
 | D. | Connect all ground conductors to a single point
Amateur Radio Practices
Group G4C

## Slide 222
 | G4C10 ~ What could be a symptom of a ground loop somewhere in your station? | 
 |  | You receive reports of "hum" on your station's transmitted signal
 |  | The SWR reading for one or more antennas is suddenly very high
 |  | An item of station equipment starts to draw excessive amounts of current
 |  | You receive reports of harmonic interference from your station
 | G4C10 ~ What could be a symptom of a ground loop somewhere in your station? | 
 |  | The SWR reading for one or more antennas is suddenly very high
 |  | An item of station equipment starts to draw excessive amounts of current
 |  | You receive reports of harmonic interference from your station
 | G4C10 ~ What could be a symptom of a ground loop somewhere in your station? | 
 | A. | You receive reports of "hum" on your station's transmitted signal
 | B. | The SWR reading for one or more antennas is suddenly very high
 | C. | An item of station equipment starts to draw excessive amounts of current
 | D. | You receive reports of harmonic interference from your station
Amateur Radio Practices
Group G4C

## Slide 223
 | G4C11 ~ Which of the following is a function of a digital signal processor? | 
 |  | To provide adequate grounding
 |  | To remove noise from received signals
 |  | To increase antenna gain
 |  | To increase antenna bandwidth
 | G4C11 ~ Which of the following is a function of a digital signal processor? | 
 |  | To provide adequate grounding
 |  | To increase antenna gain
 |  | To increase antenna bandwidth
 | G4C11 ~ Which of the following is a function of a digital signal processor? | 
 | A. | To provide adequate grounding
 | B. | To remove noise from received signals
 | C. | To increase antenna gain
 | D. | To increase antenna bandwidth
Amateur Radio Practices
Group G4C

## Slide 224
 | G4C12 ~ Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter? | 
 |  | A wide range of filter bandwidths and shapes can be created
 |  | Fewer digital components are required
 |  | Mixing products are greatly reduced
 |  | The DSP filter is much more effective at VHF frequencies
 | G4C12 ~ Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter? | 
 |  | Fewer digital components are required
 |  | Mixing products are greatly reduced
 |  | The DSP filter is much more effective at VHF frequencies
 | G4C12 ~ Which of the following is an advantage of a receiver DSP IF filter as compared to an analog filter? | 
 | A. | A wide range of filter bandwidths and shapes can be created
 | B. | Fewer digital components are required
 | C. | Mixing products are greatly reduced
 | D. | The DSP filter is much more effective at VHF frequencies
Amateur Radio Practices
Group G4C

## Slide 225
 | G4C13 ~ Which of the following can perform automatic notching of interfering carriers? | 
 |  | Bandpass tuning
 |  | A Digital Signal Processor (DSP) filter
 |  | Balanced mixing
 |  | A noise limiter
 | G4C13 ~ Which of the following can perform automatic notching of interfering carriers? | 
 |  | Bandpass tuning
 |  | Balanced mixing
 |  | A noise limiter
 | G4C13 ~ Which of the following can perform automatic notching of interfering carriers? | 
 | A. | Bandpass tuning
 | B. | A Digital Signal Processor (DSP) filter
 | C. | Balanced mixing
 | D. | A noise limiter
Amateur Radio Practices
Group G4C

## Slide 226
G4D01
G4D02
G4D03
G4D04
G4D05
G4D06
G4D07
G4D08
G4D09
G4D10
G4D11
Amateur Radio Practices
Group G4D (11 Questions)
Speech processors; S meters; sideband operation near band edges
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 227
 | G4D01 ~ What is the purpose of a speech processor as used in a modern transceiver? | 
 |  | Increase the intelligibility of transmitted phone signals during poor conditions
 |  | Increase transmitter bass response for more natural sounding SSB signals
 |  | Prevent distortion of voice signals
 |  | Decrease high-frequency voice output to prevent out of band operation
 | G4D01 ~ What is the purpose of a speech processor as used in a modern transceiver? | 
 |  | Increase transmitter bass response for more natural sounding SSB signals
 |  | Prevent distortion of voice signals
 |  | Decrease high-frequency voice output to prevent out of band operation
 | G4D01 ~ What is the purpose of a speech processor as used in a modern transceiver? | 
 | A. | Increase the intelligibility of transmitted phone signals during poor conditions
 | B. | Increase transmitter bass response for more natural sounding SSB signals
 | C. | Prevent distortion of voice signals
 | D. | Decrease high-frequency voice output to prevent out of band operation
Amateur Radio Practices
Group G4D

## Slide 228
 | G4D02 ~ Which of the following describes how a speech processor affects a transmitted single sideband phone signal? | 
 |  | It increases peak power
 |  | It increases average power
 |  | It reduces harmonic distortion
 |  | It reduces intermodulation distortion
 | G4D02 ~ Which of the following describes how a speech processor affects a transmitted single sideband phone signal? | 
 |  | It increases peak power
 |  | It reduces harmonic distortion
 |  | It reduces intermodulation distortion
 | G4D02 ~ Which of the following describes how a speech processor affects a transmitted single sideband phone signal? | 
 | A. | It increases peak power
 | B. | It increases average power
 | C. | It reduces harmonic distortion
 | D. | It reduces intermodulation distortion
Amateur Radio Practices
Group G4D

## Slide 229
 | G4D03 ~ Which of the following can be the result of an incorrectly adjusted speech processor? | 
 |  | Distorted speech
 |  | Splatter
 |  | Excessive background pickup
 |  | All of these choices are correct
 | G4D03 ~ Which of the following can be the result of an incorrectly adjusted speech processor? | 
 |  | Distorted speech
 |  | Splatter
 |  | Excessive background pickup
 | G4D03 ~ Which of the following can be the result of an incorrectly adjusted speech processor? | 
 | A. | Distorted speech
 | B. | Splatter
 | C. | Excessive background pickup
 | D. | All of these choices are correct
Amateur Radio Practices
Group G4D

## Slide 230
 | G4D04 ~ What does an S meter measure? | 
 |  | Conductance
 |  | Impedance
 |  | Received signal strength
 |  | Transmitter power output
 | G4D04 ~ What does an S meter measure? | 
 |  | Conductance
 |  | Impedance
 |  | Transmitter power output
 | G4D04 ~ What does an S meter measure? | 
 | A. | Conductance
 | B. | Impedance
 | C. | Received signal strength
 | D. | Transmitter power output
Amateur Radio Practices
Group G4D

## Slide 231
 | G4D05 ~ How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter? | 
 |  | It is 10 times less powerful
 |  | It is 20 times less powerful
 |  | It is 20 times more powerful
 |  | It is 100 times more powerful
 | G4D05 ~ How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter? | 
 |  | It is 10 times less powerful
 |  | It is 20 times less powerful
 |  | It is 20 times more powerful
 | G4D05 ~ How does a signal that reads 20 dB over S9 compare to one that reads S9 on a receiver, assuming a properly calibrated S meter? | 
 | A. | It is 10 times less powerful
 | B. | It is 20 times less powerful
 | C. | It is 20 times more powerful
 | D. | It is 100 times more powerful
Amateur Radio Practices
Group G4D

## Slide 232
 | G4D06 ~ Where is an S meter found? | 
 |  | In a receiver
 |  | In an SWR bridge
 |  | In a transmitter
 |  | In a conductance bridge
 | G4D06 ~ Where is an S meter found? | 
 |  | In an SWR bridge
 |  | In a transmitter
 |  | In a conductance bridge
 | G4D06 ~ Where is an S meter found? | 
 | A. | In a receiver
 | B. | In an SWR bridge
 | C. | In a transmitter
 | D. | In a conductance bridge
Amateur Radio Practices
Group G4D

## Slide 233
 | G4D07 ~ How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9? | 
 |  | Approximately 1.5 times
 |  | Approximately 2 times
 |  | Approximately 4 times
 |  | Approximately 8 times
 | G4D07 ~ How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9? | 
 |  | Approximately 1.5 times
 |  | Approximately 2 times
 |  | Approximately 8 times
 | G4D07 ~ How much must the power output of a transmitter be raised to change the S meter reading on a distant receiver from S8 to S9? | 
 | A. | Approximately 1.5 times
 | B. | Approximately 2 times
 | C. | Approximately 4 times
 | D. | Approximately 8 times
Amateur Radio Practices
Group G4D

## Slide 234
 | G4D08 ~ What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz? | 
 |  | 7.178 to 7.181 MHz
 |  | 7.178 to 7.184 MHz
 |  | 7.175 to 7.178 MHz
 |  | 7.1765 to 7.1795 MHz
 | G4D08 ~ What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz? | 
 |  | 7.178 to 7.181 MHz
 |  | 7.178 to 7.184 MHz
 |  | 7.1765 to 7.1795 MHz
 | G4D08 ~ What frequency range is occupied by a 3 kHz LSB signal when the displayed carrier frequency is set to 7.178 MHz? | 
 | A. | 7.178 to 7.181 MHz
 | B. | 7.178 to 7.184 MHz
 | C. | 7.175 to 7.178 MHz
 | D. | 7.1765 to 7.1795 MHz
Amateur Radio Practices
Group G4D

## Slide 235
 | G4D09 ~ What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz? | 
 |  | 14.347 to 14.647 MHz
 |  | 14.347 to 14.350 MHz
 |  | 14.344 to 14.347 MHz
 |  | 14.3455 to 14.3485 MHz
 | G4D09 ~ What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz? | 
 |  | 14.347 to 14.647 MHz
 |  | 14.344 to 14.347 MHz
 |  | 14.3455 to 14.3485 MHz
 | G4D09 ~ What frequency range is occupied by a 3 kHz USB signal with the displayed carrier frequency set to 14.347 MHz? | 
 | A. | 14.347 to 14.647 MHz
 | B. | 14.347 to 14.350 MHz
 | C. | 14.344 to 14.347 MHz
 | D. | 14.3455 to 14.3485 MHz
Amateur Radio Practices
Group G4D

## Slide 236
 | G4D10 ~ How close to the lower edge of the 40-meter General Class phone segment should your displayed carrier frequency be when using 3 kHz wide LSB? | 
 |  | At least 3 kHz above the edge of the segment
 |  | At least 3 kHz below the edge of the segment
 |  | Your displayed carrier frequency may be set at the edge of the segment
 |  | At least 1 kHz above the edge of the segment
 | G4D10 ~ How close to the lower edge of the 40-meter General Class phone segment should your displayed carrier frequency be when using 3 kHz wide LSB? | 
 |  | At least 3 kHz below the edge of the segment
 |  | Your displayed carrier frequency may be set at the edge of the segment
 |  | At least 1 kHz above the edge of the segment
 | G4D10 ~ How close to the lower edge of the 40-meter General Class phone segment should your displayed carrier frequency be when using 3 kHz wide LSB? | 
 | A. | At least 3 kHz above the edge of the segment
 | B. | At least 3 kHz below the edge of the segment
 | C. | Your displayed carrier frequency may be set at the edge of the segment
 | D. | At least 1 kHz above the edge of the segment
Amateur Radio Practices
Group G4D

## Slide 237
 | G4D11 ~ How close to the upper edge of the 20-meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB? | 
 |  | At least 3 kHz above the edge of the band
 |  | At least 3 kHz below the edge of the band
 |  | Your displayed carrier frequency may be set at the edge of the band
 |  | At least 1 kHz below the edge of the segment
 | G4D11 ~ How close to the upper edge of the 20-meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB? | 
 |  | At least 3 kHz above the edge of the band
 |  | Your displayed carrier frequency may be set at the edge of the band
 |  | At least 1 kHz below the edge of the segment
 | G4D11 ~ How close to the upper edge of the 20-meter General Class band should your displayed carrier frequency be when using 3 kHz wide USB? | 
 | A. | At least 3 kHz above the edge of the band
 | B. | At least 3 kHz below the edge of the band
 | C. | Your displayed carrier frequency may be set at the edge of the band
 | D. | At least 1 kHz below the edge of the segment
Amateur Radio Practices
Group G4D

## Slide 238
G4E01
G4E02
G4E03
G4E04
G4E05
G4E06
G4E07
G4E08
G4E09
G4E10
G4E11
Amateur Radio Practices
Group G4E (11 Questions)
HF mobile radio installations; emergency and battery powered operation
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 239
 | G4E01 ~ What is the purpose of a capacitance hat on a mobile antenna? | 
 |  | To increase the power handling capacity of a whip antenna
 |  | To allow automatic band changing
 |  | To electrically lengthen a physically short antenna
 |  | To allow remote tuning
 | G4E01 ~ What is the purpose of a capacitance hat on a mobile antenna? | 
 |  | To increase the power handling capacity of a whip antenna
 |  | To allow automatic band changing
 |  | To allow remote tuning
 | G4E01 ~ What is the purpose of a capacitance hat on a mobile antenna? | 
 | A. | To increase the power handling capacity of a whip antenna
 | B. | To allow automatic band changing
 | C. | To electrically lengthen a physically short antenna
 | D. | To allow remote tuning
Amateur Radio Practices
Group G4E

## Slide 240
 | G4E02 ~ What is the purpose of a corona ball on a HF mobile antenna? | 
 |  | To narrow the operating bandwidth of the antenna
 |  | To increase the "Q" of the antenna
 |  | To reduce the chance of damage if the antenna should strike an object
 |  | To reduce high voltage discharge from the tip of the antenna
 | G4E02 ~ What is the purpose of a corona ball on a HF mobile antenna? | 
 |  | To narrow the operating bandwidth of the antenna
 |  | To increase the "Q" of the antenna
 |  | To reduce the chance of damage if the antenna should strike an object
 | G4E02 ~ What is the purpose of a corona ball on a HF mobile antenna? | 
 | A. | To narrow the operating bandwidth of the antenna
 | B. | To increase the "Q" of the antenna
 | C. | To reduce the chance of damage if the antenna should strike an object
 | D. | To reduce high voltage discharge from the tip of the antenna
Amateur Radio Practices
Group G4E

## Slide 241
 | G4E03 ~ Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation? | 
 |  | To the battery using heavy gauge wire
 |  | To the alternator or generator using heavy gauge wire
 |  | To the battery using resistor wire
 |  | To the alternator or generator using resistor wire
 | G4E03 ~ Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation? | 
 |  | To the alternator or generator using heavy gauge wire
 |  | To the battery using resistor wire
 |  | To the alternator or generator using resistor wire
 | G4E03 ~ Which of the following direct, fused power connections would be the best for a 100 watt HF mobile installation? | 
 | A. | To the battery using heavy gauge wire
 | B. | To the alternator or generator using heavy gauge wire
 | C. | To the battery using resistor wire
 | D. | To the alternator or generator using resistor wire
Amateur Radio Practices
Group G4E

## Slide 242
 | G4E04 ~ Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle's auxiliary power socket? | 
 |  | The socket is not wired with an RF-shielded power cable
 |  | The socket's wiring may be inadequate for the current drawn by the transceiver
 |  | The DC polarity of the socket is reversed from the polarity of modern HF transceivers
 |  | Drawing more than 50 watts from this socket could cause the engine to overheat
 | G4E04 ~ Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle's auxiliary power socket? | 
 |  | The socket is not wired with an RF-shielded power cable
 |  | The DC polarity of the socket is reversed from the polarity of modern HF transceivers
 |  | Drawing more than 50 watts from this socket could cause the engine to overheat
 | G4E04 ~ Why is it best NOT to draw the DC power for a 100 watt HF transceiver from a vehicle's auxiliary power socket? | 
 | A. | The socket is not wired with an RF-shielded power cable
 | B. | The socket's wiring may be inadequate for the current drawn by the transceiver
 | C. | The DC polarity of the socket is reversed from the polarity of modern HF transceivers
 | D. | Drawing more than 50 watts from this socket could cause the engine to overheat
Amateur Radio Practices
Group G4E

## Slide 243
 | G4E05 ~ Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band? | 
 |  | "Picket Fencing" signal variation
 |  | The wire gauge of the DC power line to the transceiver
 |  | The antenna system
 |  | FCC rules limiting mobile output power on the 75-meter band
 | G4E05 ~ Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band? | 
 |  | "Picket Fencing" signal variation
 |  | The wire gauge of the DC power line to the transceiver
 |  | FCC rules limiting mobile output power on the 75-meter band
 | G4E05 ~ Which of the following most limits the effectiveness of an HF mobile transceiver operating in the 75-meter band? | 
 | A. | "Picket Fencing" signal variation
 | B. | The wire gauge of the DC power line to the transceiver
 | C. | The antenna system
 | D. | FCC rules limiting mobile output power on the 75-meter band
Amateur Radio Practices
Group G4E

## Slide 244
 | G4E06 ~ What is one disadvantage of using a shortened mobile antenna as opposed to a full size antenna? | 
 |  | Short antennas are more likely to cause distortion of transmitted signals
 |  | Short antennas can only receive circularly polarized signals
 |  | Operating bandwidth may be very limited
 |  | Harmonic radiation may increase
 | G4E06 ~ What is one disadvantage of using a shortened mobile antenna as opposed to a full size antenna? | 
 |  | Short antennas are more likely to cause distortion of transmitted signals
 |  | Short antennas can only receive circularly polarized signals
 |  | Harmonic radiation may increase
 | G4E06 ~ What is one disadvantage of using a shortened mobile antenna as opposed to a full size antenna? | 
 | A. | Short antennas are more likely to cause distortion of transmitted signals
 | B. | Short antennas can only receive circularly polarized signals
 | C. | Operating bandwidth may be very limited
 | D. | Harmonic radiation may increase
Amateur Radio Practices
Group G4E

## Slide 245
 | G4E07 ~ Which of the following may cause interference to be heard in the receiver of an HF radio installed in a recent model vehicle? | 
 |  | The battery charging system
 |  | The fuel delivery system
 |  | The vehicle control computer
 |  | All of these choices are correct
 | G4E07 ~ Which of the following may cause interference to be heard in the receiver of an HF radio installed in a recent model vehicle? | 
 |  | The battery charging system
 |  | The fuel delivery system
 |  | The vehicle control computer
 | G4E07 ~ Which of the following may cause interference to be heard in the receiver of an HF radio installed in a recent model vehicle? | 
 | A. | The battery charging system
 | B. | The fuel delivery system
 | C. | The vehicle control computer
 | D. | All of these choices are correct
Amateur Radio Practices
Group G4E

## Slide 246
 | G4E08 ~ What is the name of the process by which sunlight is changed directly into electricity? | 
 |  | Photovoltaic conversion
 |  | Photon emission
 |  | Photosynthesis
 |  | Photon decomposition
 | G4E08 ~ What is the name of the process by which sunlight is changed directly into electricity? | 
 |  | Photon emission
 |  | Photosynthesis
 |  | Photon decomposition
 | G4E08 ~ What is the name of the process by which sunlight is changed directly into electricity? | 
 | A. | Photovoltaic conversion
 | B. | Photon emission
 | C. | Photosynthesis
 | D. | Photon decomposition
Amateur Radio Practices
Group G4E

## Slide 247
 | G4E09 ~ What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell? | 
 |  | 0.02 VDC
 |  | 0.5 VDC
 |  | 0.2 VDC
 |  | 1.38 VDC
 | G4E09 ~ What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell? | 
 |  | 0.02 VDC
 |  | 0.2 VDC
 |  | 1.38 VDC
 | G4E09 ~ What is the approximate open-circuit voltage from a fully illuminated silicon photovoltaic cell? | 
 | A. | 0.02 VDC
 | B. | 0.5 VDC
 | C. | 0.2 VDC
 | D. | 1.38 VDC
Amateur Radio Practices
Group G4E

## Slide 248
 | G4E10 ~ What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel? | 
 |  | The diode serves to regulate the charging voltage to prevent overcharge
 |  | The diode prevents self-discharge of the battery though the panel during times of low or no illumination
 |  | The diode limits the current flowing from the panel to a safe value
 |  | The diode greatly increases the efficiency during times of high illumination
 | G4E10 ~ What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel? | 
 |  | The diode serves to regulate the charging voltage to prevent overcharge
 |  | The diode limits the current flowing from the panel to a safe value
 |  | The diode greatly increases the efficiency during times of high illumination
 | G4E10 ~ What is the reason that a series diode is connected between a solar panel and a storage battery that is being charged by the panel? | 
 | A. | The diode serves to regulate the charging voltage to prevent overcharge
 | B. | The diode prevents self-discharge of the battery though the panel during times of low or no illumination
 | C. | The diode limits the current flowing from the panel to a safe value
 | D. | The diode greatly increases the efficiency during times of high illumination
Amateur Radio Practices
Group G4E

## Slide 249
 | G4E11 ~ Which of the following is a disadvantage of using wind as the primary source of power for an emergency station? | 
 |  | The conversion efficiency from mechanical energy to electrical energy is less than 2 percent
 |  | The voltage and current ratings of such systems are not compatible with amateur equipment
 |  | A large energy storage system is needed to supply power when the wind is not blowing
 |  | All of these choices are correct
 | G4E11 ~ Which of the following is a disadvantage of using wind as the primary source of power for an emergency station? | 
 |  | The conversion efficiency from mechanical energy to electrical energy is less than 2 percent
 |  | The voltage and current ratings of such systems are not compatible with amateur equipment
 |  | All of these choices are correct
 | G4E11 ~ Which of the following is a disadvantage of using wind as the primary source of power for an emergency station? | 
 | A. | The conversion efficiency from mechanical energy to electrical energy is less than 2 percent
 | B. | The voltage and current ratings of such systems are not compatible with amateur equipment
 | C. | A large energy storage system is needed to supply power when the wind is not blowing
 | D. | All of these choices are correct
Amateur Radio Practices
Group G4E

## Slide 250
Group |  | Questions
G5A | Reactance; inductance; capacitance; impedance; impedance matching | 13
G5B | The Decibel; current and voltage dividers; electrical power calculations; sine wave root-mean-square (RMS) values; PEP calculations | 13
G5C | Resistors, capacitors, and inductors in series and parallel; transformers | 18
3 | Total | 44
Subelement G5 Electrical Principles
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 251
G5A01
G5A02
G5A03
G5A04
G5A05
G5A06
G5A07
G5A08
G5A09
G5A10
G5A11
G5A12
G5A13
Electrical Principles
Group G5A (13 Questions)
Reactance; inductance; capacitance; impedance; impedance matching
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 252
 | G5A01 ~ What is impedance? | 
 |  | The electric charge stored by a capacitor
 |  | The inverse of resistance
 |  | The opposition to the flow of current in an AC circuit
 |  | The force of repulsion between two similar electric fields
 | G5A01 ~ What is impedance? | 
 |  | The electric charge stored by a capacitor
 |  | The inverse of resistance
 |  | The force of repulsion between two similar electric fields
 | G5A01 ~ What is impedance? | 
 | A. | The electric charge stored by a capacitor
 | B. | The inverse of resistance
 | C. | The opposition to the flow of current in an AC circuit
 | D. | The force of repulsion between two similar electric fields
Electrical Principles
Group G5A

## Slide 253
 | G5A02 ~ What is reactance? | 
 |  | Opposition to the flow of direct current caused by resistance
 |  | Opposition to the flow of alternating current caused by capacitance or inductance
 |  | A property of ideal resistors in AC circuits
 |  | A large spark produced at switch contacts when an inductor is
 | G5A02 ~ What is reactance? | 
 |  | Opposition to the flow of direct current caused by resistance
 |  | A property of ideal resistors in AC circuits
 |  | A large spark produced at switch contacts when an inductor is
 | G5A02 ~ What is reactance? | 
 | A. | Opposition to the flow of direct current caused by resistance
 | B. | Opposition to the flow of alternating current caused by capacitance or inductance
 | C. | A property of ideal resistors in AC circuits
 | D. | A large spark produced at switch contacts when an inductor is
Electrical Principles
Group G5A

## Slide 254
 | G5A03 ~ Which of the following causes opposition to the flow of alternating current in an inductor? | 
 |  | Conductance
 |  | Reluctance
 |  | Admittance
 |  | Reactance
 | G5A03 ~ Which of the following causes opposition to the flow of alternating current in an inductor? | 
 |  | Conductance
 |  | Reluctance
 |  | Admittance
 | G5A03 ~ Which of the following causes opposition to the flow of alternating current in an inductor? | 
 | A. | Conductance
 | B. | Reluctance
 | C. | Admittance
 | D. | Reactance
Electrical Principles
Group G5A

## Slide 255
 | G5A04 ~ Which of the following causes opposition to the flow of alternating current in a capacitor? | 
 |  | Conductance
 |  | Reluctance
 |  | Reactance
 |  | Admittance
 | G5A04 ~ Which of the following causes opposition to the flow of alternating current in a capacitor? | 
 |  | Conductance
 |  | Reluctance
 |  | Admittance
 | G5A04 ~ Which of the following causes opposition to the flow of alternating current in a capacitor? | 
 | A. | Conductance
 | B. | Reluctance
 | C. | Reactance
 | D. | Admittance
Electrical Principles
Group G5A

## Slide 256
 | G5A05 ~ How does an inductor react to AC? | 
 |  | As the frequency of the applied AC increases, the reactance decreases
 |  | As the amplitude of the applied AC increases, the reactance increases
 |  | As the amplitude of the applied AC increases, the reactance decreases
 |  | As the frequency of the applied AC increases, the reactance increases
 | G5A05 ~ How does an inductor react to AC? | 
 |  | As the frequency of the applied AC increases, the reactance decreases
 |  | As the amplitude of the applied AC increases, the reactance increases
 |  | As the amplitude of the applied AC increases, the reactance decreases
 | G5A05 ~ How does an inductor react to AC? | 
 | A. | As the frequency of the applied AC increases, the reactance decreases
 | B. | As the amplitude of the applied AC increases, the reactance increases
 | C. | As the amplitude of the applied AC increases, the reactance decreases
 | D. | As the frequency of the applied AC increases, the reactance increases
Electrical Principles
Group G5A

## Slide 257
 | G5A06 ~ How does a capacitor react to AC? | 
 |  | As the frequency of the applied AC increases, the reactance decreases
 |  | As the frequency of the applied AC increases, the reactance increases
 |  | As the amplitude of the applied AC increases, the reactance increases
 |  | As the amplitude of the applied AC increases, the reactance decreases
 | G5A06 ~ How does a capacitor react to AC? | 
 |  | As the frequency of the applied AC increases, the reactance increases
 |  | As the amplitude of the applied AC increases, the reactance increases
 |  | As the amplitude of the applied AC increases, the reactance decreases
 | G5A06 ~ How does a capacitor react to AC? | 
 | A. | As the frequency of the applied AC increases, the reactance decreases
 | B. | As the frequency of the applied AC increases, the reactance increases
 | C. | As the amplitude of the applied AC increases, the reactance increases
 | D. | As the amplitude of the applied AC increases, the reactance decreases
Electrical Principles
Group G5A

## Slide 258
 | G5A07 ~ What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive? | 
 |  | The source delivers minimum power to the load
 |  | The electrical load is shorted
 |  | No current can flow through the circuit
 |  | The source can deliver maximum power to the load
 | G5A07 ~ What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive? | 
 |  | The source delivers minimum power to the load
 |  | The electrical load is shorted
 |  | No current can flow through the circuit
 | G5A07 ~ What happens when the impedance of an electrical load is equal to the output impedance of a power source, assuming both impedances are resistive? | 
 | A. | The source delivers minimum power to the load
 | B. | The electrical load is shorted
 | C. | No current can flow through the circuit
 | D. | The source can deliver maximum power to the load
Electrical Principles
Group G5A

## Slide 259
 | G5A08 ~ Why is impedance matching important? | 
 |  | So the source can deliver maximum power to the load
 |  | So the load will draw minimum power from the source
 |  | To ensure that there is less resistance than reactance in the circuit
 |  | To ensure that the resistance and reactance in the circuit are equal
 | G5A08 ~ Why is impedance matching important? | 
 |  | So the load will draw minimum power from the source
 |  | To ensure that there is less resistance than reactance in the circuit
 |  | To ensure that the resistance and reactance in the circuit are equal
 | G5A08 ~ Why is impedance matching important? | 
 | A. | So the source can deliver maximum power to the load
 | B. | So the load will draw minimum power from the source
 | C. | To ensure that there is less resistance than reactance in the circuit
 | D. | To ensure that the resistance and reactance in the circuit are equal
Electrical Principles
Group G5A

## Slide 260
 | G5A09 ~ What unit is used to measure reactance? | 
 |  | Farad
 |  | Ohm
 |  | Ampere
 |  | Siemens
 | G5A09 ~ What unit is used to measure reactance? | 
 |  | Farad
 |  | Ampere
 |  | Siemens
 | G5A09 ~ What unit is used to measure reactance? | 
 | A. | Farad
 | B. | Ohm
 | C. | Ampere
 | D. | Siemens
Electrical Principles
Group G5A

## Slide 261
 | G5A10 ~ What unit is used to measure impedance? | 
 |  | Volt
 |  | Ohm
 |  | Ampere
 |  | Watt
 | G5A10 ~ What unit is used to measure impedance? | 
 |  | Volt
 |  | Ampere
 |  | Watt
 | G5A10 ~ What unit is used to measure impedance? | 
 | A. | Volt
 | B. | Ohm
 | C. | Ampere
 | D. | Watt
Electrical Principles
Group G5A

## Slide 262
 | G5A11 ~ Which of the following describes one method of impedance matching between two AC circuits? | 
 |  | Insert an LC network between the two circuits
 |  | Reduce the power output of the first circuit
 |  | Increase the power output of the first circuit
 |  | Insert a circulator between the two circuits
 | G5A11 ~ Which of the following describes one method of impedance matching between two AC circuits? | 
 |  | Reduce the power output of the first circuit
 |  | Increase the power output of the first circuit
 |  | Insert a circulator between the two circuits
 | G5A11 ~ Which of the following describes one method of impedance matching between two AC circuits? | 
 | A. | Insert an LC network between the two circuits
 | B. | Reduce the power output of the first circuit
 | C. | Increase the power output of the first circuit
 | D. | Insert a circulator between the two circuits
Electrical Principles
Group G5A

## Slide 263
 | G5A12 ~ What is one reason to use an impedance matching transformer? | 
 |  | To minimize transmitter power output
 |  | To maximize the transfer of power
 |  | To reduce power supply ripple
 |  | To minimize radiation resistance
 | G5A12 ~ What is one reason to use an impedance matching transformer? | 
 |  | To minimize transmitter power output
 |  | To reduce power supply ripple
 |  | To minimize radiation resistance
 | G5A12 ~ What is one reason to use an impedance matching transformer? | 
 | A. | To minimize transmitter power output
 | B. | To maximize the transfer of power
 | C. | To reduce power supply ripple
 | D. | To minimize radiation resistance
Electrical Principles
Group G5A

## Slide 264
 | G5A13 ~ Which of the following devices can be used for impedance matching at radio frequencies? | 
 |  | A transformer
 |  | A Pi-network
 |  | A length of transmission line
 |  | All of these choices are correct
 | G5A13 ~ Which of the following devices can be used for impedance matching at radio frequencies? | 
 |  | A transformer
 |  | A Pi-network
 |  | A length of transmission line
 | G5A13 ~ Which of the following devices can be used for impedance matching at radio frequencies? | 
 | A. | A transformer
 | B. | A Pi-network
 | C. | A length of transmission line
 | D. | All of these choices are correct
Electrical Principles
Group G5A

## Slide 265
G5B01
G5B02
G5B03
G5B04
G5B05
G5B06
G5B07
G5B09
G5B10
G5B11
G5B12
G5B13
G5B14
Electrical Principles
Group G5B (13 Questions)
The Decibel; current and voltage dividers; electrical power calculations; sine wave root-mean-square (RMS) values; PEP calculations
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 266
 | G5B01 ~ What dB change represents a two-times increase or decrease in power? | 
 |  | Approximately 2 dB
 |  | Approximately 3 dB
 |  | Approximately 6 dB
 |  | Approximately 12 dB
 | G5B01 ~ What dB change represents a two-times increase or decrease in power? | 
 |  | Approximately 2 dB
 |  | Approximately 6 dB
 |  | Approximately 12 dB
 | G5B01 ~ What dB change represents a two-times increase or decrease in power? | 
 | A. | Approximately 2 dB
 | B. | Approximately 3 dB
 | C. | Approximately 6 dB
 | D. | Approximately 12 dB
Electrical Principles
Group G5B

## Slide 267
 | G5B02 ~ How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit? | 
 |  | It equals the average of each branch current
 |  | It decreases as more parallel branches are added to the circuit
 |  | It equals the sum of the currents through each branch
 |  | It is the sum of the reciprocal of each individual voltage drop
 | G5B02 ~ How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit? | 
 |  | It equals the average of each branch current
 |  | It decreases as more parallel branches are added to the circuit
 |  | It is the sum of the reciprocal of each individual voltage drop
 | G5B02 ~ How does the total current relate to the individual currents in each branch of a purely resistive parallel circuit? | 
 | A. | It equals the average of each branch current
 | B. | It decreases as more parallel branches are added to the circuit
 | C. | It equals the sum of the currents through each branch
 | D. | It is the sum of the reciprocal of each individual voltage drop
Electrical Principles
Group G5B

## Slide 268
 | G5B03 ~ How many watts of electrical power are used if 400 VDC is supplied to an 800 ohm load? | 
 |  | 0.5 watts
 |  | 200 watts
 |  | 400 watts
 |  | 3200 watts
 | G5B03 ~ How many watts of electrical power are used if 400 VDC is supplied to an 800 ohm load? | 
 |  | 0.5 watts
 |  | 400 watts
 |  | 3200 watts
 | G5B03 ~ How many watts of electrical power are used if 400 VDC is supplied to an 800 ohm load? | 
 | A. | 0.5 watts
 | B. | 200 watts
 | C. | 400 watts
 | D. | 3200 watts
Electrical Principles
Group G5B

## Slide 269
 | G5B04 ~ How many watts of electrical power are used by a 12 VDC light bulb that draws 0.2 amperes? | 
 |  | 2.4 watts
 |  | 24 watts
 |  | 6 watts
 |  | 60 watts
 | G5B04 ~ How many watts of electrical power are used by a 12 VDC light bulb that draws 0.2 amperes? | 
 |  | 24 watts
 |  | 6 watts
 |  | 60 watts
 | G5B04 ~ How many watts of electrical power are used by a 12 VDC light bulb that draws 0.2 amperes? | 
 | A. | 2.4 watts
 | B. | 24 watts
 | C. | 6 watts
 | D. | 60 watts
Electrical Principles
Group G5B

## Slide 270
 | G5B05 ~ How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms resistance? | 
 |  | Approximately 61 milliwatts
 |  | Approximately 61 watts
 |  | Approximately 11 milliwatts
 |  | Approximately 11 watts
 | G5B05 ~ How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms resistance? | 
 |  | Approximately 61 watts
 |  | Approximately 11 milliwatts
 |  | Approximately 11 watts
 | G5B05 ~ How many watts are dissipated when a current of 7.0 milliamperes flows through 1.25 kilohms resistance? | 
 | A. | Approximately 61 milliwatts
 | B. | Approximately 61 watts
 | C. | Approximately 11 milliwatts
 | D. | Approximately 11 watts
Electrical Principles
Group G5B

## Slide 271
 | G5B06 ~ What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output? | 
 |  | 1.4 watts
 |  | 100 watts
 |  | 353.5 watts
 |  | 400 watts
 | G5B06 ~ What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output? | 
 |  | 1.4 watts
 |  | 353.5 watts
 |  | 400 watts
 | G5B06 ~ What is the output PEP from a transmitter if an oscilloscope measures 200 volts peak-to-peak across a 50 ohm dummy load connected to the transmitter output? | 
 | A. | 1.4 watts
 | B. | 100 watts
 | C. | 353.5 watts
 | D. | 400 watts
Electrical Principles
Group G5B

## Slide 272
 | G5B07 ~ What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value? | 
 |  | The peak-to-peak value
 |  | The peak value
 |  | The RMS value
 |  | The reciprocal of the RMS value
 | G5B07 ~ What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value? | 
 |  | The peak-to-peak value
 |  | The peak value
 |  | The reciprocal of the RMS value
 | G5B07 ~ What value of an AC signal produces the same power dissipation in a resistor as a DC voltage of the same value? | 
 | A. | The peak-to-peak value
 | B. | The peak value
 | C. | The RMS value
 | D. | The reciprocal of the RMS value
Electrical Principles
Group G5B

## Slide 273
 | G5B09 ~ What is the RMS voltage of a sine wave with a value of 17 volts peak? | 
 |  | 8.5 volts
 |  | 12 volts
 |  | 24 volts
 |  | 34 volts
 | G5B09 ~ What is the RMS voltage of a sine wave with a value of 17 volts peak? | 
 |  | 8.5 volts
 |  | 24 volts
 |  | 34 volts
 | G5B09 ~ What is the RMS voltage of a sine wave with a value of 17 volts peak? | 
 | A. | 8.5 volts
 | B. | 12 volts
 | C. | 24 volts
 | D. | 34 volts
Electrical Principles
Group G5B

## Slide 274
 | G5B10 ~ What percentage of power loss would result from a transmission line loss of 1 dB? | 
 |  | 10.9 percent
 |  | 12.2 percent
 |  | 20.5 percent
 |  | 25.9 percent
 | G5B10 ~ What percentage of power loss would result from a transmission line loss of 1 dB? | 
 |  | 10.9 percent
 |  | 12.2 percent
 |  | 25.9 percent
 | G5B10 ~ What percentage of power loss would result from a transmission line loss of 1 dB? | 
 | A. | 10.9 percent
 | B. | 12.2 percent
 | C. | 20.5 percent
 | D. | 25.9 percent
Electrical Principles
Group G5B

## Slide 275
 | G5B11 ~ What is the ratio of peak envelope power to average power for an unmodulated carrier? | 
 |  | 0.707
 |  | 1.0
 |  | 1.414
 |  | 2.0
 | G5B11 ~ What is the ratio of peak envelope power to average power for an unmodulated carrier? | 
 |  | 0.707
 |  | 1.414
 |  | 2.0
 | G5B11 ~ What is the ratio of peak envelope power to average power for an unmodulated carrier? | 
 | A. | 0.707
 | B. | 1.0
 | C. | 1.414
 | D. | 2.0
Electrical Principles
Group G5B

## Slide 276
 | G5B12 ~ What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts? | 
 |  | 173 volts
 |  | 245 volts
 |  | 346 volts
 |  | 692 volts
 | G5B12 ~ What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts? | 
 |  | 173 volts
 |  | 346 volts
 |  | 692 volts
 | G5B12 ~ What would be the RMS voltage across a 50 ohm dummy load dissipating 1200 watts? | 
 | A. | 173 volts
 | B. | 245 volts
 | C. | 346 volts
 | D. | 692 volts
Electrical Principles
Group G5B

## Slide 277
 | G5B13 ~ What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts? | 
 |  | 530 watts
 |  | 1060 watts
 |  | 1500 watts
 |  | 2120 watts
 | G5B13 ~ What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts? | 
 |  | 530 watts
 |  | 1500 watts
 |  | 2120 watts
 | G5B13 ~ What is the output PEP of an unmodulated carrier if an average reading wattmeter connected to the transmitter output indicates 1060 watts? | 
 | A. | 530 watts
 | B. | 1060 watts
 | C. | 1500 watts
 | D. | 2120 watts
Electrical Principles
Group G5B

## Slide 278
 | G5B14 ~ What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output? | 
 |  | 8.75 watts
 |  | 625 watts
 |  | 2500 watts
 |  | 5000 watts
 | G5B14 ~ What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output? | 
 |  | 8.75 watts
 |  | 2500 watts
 |  | 5000 watts
 | G5B14 ~ What is the output PEP from a transmitter if an oscilloscope measures 500 volts peak-to-peak across a 50 ohm resistive load connected to the transmitter output? | 
 | A. | 8.75 watts
 | B. | 625 watts
 | C. | 2500 watts
 | D. | 5000 watts
Electrical Principles
Group G5B

## Slide 279
G5C01 | G5C15
G5C02 | G5C16
G5C03 | G5C17
G5C04 | G5C18
G5C05 | 
G5C06 | 
G5C07 | 
G5C08 | 
G5C09 | 
G5C10 | 
G5C11 | 
G5C12 | 
G5C13 | 
G5C14 | 
Electrical Principles
Group G5C (18 Questions)
Resistors, capacitors, and inductors in series and parallel; transformers
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 280
 | G5C01 ~ What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding? | 
 |  | Capacitive coupling
 |  | Displacement current coupling
 |  | Mutual inductance
 |  | Mutual capacitance
 | G5C01 ~ What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding? | 
 |  | Capacitive coupling
 |  | Displacement current coupling
 |  | Mutual capacitance
 | G5C01 ~ What causes a voltage to appear across the secondary winding of a transformer when an AC voltage source is connected across its primary winding? | 
 | A. | Capacitive coupling
 | B. | Displacement current coupling
 | C. | Mutual inductance
 | D. | Mutual capacitance
Electrical Principles
Group G5C

## Slide 281
 | G5C02 ~ What happens if you reverse the primary and secondary windings of a 4:1 voltage step down transformer? | 
 |  | The secondary voltage becomes 4 times the primary voltage
 |  | The transformer no longer functions as it is a unidirectional device
 |  | Additional resistance must be added in series with the primary to prevent overload
 |  | Additional resistance must be added in parallel with the secondary to prevent overload
 | G5C02 ~ What happens if you reverse the primary and secondary windings of a 4:1 voltage step down transformer? | 
 |  | The transformer no longer functions as it is a unidirectional device
 |  | Additional resistance must be added in series with the primary to prevent overload
 |  | Additional resistance must be added in parallel with the secondary to prevent overload
 | G5C02 ~ What happens if you reverse the primary and secondary windings of a 4:1 voltage step down transformer? | 
 | A. | The secondary voltage becomes 4 times the primary voltage
 | B. | The transformer no longer functions as it is a unidirectional device
 | C. | Additional resistance must be added in series with the primary to prevent overload
 | D. | Additional resistance must be added in parallel with the secondary to prevent overload
Electrical Principles
Group G5C

## Slide 282
 | G5C03 ~ Which of the following components should be added to an existing resistor to increase the resistance? | 
 |  | A resistor in parallel
 |  | A resistor in series
 |  | A capacitor in series
 |  | A capacitor in parallel
 | G5C03 ~ Which of the following components should be added to an existing resistor to increase the resistance? | 
 |  | A resistor in parallel
 |  | A capacitor in series
 |  | A capacitor in parallel
 | G5C03 ~ Which of the following components should be added to an existing resistor to increase the resistance? | 
 | A. | A resistor in parallel
 | B. | A resistor in series
 | C. | A capacitor in series
 | D. | A capacitor in parallel
Electrical Principles
Group G5C

## Slide 283
 | G5C04 ~ What is the total resistance of three 100 ohm resistors in parallel? | 
 |  | 0.30 ohms
 |  | 0.33 ohms
 |  | 33.3 ohms
 |  | 300 ohms
 | G5C04 ~ What is the total resistance of three 100 ohm resistors in parallel? | 
 |  | 0.30 ohms
 |  | 0.33 ohms
 |  | 300 ohms
 | G5C04 ~ What is the total resistance of three 100 ohm resistors in parallel? | 
 | A. | 0.30 ohms
 | B. | 0.33 ohms
 | C. | 33.3 ohms
 | D. | 300 ohms
Electrical Principles
Group G5C

## Slide 284
 | G5C05 ~ If three equal value resistors in series produce 450 ohms, what is the value of each resistor? | 
 |  | 1500 ohms
 |  | 90 ohms
 |  | 150 ohms
 |  | 175 ohms
 | G5C05 ~ If three equal value resistors in series produce 450 ohms, what is the value of each resistor? | 
 |  | 1500 ohms
 |  | 90 ohms
 |  | 175 ohms
 | G5C05 ~ If three equal value resistors in series produce 450 ohms, what is the value of each resistor? | 
 | A. | 1500 ohms
 | B. | 90 ohms
 | C. | 150 ohms
 | D. | 175 ohms
Electrical Principles
Group G5C

## Slide 285
 | G5C06 ~ What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC? | 
 |  | 2370 volts
 |  | 540 volts
 |  | 26.7 volts
 |  | 5.9 volts
 | G5C06 ~ What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC? | 
 |  | 2370 volts
 |  | 540 volts
 |  | 5.9 volts
 | G5C06 ~ What is the RMS voltage across a 500-turn secondary winding in a transformer if the 2250-turn primary is connected to 120 VAC? | 
 | A. | 2370 volts
 | B. | 540 volts
 | C. | 26.7 volts
 | D. | 5.9 volts
Electrical Principles
Group G5C

## Slide 286
 | G5C07 ~ What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance? | 
 |  | 12.2 to 1
 |  | 24.4 to 1
 |  | 150 to 1
 |  | 300 to 1
 | G5C07 ~ What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance? | 
 |  | 24.4 to 1
 |  | 150 to 1
 |  | 300 to 1
 | G5C07 ~ What is the turns ratio of a transformer used to match an audio amplifier having 600 ohm output impedance to a speaker having 4 ohm impedance? | 
 | A. | 12.2 to 1
 | B. | 24.4 to 1
 | C. | 150 to 1
 | D. | 300 to 1
Electrical Principles
Group G5C

## Slide 287
 | G5C08 ~ What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel? | 
 |  | 576.9 nanofarads
 |  | 1733 picofarads
 |  | 3583 picofarads
 |  | 10.750 nanofarads
 | G5C08 ~ What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel? | 
 |  | 576.9 nanofarads
 |  | 1733 picofarads
 |  | 3583 picofarads
 | G5C08 ~ What is the equivalent capacitance of two 5.0 nanofarad capacitors and one 750 picofarad capacitor connected in parallel? | 
 | A. | 576.9 nanofarads
 | B. | 1733 picofarads
 | C. | 3583 picofarads
 | D. | 10.750 nanofarads
Electrical Principles
Group G5C

## Slide 288
 | G5C09 ~ What is the capacitance of three 100 microfarad capacitors connected in series? | 
 |  | 0.30 microfarads
 |  | 0.33 microfarads
 |  | 33.3 microfarads
 |  | 300 microfarads
 | G5C09 ~ What is the capacitance of three 100 microfarad capacitors connected in series? | 
 |  | 0.30 microfarads
 |  | 0.33 microfarads
 |  | 300 microfarads
 | G5C09 ~ What is the capacitance of three 100 microfarad capacitors connected in series? | 
 | A. | 0.30 microfarads
 | B. | 0.33 microfarads
 | C. | 33.3 microfarads
 | D. | 300 microfarads
Electrical Principles
Group G5C

## Slide 289
 | G5C10 ~ What is the inductance of three 10 millihenry inductors connected in parallel? | 
 |  | 0.30 henrys
 |  | 3.3 henrys
 |  | 3.3 millihenrys
 |  | 30 millihenrys
 | G5C10 ~ What is the inductance of three 10 millihenry inductors connected in parallel? | 
 |  | 0.30 henrys
 |  | 3.3 henrys
 |  | 30 millihenrys
 | G5C10 ~ What is the inductance of three 10 millihenry inductors connected in parallel? | 
 | A. | 0.30 henrys
 | B. | 3.3 henrys
 | C. | 3.3 millihenrys
 | D. | 30 millihenrys
Electrical Principles
Group G5C

## Slide 290
 | G5C11 ~ What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor? | 
 |  | 0.07 millihenrys
 |  | 14.3 millihenrys
 |  | 70 millihenrys
 |  | 1000 millihenrys
 | G5C11 ~ What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor? | 
 |  | 0.07 millihenrys
 |  | 14.3 millihenrys
 |  | 1000 millihenrys
 | G5C11 ~ What is the inductance of a 20 millihenry inductor connected in series with a 50 millihenry inductor? | 
 | A. | 0.07 millihenrys
 | B. | 14.3 millihenrys
 | C. | 70 millihenrys
 | D. | 1000 millihenrys
Electrical Principles
Group G5C

## Slide 291
 | G5C12 ~ What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor? | 
 |  | 0.07 microfarads
 |  | 14.3 microfarads
 |  | 70 microfarads
 |  | 1000 microfarads
 | G5C12 ~ What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor? | 
 |  | 0.07 microfarads
 |  | 70 microfarads
 |  | 1000 microfarads
 | G5C12 ~ What is the capacitance of a 20 microfarad capacitor connected in series with a 50 microfarad capacitor? | 
 | A. | 0.07 microfarads
 | B. | 14.3 microfarads
 | C. | 70 microfarads
 | D. | 1000 microfarads
Electrical Principles
Group G5C

## Slide 292
 | G5C13 ~ Which of the following components should be added to a capacitor to increase the capacitance? | 
 |  | An inductor in series
 |  | A resistor in series
 |  | A capacitor in parallel
 |  | A capacitor in series
 | G5C13 ~ Which of the following components should be added to a capacitor to increase the capacitance? | 
 |  | An inductor in series
 |  | A resistor in series
 |  | A capacitor in series
 | G5C13 ~ Which of the following components should be added to a capacitor to increase the capacitance? | 
 | A. | An inductor in series
 | B. | A resistor in series
 | C. | A capacitor in parallel
 | D. | A capacitor in series
Electrical Principles
Group G5C

## Slide 293
 | G5C14 ~ Which of the following components should be added to an inductor to increase the inductance? | 
 |  | A capacitor in series
 |  | A resistor in parallel
 |  | An inductor in parallel
 |  | An inductor in series
 | G5C14 ~ Which of the following components should be added to an inductor to increase the inductance? | 
 |  | A capacitor in series
 |  | A resistor in parallel
 |  | An inductor in parallel
 | G5C14 ~ Which of the following components should be added to an inductor to increase the inductance? | 
 | A. | A capacitor in series
 | B. | A resistor in parallel
 | C. | An inductor in parallel
 | D. | An inductor in series
Electrical Principles
Group G5C

## Slide 294
 | G5C15 ~ What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor connected in parallel? | 
 |  | 5.9 ohms
 |  | 0.17 ohms
 |  | 10000 ohms
 |  | 80 ohms
 | G5C15 ~ What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor connected in parallel? | 
 |  | 0.17 ohms
 |  | 10000 ohms
 |  | 80 ohms
 | G5C15 ~ What is the total resistance of a 10 ohm, a 20 ohm, and a 50 ohm resistor connected in parallel? | 
 | A. | 5.9 ohms
 | B. | 0.17 ohms
 | C. | 10000 ohms
 | D. | 80 ohms
Electrical Principles
Group G5C

## Slide 295
 | G5C16 ~ Why is the conductor of the primary winding of many voltage step up transformers larger in diameter than the conductor of the secondary winding? | 
 |  | To improve the coupling between the primary and secondary
 |  | To accommodate the higher current of the primary
 |  | To prevent parasitic oscillations due to resistive losses in the primary
 |  | To insure that the volume of the primary winding is equal to the volume of the secondary winding
 | G5C16 ~ Why is the conductor of the primary winding of many voltage step up transformers larger in diameter than the conductor of the secondary winding? | 
 |  | To improve the coupling between the primary and secondary
 |  | To prevent parasitic oscillations due to resistive losses in the primary
 |  | To insure that the volume of the primary winding is equal to the volume of the secondary winding
 | G5C16 ~ Why is the conductor of the primary winding of many voltage step up transformers larger in diameter than the conductor of the secondary winding? | 
 | A. | To improve the coupling between the primary and secondary
 | B. | To accommodate the higher current of the primary
 | C. | To prevent parasitic oscillations due to resistive losses in the primary
 | D. | To insure that the volume of the primary winding is equal to the volume of the secondary winding
Electrical Principles
Group G5C

## Slide 296
 | G5C17 ~ What is the value in nanofarads (nF) of a 22,000 pF capacitor? | 
 |  | 0.22 nF
 |  | 2.2 nF
 |  | 22 nF
 |  | 220 nF
 | G5C17 ~ What is the value in nanofarads (nF) of a 22,000 pF capacitor? | 
 |  | 0.22 nF
 |  | 2.2 nF
 |  | 220 nF
 | G5C17 ~ What is the value in nanofarads (nF) of a 22,000 pF capacitor? | 
 | A. | 0.22 nF
 | B. | 2.2 nF
 | C. | 22 nF
 | D. | 220 nF
Electrical Principles
Group G5C

## Slide 297
 | G5C18 ~ What is the value in microfarads of a 4700 nanofarad (nF) capacitor? | 
 |  | 47 �F
 |  | 0.47 �F
 |  | 47,000 �F
 |  | 4.7 �F
 | G5C18 ~ What is the value in microfarads of a 4700 nanofarad (nF) capacitor? | 
 |  | 47 �F
 |  | 0.47 �F
 |  | 47,000 �F
 | G5C18 ~ What is the value in microfarads of a 4700 nanofarad (nF) capacitor? | 
 | A. | 47 �F
 | B. | 0.47 �F
 | C. | 47,000 �F
 | D. | 4.7 �F
Electrical Principles
Group G5C

## Slide 298
Group |  | Questions
G6A | Resistors; Capacitors; Inductors; Rectifiers; solid state diodes and transistors; vacuum tubes; batteries | 18
G6B | Analog and digital integrated circuits (ICs); microprocessors; memory; I/O devices; microwave ICs (MMICs); display devices | 18
2 | Total | 36
Subelement G6 Circuit Components
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 299
G6A01 | G6A16
G6A02 | G6A17
G6A03 | G6A18
G6A04 | G6A19
G6A05 | 
G6A06 | 
G6A07 | 
G6A08 | 
G6A09 | 
G6A10 | 
G6A11 | 
G6A12 | 
G6A13 | 
G6A14 | 
Circuit Components
Group G6A (18 Questions)
Resistors; Capacitors; Inductors; Rectifiers; solid state diodes and transistors; vacuum tubes; batteries
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 300
 | G6A01 ~ What is the minimum allowable discharge voltage for maximum life of a standard 12 volt lead acid battery? | 
 |  | 6 volts
 |  | 8.5 volts
 |  | 10.5 volts
 |  | 12 volts
 | G6A01 ~ What is the minimum allowable discharge voltage for maximum life of a standard 12 volt lead acid battery? | 
 |  | 6 volts
 |  | 8.5 volts
 |  | 12 volts
 | G6A01 ~ What is the minimum allowable discharge voltage for maximum life of a standard 12 volt lead acid battery? | 
 | A. | 6 volts
 | B. | 8.5 volts
 | C. | 10.5 volts
 | D. | 12 volts
Circuit Components
Group G6A

## Slide 301
 | G6A02 ~ What is an advantage of the low internal resistance of nickel-cadmium batteries? | 
 |  | Long life
 |  | High discharge current
 |  | High voltage
 |  | Rapid recharge
 | G6A02 ~ What is an advantage of the low internal resistance of nickel-cadmium batteries? | 
 |  | Long life
 |  | High voltage
 |  | Rapid recharge
 | G6A02 ~ What is an advantage of the low internal resistance of nickel-cadmium batteries? | 
 | A. | Long life
 | B. | High discharge current
 | C. | High voltage
 | D. | Rapid recharge
Circuit Components
Group G6A

## Slide 302
 | G6A03 ~ What is the approximate junction threshold voltage of a germanium diode? | 
 |  | 0.1 volt
 |  | 0.3 volts
 |  | 0.7 volts
 |  | 1.0 volts
 | G6A03 ~ What is the approximate junction threshold voltage of a germanium diode? | 
 |  | 0.1 volt
 |  | 0.7 volts
 |  | 1.0 volts
 | G6A03 ~ What is the approximate junction threshold voltage of a germanium diode? | 
 | A. | 0.1 volt
 | B. | 0.3 volts
 | C. | 0.7 volts
 | D. | 1.0 volts
Circuit Components
Group G6A

## Slide 303
 | G6A04 ~ When is it acceptable to recharge a carbon-zinc primary cell? | 
 |  | As long as the voltage has not been allowed to drop below 1.0 volt
 |  | When the cell is kept warm during the recharging period
 |  | When a constant current charger is used
 |  | Never
 | G6A04 ~ When is it acceptable to recharge a carbon-zinc primary cell? | 
 |  | As long as the voltage has not been allowed to drop below 1.0 volt
 |  | When the cell is kept warm during the recharging period
 |  | When a constant current charger is used
 | G6A04 ~ When is it acceptable to recharge a carbon-zinc primary cell? | 
 | A. | As long as the voltage has not been allowed to drop below 1.0 volt
 | B. | When the cell is kept warm during the recharging period
 | C. | When a constant current charger is used
 | D. | Never
Circuit Components
Group G6A

## Slide 304
 | G6A05 ~ What is the approximate junction threshold voltage of a conventional silicon diode? | 
 |  | 0.1 volt
 |  | 0.3 volts
 |  | 0.7 volts
 |  | 1.0 volts
 | G6A05 ~ What is the approximate junction threshold voltage of a conventional silicon diode? | 
 |  | 0.1 volt
 |  | 0.3 volts
 |  | 1.0 volts
 | G6A05 ~ What is the approximate junction threshold voltage of a conventional silicon diode? | 
 | A. | 0.1 volt
 | B. | 0.3 volts
 | C. | 0.7 volts
 | D. | 1.0 volts
Circuit Components
Group G6A

## Slide 305
 | G6A06 ~ Which of the following is an advantage of using a Schottky diode in an RF switching circuit rather than a standard silicon diode? | 
 |  | Lower capacitance
 |  | Lower inductance
 |  | Longer switching times
 |  | Higher breakdown voltage
 | G6A06 ~ Which of the following is an advantage of using a Schottky diode in an RF switching circuit rather than a standard silicon diode? | 
 |  | Lower inductance
 |  | Longer switching times
 |  | Higher breakdown voltage
 | G6A06 ~ Which of the following is an advantage of using a Schottky diode in an RF switching circuit rather than a standard silicon diode? | 
 | A. | Lower capacitance
 | B. | Lower inductance
 | C. | Longer switching times
 | D. | Higher breakdown voltage
Circuit Components
Group G6A

## Slide 306
 | G6A07 ~ What are the stable operating points for a bipolar transistor used as a switch in a logic circuit? | 
 |  | Its saturation and cutoff regions
 |  | Its active region (between the cutoff and saturation regions)
 |  | Its peak and valley current points
 |  | Its enhancement and depletion modes
 | G6A07 ~ What are the stable operating points for a bipolar transistor used as a switch in a logic circuit? | 
 |  | Its active region (between the cutoff and saturation regions)
 |  | Its peak and valley current points
 |  | Its enhancement and depletion modes
 | G6A07 ~ What are the stable operating points for a bipolar transistor used as a switch in a logic circuit? | 
 | A. | Its saturation and cutoff regions
 | B. | Its active region (between the cutoff and saturation regions)
 | C. | Its peak and valley current points
 | D. | Its enhancement and depletion modes
Circuit Components
Group G6A

## Slide 307
 | G6A08 ~ Why must the cases of some large power transistors be insulated from ground? | 
 |  | To increase the beta of the transistor
 |  | To improve the power dissipation capability
 |  | To reduce stray capacitance
 |  | To avoid shorting the collector or drain voltage to ground
 | G6A08 ~ Why must the cases of some large power transistors be insulated from ground? | 
 |  | To increase the beta of the transistor
 |  | To improve the power dissipation capability
 |  | To reduce stray capacitance
 | G6A08 ~ Why must the cases of some large power transistors be insulated from ground? | 
 | A. | To increase the beta of the transistor
 | B. | To improve the power dissipation capability
 | C. | To reduce stray capacitance
 | D. | To avoid shorting the collector or drain voltage to ground
Circuit Components
Group G6A

## Slide 308
 | G6A09 ~ Which of the following describes the construction of a MOSFET? | 
 |  | The gate is formed by a back-biased junction
 |  | The gate is separated from the channel with a thin insulating layer
 |  | The source is separated from the drain by a thin insulating layer
 |  | The source is formed by depositing metal on silicon
 | G6A09 ~ Which of the following describes the construction of a MOSFET? | 
 |  | The gate is formed by a back-biased junction
 |  | The source is separated from the drain by a thin insulating layer
 |  | The source is formed by depositing metal on silicon
 | G6A09 ~ Which of the following describes the construction of a MOSFET? | 
 | A. | The gate is formed by a back-biased junction
 | B. | The gate is separated from the channel with a thin insulating layer
 | C. | The source is separated from the drain by a thin insulating layer
 | D. | The source is formed by depositing metal on silicon
Circuit Components
Group G6A

## Slide 309
 | G6A10 ~ Which element of a triode vacuum tube is used to regulate the flow of electrons between cathode and plate? | 
 |  | Control grid
 |  | Heater
 |  | Screen Grid
 |  | Trigger electrode
 | G6A10 ~ Which element of a triode vacuum tube is used to regulate the flow of electrons between cathode and plate? | 
 |  | Heater
 |  | Screen Grid
 |  | Trigger electrode
 | G6A10 ~ Which element of a triode vacuum tube is used to regulate the flow of electrons between cathode and plate? | 
 | A. | Control grid
 | B. | Heater
 | C. | Screen Grid
 | D. | Trigger electrode
Circuit Components
Group G6A

## Slide 310
 | G6A11 ~ Which of the following solid state devices is most like a vacuum tube in its general operating characteristics? | 
 |  | A bipolar transistor
 |  | A field effect transistor
 |  | A tunnel diode
 |  | A varistor
 | G6A11 ~ Which of the following solid state devices is most like a vacuum tube in its general operating characteristics? | 
 |  | A bipolar transistor
 |  | A tunnel diode
 |  | A varistor
 | G6A11 ~ Which of the following solid state devices is most like a vacuum tube in its general operating characteristics? | 
 | A. | A bipolar transistor
 | B. | A field effect transistor
 | C. | A tunnel diode
 | D. | A varistor
Circuit Components
Group G6A

## Slide 311
 | G6A12 ~ What is the primary purpose of a screen grid in a vacuum tube? | 
 |  | To reduce grid-to-plate capacitance
 |  | To increase efficiency
 |  | To increase the control grid resistance
 |  | To decrease plate resistance
 | G6A12 ~ What is the primary purpose of a screen grid in a vacuum tube? | 
 |  | To increase efficiency
 |  | To increase the control grid resistance
 |  | To decrease plate resistance
 | G6A12 ~ What is the primary purpose of a screen grid in a vacuum tube? | 
 | A. | To reduce grid-to-plate capacitance
 | B. | To increase efficiency
 | C. | To increase the control grid resistance
 | D. | To decrease plate resistance
Circuit Components
Group G6A

## Slide 312
 | G6A13 ~ Why is the polarity of applied voltages important for polarized capacitors? | 
 |  | Incorrect polarity can cause the capacitor to short-circuit
 |  | Reverse voltages can destroy the dielectric layer of an electrolytic capacitor
 |  | The capacitor could overheat and explode
 |  | All of these choices are correct
 | G6A13 ~ Why is the polarity of applied voltages important for polarized capacitors? | 
 |  | Incorrect polarity can cause the capacitor to short-circuit
 |  | Reverse voltages can destroy the dielectric layer of an electrolytic capacitor
 |  | The capacitor could overheat and explode
 | G6A13 ~ Why is the polarity of applied voltages important for polarized capacitors? | 
 | A. | Incorrect polarity can cause the capacitor to short-circuit
 | B. | Reverse voltages can destroy the dielectric layer of an electrolytic capacitor
 | C. | The capacitor could overheat and explode
 | D. | All of these choices are correct
Circuit Components
Group G6A

## Slide 313
 | G6A14 ~ Which of the following is an advantage of ceramic capacitors as compared to other types of capacitors? | 
 |  | Tight tolerance
 |  | High stability
 |  | High capacitance for given volume
 |  | Comparatively low cost
 | G6A14 ~ Which of the following is an advantage of ceramic capacitors as compared to other types of capacitors? | 
 |  | Tight tolerance
 |  | High stability
 |  | High capacitance for given volume
 | G6A14 ~ Which of the following is an advantage of ceramic capacitors as compared to other types of capacitors? | 
 | A. | Tight tolerance
 | B. | High stability
 | C. | High capacitance for given volume
 | D. | Comparatively low cost
Circuit Components
Group G6A

## Slide 314
 | G6A16 ~ What will happen to the resistance if the temperature of a resistor is increased? | 
 |  | It will change depending on the resistor's reactance coefficient
 |  | It will stay the same
 |  | It will change depending on the resistor's temperature coefficient
 |  | It will become time dependent
 | G6A16 ~ What will happen to the resistance if the temperature of a resistor is increased? | 
 |  | It will change depending on the resistor's reactance coefficient
 |  | It will stay the same
 |  | It will become time dependent
 | G6A16 ~ What will happen to the resistance if the temperature of a resistor is increased? | 
 | A. | It will change depending on the resistor's reactance coefficient
 | B. | It will stay the same
 | C. | It will change depending on the resistor's temperature coefficient
 | D. | It will become time dependent
Circuit Components
Group G6A

## Slide 315
 | G6A17 ~ Which of the following is a reason not to use wire-wound resistors in an RF circuit? | 
 |  | The resistor's tolerance value would not be adequate for such a circuit
 |  | The resistor's inductance could make circuit performance unpredictable
 |  | The resistor could overheat
 |  | The resistor's internal capacitance would detune the circuit
 | G6A17 ~ Which of the following is a reason not to use wire-wound resistors in an RF circuit? | 
 |  | The resistor's tolerance value would not be adequate for such a circuit
 |  | The resistor could overheat
 |  | The resistor's internal capacitance would detune the circuit
 | G6A17 ~ Which of the following is a reason not to use wire-wound resistors in an RF circuit? | 
 | A. | The resistor's tolerance value would not be adequate for such a circuit
 | B. | The resistor's inductance could make circuit performance unpredictable
 | C. | The resistor could overheat
 | D. | The resistor's internal capacitance would detune the circuit
Circuit Components
Group G6A

## Slide 316
 | G6A18 ~ What is an advantage of using a ferrite core toroidal inductor? | 
 |  | Large values of inductance may be obtained
 |  | The magnetic properties of the core may be optimized for a specific range of frequencies
 |  | Most of the magnetic field is contained in the core
 |  | All of these choices are correct
 | G6A18 ~ What is an advantage of using a ferrite core toroidal inductor? | 
 |  | Large values of inductance may be obtained
 |  | The magnetic properties of the core may be optimized for a specific range of frequencies
 |  | Most of the magnetic field is contained in the core
 | G6A18 ~ What is an advantage of using a ferrite core toroidal inductor? | 
 | A. | Large values of inductance may be obtained
 | B. | The magnetic properties of the core may be optimized for a specific range of frequencies
 | C. | Most of the magnetic field is contained in the core
 | D. | All of these choices are correct
Circuit Components
Group G6A

## Slide 317
 | G6A19 ~ How should the winding axes of two solenoid inductors be oriented to minimize their mutual inductance? | 
 |  | In line
 |  | Parallel to each other
 |  | At right angles to each other
 |  | Interleaved
 | G6A19 ~ How should the winding axes of two solenoid inductors be oriented to minimize their mutual inductance? | 
 |  | In line
 |  | Parallel to each other
 |  | Interleaved
 | G6A19 ~ How should the winding axes of two solenoid inductors be oriented to minimize their mutual inductance? | 
 | A. | In line
 | B. | Parallel to each other
 | C. | At right angles to each other
 | D. | Interleaved
Circuit Components
Group G6A

## Slide 318
G6B01 | G6B15
G6B02 | G6B16
G6B03 | G6B17
G6B04 | G6B18
G6B05 | 
G6B06 | 
G6B07 | 
G6B08 | 
G6B09 | 
G6B10 | 
G6B11 | 
G6B12 | 
G6B13 | 
G6B14 | 
Circuit Components
Group G6B (18 Questions)
Analog and digital integrated circuits (ICs); microprocessors; memory; I/O devices; microwave ICs (MMICs); display devices
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 319
 | G6B01 ~ Which of the following is an analog integrated circuit? | 
 |  | NAND Gate
 |  | Microprocessor
 |  | Frequency Counter
 |  | Linear voltage regulator
 | G6B01 ~ Which of the following is an analog integrated circuit? | 
 |  | NAND Gate
 |  | Microprocessor
 |  | Frequency Counter
 | G6B01 ~ Which of the following is an analog integrated circuit? | 
 | A. | NAND Gate
 | B. | Microprocessor
 | C. | Frequency Counter
 | D. | Linear voltage regulator
Circuit Components
Group G6B

## Slide 320
 | G6B02 ~ What is meant by the term MMIC? | 
 |  | Multi Megabyte Integrated Circuit
 |  | Monolithic Microwave Integrated Circuit
 |  | Military Manufactured Integrated Circuit
 |  | Mode Modulated Integrated Circuit
 | G6B02 ~ What is meant by the term MMIC? | 
 |  | Multi Megabyte Integrated Circuit
 |  | Military Manufactured Integrated Circuit
 |  | Mode Modulated Integrated Circuit
 | G6B02 ~ What is meant by the term MMIC? | 
 | A. | Multi Megabyte Integrated Circuit
 | B. | Monolithic Microwave Integrated Circuit
 | C. | Military Manufactured Integrated Circuit
 | D. | Mode Modulated Integrated Circuit
Circuit Components
Group G6B

## Slide 321
 | G6B03 ~ Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits? | 
 |  | Low power consumption
 |  | High power handling capability
 |  | Better suited for RF amplification
 |  | Better suited for power supply regulation
 | G6B03 ~ Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits? | 
 |  | High power handling capability
 |  | Better suited for RF amplification
 |  | Better suited for power supply regulation
 | G6B03 ~ Which of the following is an advantage of CMOS integrated circuits compared to TTL integrated circuits? | 
 | A. | Low power consumption
 | B. | High power handling capability
 | C. | Better suited for RF amplification
 | D. | Better suited for power supply regulation
Circuit Components
Group G6B

## Slide 322
 | G6B04 ~ What is meant by the term ROM? | 
 |  | Resistor Operated Memory
 |  | Read Only Memory
 |  | Random Operational Memory
 |  | Resistant to Overload Memory
 | G6B04 ~ What is meant by the term ROM? | 
 |  | Resistor Operated Memory
 |  | Random Operational Memory
 |  | Resistant to Overload Memory
 | G6B04 ~ What is meant by the term ROM? | 
 | A. | Resistor Operated Memory
 | B. | Read Only Memory
 | C. | Random Operational Memory
 | D. | Resistant to Overload Memory
Circuit Components
Group G6B

## Slide 323
 | G6B05 ~ What is meant when memory is characterized as non-volatile? | 
 |  | It is resistant to radiation damage
 |  | It is resistant to high temperatures
 |  | The stored information is maintained even if power is removed
 |  | The stored information cannot be changed once written
 | G6B05 ~ What is meant when memory is characterized as non-volatile? | 
 |  | It is resistant to radiation damage
 |  | It is resistant to high temperatures
 |  | The stored information cannot be changed once written
 | G6B05 ~ What is meant when memory is characterized as non-volatile? | 
 | A. | It is resistant to radiation damage
 | B. | It is resistant to high temperatures
 | C. | The stored information is maintained even if power is removed
 | D. | The stored information cannot be changed once written
Circuit Components
Group G6B

## Slide 324
 | G6B06 ~ What kind of device is an integrated circuit operational amplifier? | 
 |  | Digital
 |  | MMIC
 |  | Programmable Logic
 |  | Analog
 | G6B06 ~ What kind of device is an integrated circuit operational amplifier? | 
 |  | Digital
 |  | MMIC
 |  | Programmable Logic
 | G6B06 ~ What kind of device is an integrated circuit operational amplifier? | 
 | A. | Digital
 | B. | MMIC
 | C. | Programmable Logic
 | D. | Analog
Circuit Components
Group G6B

## Slide 325
 | G6B07 ~ Which of the following is an advantage of an LED indicator compared to an incandescent indicator? | 
 |  | Lower power consumption
 |  | Faster response time
 |  | Longer life
 |  | All of these choices are correct
 | G6B07 ~ Which of the following is an advantage of an LED indicator compared to an incandescent indicator? | 
 |  | Lower power consumption
 |  | Faster response time
 |  | Longer life
 | G6B07 ~ Which of the following is an advantage of an LED indicator compared to an incandescent indicator? | 
 | A. | Lower power consumption
 | B. | Faster response time
 | C. | Longer life
 | D. | All of these choices are correct
Circuit Components
Group G6B

## Slide 326
 | G6B08 ~ How is an LED biased when emitting light? | 
 |  | Beyond cutoff
 |  | At the Zener voltage
 |  | Reverse Biased
 |  | Forward Biased
 | G6B08 ~ How is an LED biased when emitting light? | 
 |  | Beyond cutoff
 |  | At the Zener voltage
 |  | Reverse Biased
 | G6B08 ~ How is an LED biased when emitting light? | 
 | A. | Beyond cutoff
 | B. | At the Zener voltage
 | C. | Reverse Biased
 | D. | Forward Biased
Circuit Components
Group G6B

## Slide 327
 | G6B09 ~ Which of the following is a characteristic of a liquid crystal display? | 
 |  | It requires ambient or back lighting
 |  | It offers a wide dynamic range
 |  | It has a wide viewing angle
 |  | All of these choices are correct
 | G6B09 ~ Which of the following is a characteristic of a liquid crystal display? | 
 |  | It offers a wide dynamic range
 |  | It has a wide viewing angle
 |  | All of these choices are correct
 | G6B09 ~ Which of the following is a characteristic of a liquid crystal display? | 
 | A. | It requires ambient or back lighting
 | B. | It offers a wide dynamic range
 | C. | It has a wide viewing angle
 | D. | All of these choices are correct
Circuit Components
Group G6B

## Slide 328
 | G6B10 ~ What two devices in an Amateur Radio station might be connected using a USB interface? | 
 |  | Computer and transceiver
 |  | Microphone and transceiver
 |  | Amplifier and antenna
 |  | Power supply and amplifier
 | G6B10 ~ What two devices in an Amateur Radio station might be connected using a USB interface? | 
 |  | Microphone and transceiver
 |  | Amplifier and antenna
 |  | Power supply and amplifier
 | G6B10 ~ What two devices in an Amateur Radio station might be connected using a USB interface? | 
 | A. | Computer and transceiver
 | B. | Microphone and transceiver
 | C. | Amplifier and antenna
 | D. | Power supply and amplifier
Circuit Components
Group G6B

## Slide 329
 | G6B11 ~ What is a microprocessor? | 
 |  | A low power analog signal processor used as a microwave detector
 |  | A computer on a single integrated circuit
 |  | A microwave detector, amplifier, and local oscillator on a single integrated circuit
 |  | A low voltage amplifier used in a microwave transmitter modulator stage
 | G6B11 ~ What is a microprocessor? | 
 |  | A low power analog signal processor used as a microwave detector
 |  | A microwave detector, amplifier, and local oscillator on a single integrated circuit
 |  | A low voltage amplifier used in a microwave transmitter modulator stage
 | G6B11 ~ What is a microprocessor? | 
 | A. | A low power analog signal processor used as a microwave detector
 | B. | A computer on a single integrated circuit
 | C. | A microwave detector, amplifier, and local oscillator on a single integrated circuit
 | D. | A low voltage amplifier used in a microwave transmitter modulator stage
Circuit Components
Group G6B

## Slide 330
 | G6B12 ~ Which of the following connectors would be a good choice for a serial data port? | 
 |  | PL-259
 |  | Type N
 |  | Type SMA
 |  | DE-9
 | G6B12 ~ Which of the following connectors would be a good choice for a serial data port? | 
 |  | PL-259
 |  | Type N
 |  | Type SMA
 | G6B12 ~ Which of the following connectors would be a good choice for a serial data port? | 
 | A. | PL-259
 | B. | Type N
 | C. | Type SMA
 | D. | DE-9
Circuit Components
Group G6B

## Slide 331
 | G6B13 ~ Which of these connector types is commonly used for RF connections at frequencies up to 150 MHz? | 
 |  | Octal
 |  | RJ-11
 |  | PL-259
 |  | DB-25
 | G6B13 ~ Which of these connector types is commonly used for RF connections at frequencies up to 150 MHz? | 
 |  | Octal
 |  | RJ-11
 |  | DB-25
 | G6B13 ~ Which of these connector types is commonly used for RF connections at frequencies up to 150 MHz? | 
 | A. | Octal
 | B. | RJ-11
 | C. | PL-259
 | D. | DB-25
Circuit Components
Group G6B

## Slide 332
 | G6B14 ~ Which of these connector types is commonly used for audio signals in Amateur Radio stations? | 
 |  | PL-259
 |  | BNC
 |  | RCA Phono
 |  | Type N
 | G6B14 ~ Which of these connector types is commonly used for audio signals in Amateur Radio stations? | 
 |  | PL-259
 |  | BNC
 |  | Type N
 | G6B14 ~ Which of these connector types is commonly used for audio signals in Amateur Radio stations? | 
 | A. | PL-259
 | B. | BNC
 | C. | RCA Phono
 | D. | Type N
Circuit Components
Group G6B

## Slide 333
 | G6B15 ~ What is the main reason to use keyed connectors instead of non-keyed types? | 
 |  | Prevention of use by unauthorized persons
 |  | Reduced chance of incorrect mating
 |  | Higher current carrying capacity
 |  | All of these choices are correct
 | G6B15 ~ What is the main reason to use keyed connectors instead of non-keyed types? | 
 |  | Prevention of use by unauthorized persons
 |  | Higher current carrying capacity
 |  | All of these choices are correct
 | G6B15 ~ What is the main reason to use keyed connectors instead of non-keyed types? | 
 | A. | Prevention of use by unauthorized persons
 | B. | Reduced chance of incorrect mating
 | C. | Higher current carrying capacity
 | D. | All of these choices are correct
Circuit Components
Group G6B

## Slide 334
 | G6B16 ~ Which of the following describes a type N connector? | 
 |  | A moisture-resistant RF connector useful to 10 GHz
 |  | A small bayonet connector used for data circuits
 |  | A threaded connector used for hydraulic systems
 |  | An audio connector used in surround-sound installations
 | G6B16 ~ Which of the following describes a type N connector? | 
 |  | A small bayonet connector used for data circuits
 |  | A threaded connector used for hydraulic systems
 |  | An audio connector used in surround-sound installations
 | G6B16 ~ Which of the following describes a type N connector? | 
 | A. | A moisture-resistant RF connector useful to 10 GHz
 | B. | A small bayonet connector used for data circuits
 | C. | A threaded connector used for hydraulic systems
 | D. | An audio connector used in surround-sound installations
Circuit Components
Group G6B

## Slide 335
 | G6B17 ~ What is the general description of a DIN type connector? | 
 |  | A special connector for microwave interfacing
 |  | A DC power connector rated for currents between 30 and 50 amperes
 |  | A family of multiple circuit connectors suitable for audio and control signals
 |  | A special watertight connector for use in marine applications
 | G6B17 ~ What is the general description of a DIN type connector? | 
 |  | A special connector for microwave interfacing
 |  | A DC power connector rated for currents between 30 and 50 amperes
 |  | A special watertight connector for use in marine applications
 | G6B17 ~ What is the general description of a DIN type connector? | 
 | A. | A special connector for microwave interfacing
 | B. | A DC power connector rated for currents between 30 and 50 amperes
 | C. | A family of multiple circuit connectors suitable for audio and control signals
 | D. | A special watertight connector for use in marine applications
Circuit Components
Group G6B

## Slide 336
 | G6B18 ~ What is a type SMA connector? | 
 |  | A large bayonet connector usable at power levels in excess of 1 KW
 |  | A small threaded connector suitable for signals up to several GHz
 |  | A connector designed for serial multiple access signals
 |  | A type of push-on connector intended for high voltage applications
 | G6B18 ~ What is a type SMA connector? | 
 |  | A large bayonet connector usable at power levels in excess of 1 KW
 |  | A connector designed for serial multiple access signals
 |  | A type of push-on connector intended for high voltage applications
 | G6B18 ~ What is a type SMA connector? | 
 | A. | A large bayonet connector usable at power levels in excess of 1 KW
 | B. | A small threaded connector suitable for signals up to several GHz
 | C. | A connector designed for serial multiple access signals
 | D. | A type of push-on connector intended for high voltage applications
Circuit Components
Group G6B

## Slide 337
Group |  | Questions
G7A | Power supplies; and schematic symbols | 12
G7B | Digital circuits; amplifiers and oscillators | 14
G7C | Receivers and transmitters; filters, oscillators | 11
3 | Total | 37
Subelement G7 Practical Circuits
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 338
G7A01
G7A02
G7A03
G7A04
G7A05
G7A06
G7A07
G7A09
G7A10
G7A11
G7A12
G7A13
Practical Circuits
Group G7A (12 Questions)
Power supplies; and schematic symbols
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 339
 | G7A01 ~ What useful feature does a power supply bleeder resistor provide? | 
 |  | It acts as a fuse for excess voltage
 |  | It ensures that the filter capacitors are discharged when power is removed
 |  | It removes shock hazards from the induction coils
 |  | It eliminates ground loop current
 | G7A01 ~ What useful feature does a power supply bleeder resistor provide? | 
 |  | It acts as a fuse for excess voltage
 |  | It removes shock hazards from the induction coils
 |  | It eliminates ground loop current
 | G7A01 ~ What useful feature does a power supply bleeder resistor provide? | 
 | A. | It acts as a fuse for excess voltage
 | B. | It ensures that the filter capacitors are discharged when power is removed
 | C. | It removes shock hazards from the induction coils
 | D. | It eliminates ground loop current
Practical Circuits
Group G7A

## Slide 340
 | G7A02 ~ Which of the following components are used in a power supply filter network? | 
 |  | Diodes
 |  | Transformers and transducers
 |  | Quartz crystals
 |  | Capacitors and inductors
 | G7A02 ~ Which of the following components are used in a power supply filter network? | 
 |  | Diodes
 |  | Transformers and transducers
 |  | Quartz crystals
 | G7A02 ~ Which of the following components are used in a power supply filter network? | 
 | A. | Diodes
 | B. | Transformers and transducers
 | C. | Quartz crystals
 | D. | Capacitors and inductors
Practical Circuits
Group G7A

## Slide 341
 | G7A03 ~ What is the peak-inverse-voltage across the rectifiers in a full-wave bridge power supply? | 
 |  | One-quarter the normal output voltage of the power supply
 |  | Half the normal output voltage of the power supply
 |  | Double the normal peak output voltage of the power supply
 |  | Equal to the normal peak output voltage of the power supply
 | G7A03 ~ What is the peak-inverse-voltage across the rectifiers in a full-wave bridge power supply? | 
 |  | One-quarter the normal output voltage of the power supply
 |  | Half the normal output voltage of the power supply
 |  | Double the normal peak output voltage of the power supply
 | G7A03 ~ What is the peak-inverse-voltage across the rectifiers in a full-wave bridge power supply? | 
 | A. | One-quarter the normal output voltage of the power supply
 | B. | Half the normal output voltage of the power supply
 | C. | Double the normal peak output voltage of the power supply
 | D. | Equal to the normal peak output voltage of the power supply
Practical Circuits
Group G7A

## Slide 342
 | G7A04 ~ What is the peak-inverse-voltage across the rectifier in a half-wave power supply? | 
 |  | One-half the normal peak output voltage of the power supply
 |  | One-half the normal output voltage of the power supply
 |  | Equal to the normal output voltage of the power supply
 |  | Two times the normal peak output voltage of the power supply
 | G7A04 ~ What is the peak-inverse-voltage across the rectifier in a half-wave power supply? | 
 |  | One-half the normal peak output voltage of the power supply
 |  | One-half the normal output voltage of the power supply
 |  | Equal to the normal output voltage of the power supply
 | G7A04 ~ What is the peak-inverse-voltage across the rectifier in a half-wave power supply? | 
 | A. | One-half the normal peak output voltage of the power supply
 | B. | One-half the normal output voltage of the power supply
 | C. | Equal to the normal output voltage of the power supply
 | D. | Two times the normal peak output voltage of the power supply
Practical Circuits
Group G7A

## Slide 343
 | G7A05 ~ What portion of the AC cycle is converted to DC by a half-wave rectifier? | 
 |  | 90 degrees
 |  | 180 degrees
 |  | 270 degrees
 |  | 360 degrees
 | G7A05 ~ What portion of the AC cycle is converted to DC by a half-wave rectifier? | 
 |  | 90 degrees
 |  | 270 degrees
 |  | 360 degrees
 | G7A05 ~ What portion of the AC cycle is converted to DC by a half-wave rectifier? | 
 | A. | 90 degrees
 | B. | 180 degrees
 | C. | 270 degrees
 | D. | 360 degrees
Practical Circuits
Group G7A

## Slide 344
 | G7A06 ~ What portion of the AC cycle is converted to DC by a full-wave rectifier? | 
 |  | 90 degrees
 |  | 180 degrees
 |  | 270 degrees
 |  | 360 degrees
 | G7A06 ~ What portion of the AC cycle is converted to DC by a full-wave rectifier? | 
 |  | 90 degrees
 |  | 180 degrees
 |  | 270 degrees
 | G7A06 ~ What portion of the AC cycle is converted to DC by a full-wave rectifier? | 
 | A. | 90 degrees
 | B. | 180 degrees
 | C. | 270 degrees
 | D. | 360 degrees
Practical Circuits
Group G7A

## Slide 345
 | G7A07 ~ What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load? | 
 |  | A series of DC pulses at twice the frequency of the AC input
 |  | A series of DC pulses at the same frequency as the AC input
 |  | A sine wave at half the frequency of the AC input
 |  | A steady DC voltage
 | G7A07 ~ What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load? | 
 |  | A series of DC pulses at the same frequency as the AC input
 |  | A sine wave at half the frequency of the AC input
 |  | A steady DC voltage
 | G7A07 ~ What is the output waveform of an unfiltered full-wave rectifier connected to a resistive load? | 
 | A. | A series of DC pulses at twice the frequency of the AC input
 | B. | A series of DC pulses at the same frequency as the AC input
 | C. | A sine wave at half the frequency of the AC input
 | D. | A steady DC voltage
Practical Circuits
Group G7A

## Slide 346
 | G7A09 ~ Which symbol in figure G7-1 represents a field effect transistor? | 
 |  | Symbol 2
 |  | Symbol 5
 |  | Symbol 1
 |  | Symbol 4
 | G7A09 ~ Which symbol in figure G7-1 represents a field effect transistor? | 
 |  | Symbol 2
 |  | Symbol 5
 |  | Symbol 4
 | G7A09 ~ Which symbol in figure G7-1 represents a field effect transistor? | 
 | A. | Symbol 2
 | B. | Symbol 5
 | C. | Symbol 1
 | D. | Symbol 4
Practical Circuits
Group G7A

## Slide 347
 | G7A10 ~ Which symbol in figure G7-1 represents a Zener diode? | 
 |  | Symbol 4
 |  | Symbol 1
 |  | Symbol 11
 |  | Symbol 5
 | G7A10 ~ Which symbol in figure G7-1 represents a Zener diode? | 
 |  | Symbol 4
 |  | Symbol 1
 |  | Symbol 11
 | G7A10 ~ Which symbol in figure G7-1 represents a Zener diode? | 
 | A. | Symbol 4
 | B. | Symbol 1
 | C. | Symbol 11
 | D. | Symbol 5
Practical Circuits
Group G7A

## Slide 348
 | G7A11 ~ Which symbol in figure G7-1 represents an NPN junction transistor? | 
 |  | Symbol 1
 |  | Symbol 2
 |  | Symbol 7
 |  | Symbol 11
 | G7A11 ~ Which symbol in figure G7-1 represents an NPN junction transistor? | 
 |  | Symbol 1
 |  | Symbol 7
 |  | Symbol 11
 | G7A11 ~ Which symbol in figure G7-1 represents an NPN junction transistor? | 
 | A. | Symbol 1
 | B. | Symbol 2
 | C. | Symbol 7
 | D. | Symbol 11
Practical Circuits
Group G7A

## Slide 349
 | G7A12 ~ Which symbol in Figure G7-1 represents a multiple-winding transformer? | 
 |  | Symbol 4
 |  | Symbol 7
 |  | Symbol 6
 |  | Symbol 1
 | G7A12 ~ Which symbol in Figure G7-1 represents a multiple-winding transformer? | 
 |  | Symbol 4
 |  | Symbol 7
 |  | Symbol 1
 | G7A12 ~ Which symbol in Figure G7-1 represents a multiple-winding transformer? | 
 | A. | Symbol 4
 | B. | Symbol 7
 | C. | Symbol 6
 | D. | Symbol 1
Practical Circuits
Group G7A

## Slide 350
 | G7A13 ~ Which symbol in Figure G7-1 represents a tapped inductor? | 
 |  | Symbol 7
 |  | Symbol 11
 |  | Symbol 6
 |  | Symbol 1
 | G7A13 ~ Which symbol in Figure G7-1 represents a tapped inductor? | 
 |  | Symbol 11
 |  | Symbol 6
 |  | Symbol 1
 | G7A13 ~ Which symbol in Figure G7-1 represents a tapped inductor? | 
 | A. | Symbol 7
 | B. | Symbol 11
 | C. | Symbol 6
 | D. | Symbol 1
Practical Circuits
Group G7A

## Slide 351
G7B01
G7B02
G7B03
G7B04
G7B05
G7B06
G7B07
G7B08
G7B09
G7B10
G7B11
G7B12
G7B13
G7B14
Practical Circuits
Group G7B (14 Questions)
Digital circuits; amplifiers and oscillators
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 352
 | G7B01 ~ Complex digital circuitry can often be replaced by what type of integrated circuit? | 
 |  | Microcontroller
 |  | Charge-coupled device
 |  | Phase detector
 |  | Window comparator
 | G7B01 ~ Complex digital circuitry can often be replaced by what type of integrated circuit? | 
 |  | Charge-coupled device
 |  | Phase detector
 |  | Window comparator
 | G7B01 ~ Complex digital circuitry can often be replaced by what type of integrated circuit? | 
 | A. | Microcontroller
 | B. | Charge-coupled device
 | C. | Phase detector
 | D. | Window comparator
Practical Circuits
Group G7B

## Slide 353
 | G7B02 ~ Which of the following is an advantage of using the binary system when processing digital signals? | 
 |  | Binary "ones" and "zeros" are easy to represent by an "on" or "off" state
 |  | The binary number system is most accurate
 |  | Binary numbers are more compatible with analog circuitry
 |  | All of these choices are correct
 | G7B02 ~ Which of the following is an advantage of using the binary system when processing digital signals? | 
 |  | The binary number system is most accurate
 |  | Binary numbers are more compatible with analog circuitry
 |  | All of these choices are correct
 | G7B02 ~ Which of the following is an advantage of using the binary system when processing digital signals? | 
 | A. | Binary "ones" and "zeros" are easy to represent by an "on" or "off" state
 | B. | The binary number system is most accurate
 | C. | Binary numbers are more compatible with analog circuitry
 | D. | All of these choices are correct
Practical Circuits
Group G7B

## Slide 354
 | G7B03 ~ Which of the following describes the function of a two input AND gate? | 
 |  | Output is high when either or both inputs are low
 |  | Output is high only when both inputs are high
 |  | Output is low when either or both inputs are high
 |  | Output is low only when both inputs are high
 | G7B03 ~ Which of the following describes the function of a two input AND gate? | 
 |  | Output is high when either or both inputs are low
 |  | Output is low when either or both inputs are high
 |  | Output is low only when both inputs are high
 | G7B03 ~ Which of the following describes the function of a two input AND gate? | 
 | A. | Output is high when either or both inputs are low
 | B. | Output is high only when both inputs are high
 | C. | Output is low when either or both inputs are high
 | D. | Output is low only when both inputs are high
Practical Circuits
Group G7B

## Slide 355
 | G7B04 ~ Which of the following describes the function of a two input NOR gate? | 
 |  | Output is high when either or both inputs are low
 |  | Output is high only when both inputs are high
 |  | Output is low when either or both inputs are high
 |  | Output is low only when both inputs are high
 | G7B04 ~ Which of the following describes the function of a two input NOR gate? | 
 |  | Output is high when either or both inputs are low
 |  | Output is high only when both inputs are high
 |  | Output is low only when both inputs are high
 | G7B04 ~ Which of the following describes the function of a two input NOR gate? | 
 | A. | Output is high when either or both inputs are low
 | B. | Output is high only when both inputs are high
 | C. | Output is low when either or both inputs are high
 | D. | Output is low only when both inputs are high
Practical Circuits
Group G7B

## Slide 356
 | G7B05 ~ How many states does a 3-bit binary counter have? | 
 |  | 3
 |  | 6
 |  | 8
 |  | 16
 | G7B05 ~ How many states does a 3-bit binary counter have? | 
 |  | 3
 |  | 6
 |  | 16
 | G7B05 ~ How many states does a 3-bit binary counter have? | 
 | A. | 3
 | B. | 6
 | C. | 8
 | D. | 16
Practical Circuits
Group G7B

## Slide 357
 | G7B06 ~ What is a shift register? | 
 |  | A clocked array of circuits that passes data in steps along the array
 |  | An array of operational amplifiers used for tri-state arithmetic operations
 |  | A digital mixer
 |  | An analog mixer
 | G7B06 ~ What is a shift register? | 
 |  | An array of operational amplifiers used for tri-state arithmetic operations
 |  | A digital mixer
 |  | An analog mixer
 | G7B06 ~ What is a shift register? | 
 | A. | A clocked array of circuits that passes data in steps along the array
 | B. | An array of operational amplifiers used for tri-state arithmetic operations
 | C. | A digital mixer
 | D. | An analog mixer
Practical Circuits
Group G7B

## Slide 358
 | G7B07 ~ What are the basic components of virtually all sine wave oscillators? | 
 |  | An amplifier and a divider
 |  | A frequency multiplier and a mixer
 |  | A circulator and a filter operating in a feed-forward loop
 |  | A filter and an amplifier operating in a feedback loop
 | G7B07 ~ What are the basic components of virtually all sine wave oscillators? | 
 |  | An amplifier and a divider
 |  | A frequency multiplier and a mixer
 |  | A circulator and a filter operating in a feed-forward loop
 | G7B07 ~ What are the basic components of virtually all sine wave oscillators? | 
 | A. | An amplifier and a divider
 | B. | A frequency multiplier and a mixer
 | C. | A circulator and a filter operating in a feed-forward loop
 | D. | A filter and an amplifier operating in a feedback loop
Practical Circuits
Group G7B

## Slide 359
 | G7B08 ~ How is the efficiency of an RF power amplifier determined? | 
 |  | Divide the DC input power by the DC output power
 |  | Divide the RF output power by the DC input power
 |  | Multiply the RF input power by the reciprocal of the RF output power
 |  | Add the RF input power to the DC output power
 | G7B08 ~ How is the efficiency of an RF power amplifier determined? | 
 |  | Divide the DC input power by the DC output power
 |  | Multiply the RF input power by the reciprocal of the RF output power
 |  | Add the RF input power to the DC output power
 | G7B08 ~ How is the efficiency of an RF power amplifier determined? | 
 | A. | Divide the DC input power by the DC output power
 | B. | Divide the RF output power by the DC input power
 | C. | Multiply the RF input power by the reciprocal of the RF output power
 | D. | Add the RF input power to the DC output power
Practical Circuits
Group G7B

## Slide 360
 | G7B09 ~ What determines the frequency of an LC oscillator? | 
 |  | The number of stages in the counter
 |  | The number of stages in the divider
 |  | The inductance and capacitance in the tank circuit
 |  | The time delay of the lag circuit
 | G7B09 ~ What determines the frequency of an LC oscillator? | 
 |  | The number of stages in the counter
 |  | The number of stages in the divider
 |  | The time delay of the lag circuit
 | G7B09 ~ What determines the frequency of an LC oscillator? | 
 | A. | The number of stages in the counter
 | B. | The number of stages in the divider
 | C. | The inductance and capacitance in the tank circuit
 | D. | The time delay of the lag circuit
Practical Circuits
Group G7B

## Slide 361
 | G7B10 ~ Which of the following is a characteristic of a Class A amplifier? | 
 |  | Low standby power
 |  | High Efficiency
 |  | No need for bias
 |  | Low distortion
 | G7B10 ~ Which of the following is a characteristic of a Class A amplifier? | 
 |  | Low standby power
 |  | High Efficiency
 |  | No need for bias
 | G7B10 ~ Which of the following is a characteristic of a Class A amplifier? | 
 | A. | Low standby power
 | B. | High Efficiency
 | C. | No need for bias
 | D. | Low distortion
Practical Circuits
Group G7B

## Slide 362
 | G7B11 ~ For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal? | 
 |  | SSB
 |  | CW
 |  | AM
 |  | All of these choices are correct
 | G7B11 ~ For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal? | 
 |  | SSB
 |  | AM
 |  | All of these choices are correct
 | G7B11 ~ For which of the following modes is a Class C power stage appropriate for amplifying a modulated signal? | 
 | A. | SSB
 | B. | CW
 | C. | AM
 | D. | All of these choices are correct
Practical Circuits
Group G7B

## Slide 363
 | G7B12 ~ Which of these classes of amplifiers has the highest efficiency? | 
 |  | Class A
 |  | Class B
 |  | Class AB
 |  | Class C
 | G7B12 ~ Which of these classes of amplifiers has the highest efficiency? | 
 |  | Class A
 |  | Class B
 |  | Class AB
 | G7B12 ~ Which of these classes of amplifiers has the highest efficiency? | 
 | A. | Class A
 | B. | Class B
 | C. | Class AB
 | D. | Class C
Practical Circuits
Group G7B

## Slide 364
 | G7B13 ~ What is the reason for neutralizing the final amplifier stage of a transmitter? | 
 |  | To limit the modulation index
 |  | To eliminate self-oscillations
 |  | To cut off the final amplifier during standby periods
 |  | To keep the carrier on frequency
 | G7B13 ~ What is the reason for neutralizing the final amplifier stage of a transmitter? | 
 |  | To limit the modulation index
 |  | To cut off the final amplifier during standby periods
 |  | To keep the carrier on frequency
 | G7B13 ~ What is the reason for neutralizing the final amplifier stage of a transmitter? | 
 | A. | To limit the modulation index
 | B. | To eliminate self-oscillations
 | C. | To cut off the final amplifier during standby periods
 | D. | To keep the carrier on frequency
Practical Circuits
Group G7B

## Slide 365
 | G7B14 ~ Which of the following describes a linear amplifier? | 
 |  | Any RF power amplifier used in conjunction with an amateur transceiver
 |  | An amplifier in which the output preserves the input waveform
 |  | A Class C high efficiency amplifier
 |  | An amplifier used as a frequency multiplier
 | G7B14 ~ Which of the following describes a linear amplifier? | 
 |  | Any RF power amplifier used in conjunction with an amateur transceiver
 |  | A Class C high efficiency amplifier
 |  | An amplifier used as a frequency multiplier
 | G7B14 ~ Which of the following describes a linear amplifier? | 
 | A. | Any RF power amplifier used in conjunction with an amateur transceiver
 | B. | An amplifier in which the output preserves the input waveform
 | C. | A Class C high efficiency amplifier
 | D. | An amplifier used as a frequency multiplier
Practical Circuits
Group G7B

## Slide 366
G7C01
G7C02
G7C03
G7C04
G7C05
G7C06
G7C07
G7C08
G7C09
G7C10
G7C11
Practical Circuits
Group G7C (11 Questions)
Receivers and transmitters; filters, oscillators
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 367
 | G7C01 ~ Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters? | 
 |  | Carrier oscillator
 |  | Filter
 |  | IF amplifier
 |  | RF amplifier
 | G7C01 ~ Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters? | 
 |  | Carrier oscillator
 |  | IF amplifier
 |  | RF amplifier
 | G7C01 ~ Which of the following is used to process signals from the balanced modulator then send them to the mixer in some single sideband phone transmitters? | 
 | A. | Carrier oscillator
 | B. | Filter
 | C. | IF amplifier
 | D. | RF amplifier
Practical Circuits
Group G7C

## Slide 368
 | G7C02 ~ Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters? | 
 |  | Discriminator
 |  | Detector
 |  | IF amplifier
 |  | Balanced modulator
 | G7C02 ~ Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters? | 
 |  | Discriminator
 |  | Detector
 |  | IF amplifier
 | G7C02 ~ Which circuit is used to combine signals from the carrier oscillator and speech amplifier then send the result to the filter in some single sideband phone transmitters? | 
 | A. | Discriminator
 | B. | Detector
 | C. | IF amplifier
 | D. | Balanced modulator
Practical Circuits
Group G7C

## Slide 369
 | G7C03 ~ What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver? | 
 |  | Balanced modulator
 |  | IF amplifier
 |  | Mixer
 |  | Detector
 | G7C03 ~ What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver? | 
 |  | Balanced modulator
 |  | IF amplifier
 |  | Detector
 | G7C03 ~ What circuit is used to process signals from the RF amplifier and local oscillator then send the result to the IF filter in a superheterodyne receiver? | 
 | A. | Balanced modulator
 | B. | IF amplifier
 | C. | Mixer
 | D. | Detector
Practical Circuits
Group G7C

## Slide 370
 | G7C04 ~ What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers? | 
 |  | RF oscillator
 |  | IF filter
 |  | Balanced modulator
 |  | Product detector
 | G7C04 ~ What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers? | 
 |  | RF oscillator
 |  | IF filter
 |  | Balanced modulator
 | G7C04 ~ What circuit is used to combine signals from the IF amplifier and BFO and send the result to the AF amplifier in some single sideband receivers? | 
 | A. | RF oscillator
 | B. | IF filter
 | C. | Balanced modulator
 | D. | Product detector
Practical Circuits
Group G7C

## Slide 371
 | G7C05 ~ Which of the following is an advantage of a transceiver controlled by a direct digital synthesizer (DDS)? | 
 |  | Wide tuning range and no need for band switching
 |  | Relatively high power output
 |  | Relatively low power consumption
 |  | Variable frequency with the stability of a crystal oscillator
 | G7C05 ~ Which of the following is an advantage of a transceiver controlled by a direct digital synthesizer (DDS)? | 
 |  | Wide tuning range and no need for band switching
 |  | Relatively high power output
 |  | Relatively low power consumption
 | G7C05 ~ Which of the following is an advantage of a transceiver controlled by a direct digital synthesizer (DDS)? | 
 | A. | Wide tuning range and no need for band switching
 | B. | Relatively high power output
 | C. | Relatively low power consumption
 | D. | Variable frequency with the stability of a crystal oscillator
Practical Circuits
Group G7C

## Slide 372
 | G7C06 ~ What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted? | 
 |  | Substantially higher
 |  | About the same
 |  | Substantially lower
 |  | Twice the transmission line impedance
 | G7C06 ~ What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted? | 
 |  | Substantially higher
 |  | Substantially lower
 |  | Twice the transmission line impedance
 | G7C06 ~ What should be the impedance of a low-pass filter as compared to the impedance of the transmission line into which it is inserted? | 
 | A. | Substantially higher
 | B. | About the same
 | C. | Substantially lower
 | D. | Twice the transmission line impedance
Practical Circuits
Group G7C

## Slide 373
 | G7C07 ~ What is the simplest combination of stages that implement a superheterodyne receiver? | 
 |  | RF amplifier, detector, audio amplifier
 |  | RF amplifier, mixer, IF discriminator
 |  | HF oscillator, mixer, detector
 |  | HF oscillator, prescaler, audio amplifier
 | G7C07 ~ What is the simplest combination of stages that implement a superheterodyne receiver? | 
 |  | RF amplifier, detector, audio amplifier
 |  | RF amplifier, mixer, IF discriminator
 |  | HF oscillator, prescaler, audio amplifier
 | G7C07 ~ What is the simplest combination of stages that implement a superheterodyne receiver? | 
 | A. | RF amplifier, detector, audio amplifier
 | B. | RF amplifier, mixer, IF discriminator
 | C. | HF oscillator, mixer, detector
 | D. | HF oscillator, prescaler, audio amplifier
Practical Circuits
Group G7C

## Slide 374
 | G7C08 ~ What type of circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio? | 
 |  | Product detector
 |  | Phase inverter
 |  | Mixer
 |  | Discriminator
 | G7C08 ~ What type of circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio? | 
 |  | Product detector
 |  | Phase inverter
 |  | Mixer
 | G7C08 ~ What type of circuit is used in many FM receivers to convert signals coming from the IF amplifier to audio? | 
 | A. | Product detector
 | B. | Phase inverter
 | C. | Mixer
 | D. | Discriminator
Practical Circuits
Group G7C

## Slide 375
 | G7C09 ~ Which of the following is needed for a Digital Signal Processor IF filter? | 
 |  | An analog to digital converter
 |  | A digital to analog converter
 |  | A digital processor chip
 |  | All of the these choices are correct
 | G7C09 ~ Which of the following is needed for a Digital Signal Processor IF filter? | 
 |  | An analog to digital converter
 |  | A digital to analog converter
 |  | A digital processor chip
 | G7C09 ~ Which of the following is needed for a Digital Signal Processor IF filter? | 
 | A. | An analog to digital converter
 | B. | A digital to analog converter
 | C. | A digital processor chip
 | D. | All of the these choices are correct
Practical Circuits
Group G7C

## Slide 376
 | G7C10 ~ How is Digital Signal Processor filtering accomplished? | 
 |  | By using direct signal phasing
 |  | By converting the signal from analog to digital and using digital processing
 |  | By differential spurious phasing
 |  | By converting the signal from digital to analog and taking the difference of mixing products
 | G7C10 ~ How is Digital Signal Processor filtering accomplished? | 
 |  | By using direct signal phasing
 |  | By differential spurious phasing
 |  | By converting the signal from digital to analog and taking the difference of mixing products
 | G7C10 ~ How is Digital Signal Processor filtering accomplished? | 
 | A. | By using direct signal phasing
 | B. | By converting the signal from analog to digital and using digital processing
 | C. | By differential spurious phasing
 | D. | By converting the signal from digital to analog and taking the difference of mixing products
Practical Circuits
Group G7C

## Slide 377
 | G7C11 ~ What is meant by the term "software defined radio" (SDR)? | 
 |  | A radio in which most major signal processing functions are performed by software
 |  | A radio that provides computer interface for automatic logging of band and frequency
 |  | A radio that uses crystal filters designed using software
 |  | A computer model that can simulate performance of a radio to aid in the design process
 | G7C11 ~ What is meant by the term "software defined radio" (SDR)? | 
 |  | A radio that provides computer interface for automatic logging of band and frequency
 |  | A radio that uses crystal filters designed using software
 |  | A computer model that can simulate performance of a radio to aid in the design process
 | G7C11 ~ What is meant by the term "software defined radio" (SDR)? | 
 | A. | A radio in which most major signal processing functions are performed by software
 | B. | A radio that provides computer interface for automatic logging of band and frequency
 | C. | A radio that uses crystal filters designed using software
 | D. | A computer model that can simulate performance of a radio to aid in the design process
Practical Circuits
Group G7C

## Slide 378
Group |  | Questions
G8A | Carriers and modulation: AM; FM; single sideband; modulation envelope; digital modulation; overmodulation | 11
G8B | Frequency mixing; multiplication; bandwidths of various modes; deviation; duty cycle | 10
G8C | Digital emission modes | 11
3 | Total | 32
Subelement G8 Signals and Emissions
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 379
G8A01
G8A02
G8A03
G8A04
G8A05
G8A06
G8A07
G8A08
G8A09
G8A10
G8A11
Signals and Emissions
Group G8A (11 Questions)
Carriers and modulation: AM; FM; single sideband; modulation envelope; digital modulation; overmodulation
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 380
 | G8A01 ~ How is an FSK signal generated? | 
 |  | By keying an FM transmitter with a sub-audible tone
 |  | By changing an oscillator's frequency directly with a digital control signal
 |  | By using a transceiver's computer data interface protocol to change frequencies
 |  | By reconfiguring the CW keying input to act as a tone generator
 | G8A01 ~ How is an FSK signal generated? | 
 |  | By keying an FM transmitter with a sub-audible tone
 |  | By using a transceiver's computer data interface protocol to change frequencies
 |  | By reconfiguring the CW keying input to act as a tone generator
 | G8A01 ~ How is an FSK signal generated? | 
 | A. | By keying an FM transmitter with a sub-audible tone
 | B. | By changing an oscillator's frequency directly with a digital control signal
 | C. | By using a transceiver's computer data interface protocol to change frequencies
 | D. | By reconfiguring the CW keying input to act as a tone generator
Signals and Emissions
Group G8A

## Slide 381
 | G8A02 ~ What is the name of the process that changes the phase angle of an RF wave to convey information? | 
 |  | Phase convolution
 |  | Phase modulation
 |  | Angle convolution
 |  | Radian inversion
 | G8A02 ~ What is the name of the process that changes the phase angle of an RF wave to convey information? | 
 |  | Phase convolution
 |  | Angle convolution
 |  | Radian inversion
 | G8A02 ~ What is the name of the process that changes the phase angle of an RF wave to convey information? | 
 | A. | Phase convolution
 | B. | Phase modulation
 | C. | Angle convolution
 | D. | Radian inversion
Signals and Emissions
Group G8A

## Slide 382
 | G8A03 ~ What is the name of the process that changes the instantaneous frequency of an RF wave to convey information? | 
 |  | Frequency convolution
 |  | Frequency transformation
 |  | Frequency conversion
 |  | Frequency modulation
 | G8A03 ~ What is the name of the process that changes the instantaneous frequency of an RF wave to convey information? | 
 |  | Frequency convolution
 |  | Frequency transformation
 |  | Frequency conversion
 | G8A03 ~ What is the name of the process that changes the instantaneous frequency of an RF wave to convey information? | 
 | A. | Frequency convolution
 | B. | Frequency transformation
 | C. | Frequency conversion
 | D. | Frequency modulation
Signals and Emissions
Group G8A

## Slide 383
 | G8A04 ~ What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage? | 
 |  | Multiplex modulation
 |  | Phase modulation
 |  | Amplitude modulation
 |  | Pulse modulation
 | G8A04 ~ What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage? | 
 |  | Multiplex modulation
 |  | Amplitude modulation
 |  | Pulse modulation
 | G8A04 ~ What emission is produced by a reactance modulator connected to a transmitter RF amplifier stage? | 
 | A. | Multiplex modulation
 | B. | Phase modulation
 | C. | Amplitude modulation
 | D. | Pulse modulation
Signals and Emissions
Group G8A

## Slide 384
 | G8A05 ~ What type of modulation varies the instantaneous power level of the RF signal? | 
 |  | Frequency shift keying
 |  | Phase modulation
 |  | Frequency modulation
 |  | Amplitude modulation
 | G8A05 ~ What type of modulation varies the instantaneous power level of the RF signal? | 
 |  | Frequency shift keying
 |  | Phase modulation
 |  | Frequency modulation
 | G8A05 ~ What type of modulation varies the instantaneous power level of the RF signal? | 
 | A. | Frequency shift keying
 | B. | Phase modulation
 | C. | Frequency modulation
 | D. | Amplitude modulation
Signals and Emissions
Group G8A

## Slide 385
 | G8A06 ~ What is one advantage of carrier suppression in a single sideband phone transmission versus full carrier amplitude modulation? | 
 |  | Audio fidelity is improved
 |  | Greater modulation percentage is obtainable with lower distortion
 |  | Available transmitter power can be used more effectively
 |  | Simpler receiving equipment can be used
 | G8A06 ~ What is one advantage of carrier suppression in a single sideband phone transmission versus full carrier amplitude modulation? | 
 |  | Audio fidelity is improved
 |  | Greater modulation percentage is obtainable with lower distortion
 |  | Simpler receiving equipment can be used
 | G8A06 ~ What is one advantage of carrier suppression in a single sideband phone transmission versus full carrier amplitude modulation? | 
 | A. | Audio fidelity is improved
 | B. | Greater modulation percentage is obtainable with lower distortion
 | C. | Available transmitter power can be used more effectively
 | D. | Simpler receiving equipment can be used
Signals and Emissions
Group G8A

## Slide 386
 | G8A07 ~ Which of the following phone emissions uses the narrowest bandwidth? | 
 |  | Single sideband
 |  | Double sideband
 |  | Phase modulation
 |  | Frequency modulation
 | G8A07 ~ Which of the following phone emissions uses the narrowest bandwidth? | 
 |  | Double sideband
 |  | Phase modulation
 |  | Frequency modulation
 | G8A07 ~ Which of the following phone emissions uses the narrowest bandwidth? | 
 | A. | Single sideband
 | B. | Double sideband
 | C. | Phase modulation
 | D. | Frequency modulation
Signals and Emissions
Group G8A

## Slide 387
 | G8A08 ~ Which of the following is an effect of overmodulation? | 
 |  | Insufficient audio
 |  | Insufficient bandwidth
 |  | Frequency drift
 |  | Excessive bandwidth
 | G8A08 ~ Which of the following is an effect of overmodulation? | 
 |  | Insufficient audio
 |  | Insufficient bandwidth
 |  | Frequency drift
 | G8A08 ~ Which of the following is an effect of overmodulation? | 
 | A. | Insufficient audio
 | B. | Insufficient bandwidth
 | C. | Frequency drift
 | D. | Excessive bandwidth
Signals and Emissions
Group G8A

## Slide 388
 | G8A09 ~ What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver? | 
 |  | The RF clipping level
 |  | Transmit audio or microphone gain
 |  | Antenna inductance or capacitance
 |  | Attenuator level
 | G8A09 ~ What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver? | 
 |  | The RF clipping level
 |  | Antenna inductance or capacitance
 |  | Attenuator level
 | G8A09 ~ What control is typically adjusted for proper ALC setting on an amateur single sideband transceiver? | 
 | A. | The RF clipping level
 | B. | Transmit audio or microphone gain
 | C. | Antenna inductance or capacitance
 | D. | Attenuator level
Signals and Emissions
Group G8A

## Slide 389
 | G8A10 ~ What is meant by the term flat-topping when referring to a single sideband phone transmission? | 
 |  | Signal distortion caused by insufficient collector current
 |  | The transmitter's automatic level control (ALC) is properly adjusted
 |  | Signal distortion caused by excessive drive
 |  | The transmitter's carrier is properly suppressed
 | G8A10 ~ What is meant by the term flat-topping when referring to a single sideband phone transmission? | 
 |  | Signal distortion caused by insufficient collector current
 |  | The transmitter's automatic level control (ALC) is properly adjusted
 |  | The transmitter's carrier is properly suppressed
 | G8A10 ~ What is meant by the term flat-topping when referring to a single sideband phone transmission? | 
 | A. | Signal distortion caused by insufficient collector current
 | B. | The transmitter's automatic level control (ALC) is properly adjusted
 | C. | Signal distortion caused by excessive drive
 | D. | The transmitter's carrier is properly suppressed
Signals and Emissions
Group G8A

## Slide 390
 | G8A11 ~ What is the modulation envelope of an AM signal? | 
 |  | The waveform created by connecting the peak values of the modulated signal
 |  | The carrier frequency that contains the signal
 |  | Spurious signals that envelop nearby frequencies
 |  | The bandwidth of the modulated signal
 | G8A11 ~ What is the modulation envelope of an AM signal? | 
 |  | The carrier frequency that contains the signal
 |  | Spurious signals that envelop nearby frequencies
 |  | The bandwidth of the modulated signal
 | G8A11 ~ What is the modulation envelope of an AM signal? | 
 | A. | The waveform created by connecting the peak values of the modulated signal
 | B. | The carrier frequency that contains the signal
 | C. | Spurious signals that envelop nearby frequencies
 | D. | The bandwidth of the modulated signal
Signals and Emissions
Group G8A

## Slide 391
G8B01
G8B02
G8B03
G8B04
G8B05
G8B06
G8B07
G8B08
G8B09
G8B10
Signals and Emissions
Group G8B (10 Questions)
Frequency mixing; multiplication; bandwidths of various modes; deviation; duty cycle
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 392
 | G8B01 ~ What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal? | 
 |  | Mixer
 |  | BFO
 |  | VFO
 |  | Discriminator
 | G8B01 ~ What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal? | 
 |  | BFO
 |  | VFO
 |  | Discriminator
 | G8B01 ~ What receiver stage combines a 14.250 MHz input signal with a 13.795 MHz oscillator signal to produce a 455 kHz intermediate frequency (IF) signal? | 
 | A. | Mixer
 | B. | BFO
 | C. | VFO
 | D. | Discriminator
Signals and Emissions
Group G8B

## Slide 393
 | G8B02 ~ If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, what type of interference will a 13.345 MHz signal produce in the receiver? | 
 |  | Quadrature noise
 |  | Image response
 |  | Mixer interference
 |  | Intermediate interference
 | G8B02 ~ If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, what type of interference will a 13.345 MHz signal produce in the receiver? | 
 |  | Quadrature noise
 |  | Mixer interference
 |  | Intermediate interference
 | G8B02 ~ If a receiver mixes a 13.800 MHz VFO with a 14.255 MHz received signal to produce a 455 kHz intermediate frequency (IF) signal, what type of interference will a 13.345 MHz signal produce in the receiver? | 
 | A. | Quadrature noise
 | B. | Image response
 | C. | Mixer interference
 | D. | Intermediate interference
Signals and Emissions
Group G8B

## Slide 394
 | G8B03 ~ What is another term for the mixing of two RF signals? | 
 |  | Heterodyning
 |  | Synthesizing
 |  | Cancellation
 |  | Phase inverting
 | G8B03 ~ What is another term for the mixing of two RF signals? | 
 |  | Synthesizing
 |  | Cancellation
 |  | Phase inverting
 | G8B03 ~ What is another term for the mixing of two RF signals? | 
 | A. | Heterodyning
 | B. | Synthesizing
 | C. | Cancellation
 | D. | Phase inverting
Signals and Emissions
Group G8B

## Slide 395
 | G8B04 ~ What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency? | 
 |  | Mixer
 |  | Reactance modulator
 |  | Pre-emphasis network
 |  | Multiplier
 | G8B04 ~ What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency? | 
 |  | Mixer
 |  | Reactance modulator
 |  | Pre-emphasis network
 | G8B04 ~ What is the stage in a VHF FM transmitter that generates a harmonic of a lower frequency signal to reach the desired operating frequency? | 
 | A. | Mixer
 | B. | Reactance modulator
 | C. | Pre-emphasis network
 | D. | Multiplier
Signals and Emissions
Group G8B

## Slide 396
 | G8B05 ~ What is the approximate bandwidth of a PACTOR3 signal at maximum data rate? | 
 |  | 31.5 Hz
 |  | 500 Hz
 |  | 1800 Hz
 |  | 2300 Hz
 | G8B05 ~ What is the approximate bandwidth of a PACTOR3 signal at maximum data rate? | 
 |  | 31.5 Hz
 |  | 500 Hz
 |  | 1800 Hz
 | G8B05 ~ What is the approximate bandwidth of a PACTOR3 signal at maximum data rate? | 
 | A. | 31.5 Hz
 | B. | 500 Hz
 | C. | 1800 Hz
 | D. | 2300 Hz
Signals and Emissions
Group G8B

## Slide 397
 | G8B06 ~ What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency? | 
 |  | 3 kHz
 |  | 5 kHz
 |  | 8 kHz
 |  | 16 kHz
 | G8B06 ~ What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency? | 
 |  | 3 kHz
 |  | 5 kHz
 |  | 8 kHz
 | G8B06 ~ What is the total bandwidth of an FM phone transmission having 5 kHz deviation and 3 kHz modulating frequency? | 
 | A. | 3 kHz
 | B. | 5 kHz
 | C. | 8 kHz
 | D. | 16 kHz
Signals and Emissions
Group G8B

## Slide 398
 | G8B07 ~ What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter? | 
 |  | 101.75 Hz
 |  | 416.7 Hz
 |  | 5 kHz
 |  | 60 kHz
 | G8B07 ~ What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter? | 
 |  | 101.75 Hz
 |  | 5 kHz
 |  | 60 kHz
 | G8B07 ~ What is the frequency deviation for a 12.21 MHz reactance modulated oscillator in a 5 kHz deviation, 146.52 MHz FM phone transmitter? | 
 | A. | 101.75 Hz
 | B. | 416.7 Hz
 | C. | 5 kHz
 | D. | 60 kHz
Signals and Emissions
Group G8B

## Slide 399
 | G8B08 ~ Why is it important to know the duty cycle of the mode you are using when transmitting? | 
 |  | To aid in tuning your transmitter
 |  | Some modes have high duty cycles which could exceed the transmitter's average power rating.
 |  | To allow time for the other station to break in during a transmission
 |  | All of these choices are correct
 | G8B08 ~ Why is it important to know the duty cycle of the mode you are using when transmitting? | 
 |  | To aid in tuning your transmitter
 |  | To allow time for the other station to break in during a transmission
 |  | All of these choices are correct
 | G8B08 ~ Why is it important to know the duty cycle of the mode you are using when transmitting? | 
 | A. | To aid in tuning your transmitter
 | B. | Some modes have high duty cycles which could exceed the transmitter's average power rating.
 | C. | To allow time for the other station to break in during a transmission
 | D. | All of these choices are correct
Signals and Emissions
Group G8B

## Slide 400
 | G8B09 ~ Why is it good to match receiver bandwidth to the bandwidth of the operating mode? | 
 |  | It is required by FCC rules
 |  | It minimizes power consumption in the receiver
 |  | It improves impedance matching of the antenna
 |  | It results in the best signal to noise ratio
 | G8B09 ~ Why is it good to match receiver bandwidth to the bandwidth of the operating mode? | 
 |  | It is required by FCC rules
 |  | It minimizes power consumption in the receiver
 |  | It improves impedance matching of the antenna
 | G8B09 ~ Why is it good to match receiver bandwidth to the bandwidth of the operating mode? | 
 | A. | It is required by FCC rules
 | B. | It minimizes power consumption in the receiver
 | C. | It improves impedance matching of the antenna
 | D. | It results in the best signal to noise ratio
Signals and Emissions
Group G8B

## Slide 401
 | G8B10 ~ What is the relationship between transmitted symbol rate and bandwidth? | 
 |  | Symbol rate and bandwidth are not related
 |  | Higher symbol rates require wider bandwidth
 |  | Lower symbol rates require wider bandwidth
 |  | Bandwidth is always half the symbol rate
 | G8B10 ~ What is the relationship between transmitted symbol rate and bandwidth? | 
 |  | Symbol rate and bandwidth are not related
 |  | Lower symbol rates require wider bandwidth
 |  | Bandwidth is always half the symbol rate
 | G8B10 ~ What is the relationship between transmitted symbol rate and bandwidth? | 
 | A. | Symbol rate and bandwidth are not related
 | B. | Higher symbol rates require wider bandwidth
 | C. | Lower symbol rates require wider bandwidth
 | D. | Bandwidth is always half the symbol rate
Signals and Emissions
Group G8B

## Slide 402
G8C01
G8C03
G8C04
G8C05
G8C06
G8C07
G8C08
G8C09
G8C10
G8C11
G8C12
Signals and Emissions
Group G8C (11 Questions)
Digital emission modes
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 403
 | G8C01 ~ Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands? | 
 |  | FSK441 and Hellschreiber
 |  | JT9 and JT65
 |  | Clover
 |  | RTTY
 | G8C01 ~ Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands? | 
 |  | FSK441 and Hellschreiber
 |  | Clover
 |  | RTTY
 | G8C01 ~ Which of the following digital modes is designed to operate at extremely low signal strength on the HF bands? | 
 | A. | FSK441 and Hellschreiber
 | B. | JT9 and JT65
 | C. | Clover
 | D. | RTTY
Signals and Emissions
Group G8C

## Slide 404
 | G8C03 ~ What part of a data packet contains the routing and handling information? | 
 |  | Directory
 |  | Preamble
 |  | Header
 |  | Footer
 | G8C03 ~ What part of a data packet contains the routing and handling information? | 
 |  | Directory
 |  | Preamble
 |  | Footer
 | G8C03 ~ What part of a data packet contains the routing and handling information? | 
 | A. | Directory
 | B. | Preamble
 | C. | Header
 | D. | Footer
Signals and Emissions
Group G8C

## Slide 405
 | G8C04 ~ Which of the following describes Baudot code? | 
 |  | A 7-bit code with start, stop and parity bits
 |  | A code using error detection and correction
 |  | A 5-bit code with additional start and stop bits
 |  | A code using SELCAL and LISTEN
 | G8C04 ~ Which of the following describes Baudot code? | 
 |  | A 7-bit code with start, stop and parity bits
 |  | A code using error detection and correction
 |  | A code using SELCAL and LISTEN
 | G8C04 ~ Which of the following describes Baudot code? | 
 | A. | A 7-bit code with start, stop and parity bits
 | B. | A code using error detection and correction
 | C. | A 5-bit code with additional start and stop bits
 | D. | A code using SELCAL and LISTEN
Signals and Emissions
Group G8C

## Slide 406
 | G8C05 ~ In the PACTOR protocol, what is meant by an NAK response to a transmitted packet? | 
 |  | The receiver is requesting the packet be retransmitted
 |  | The receiver is reporting the packet was received without error
 |  | The receiver is busy decoding the packet
 |  | The entire file has been received correctly
 | G8C05 ~ In the PACTOR protocol, what is meant by an NAK response to a transmitted packet? | 
 |  | The receiver is reporting the packet was received without error
 |  | The receiver is busy decoding the packet
 |  | The entire file has been received correctly
 | G8C05 ~ In the PACTOR protocol, what is meant by an NAK response to a transmitted packet? | 
 | A. | The receiver is requesting the packet be retransmitted
 | B. | The receiver is reporting the packet was received without error
 | C. | The receiver is busy decoding the packet
 | D. | The entire file has been received correctly
Signals and Emissions
Group G8C

## Slide 407
 | G8C06 ~ What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR? | 
 |  | The checksum overflows
 |  | The connection is dropped
 |  | Packets will be routed incorrectly
 |  | Encoding reverts to the default character set
 | G8C06 ~ What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR? | 
 |  | The checksum overflows
 |  | Packets will be routed incorrectly
 |  | Encoding reverts to the default character set
 | G8C06 ~ What action results from a failure to exchange information due to excessive transmission attempts when using PACTOR or WINMOR? | 
 | A. | The checksum overflows
 | B. | The connection is dropped
 | C. | Packets will be routed incorrectly
 | D. | Encoding reverts to the default character set
Signals and Emissions
Group G8C

## Slide 408
 | G8C07 ~ How does the receiving station respond to an ARQ data mode packet containing errors? | 
 |  | It terminates the contact
 |  | It requests the packet be retransmitted
 |  | It sends the packet back to the transmitting station
 |  | It requests a change in transmitting protocol
 | G8C07 ~ How does the receiving station respond to an ARQ data mode packet containing errors? | 
 |  | It terminates the contact
 |  | It sends the packet back to the transmitting station
 |  | It requests a change in transmitting protocol
 | G8C07 ~ How does the receiving station respond to an ARQ data mode packet containing errors? | 
 | A. | It terminates the contact
 | B. | It requests the packet be retransmitted
 | C. | It sends the packet back to the transmitting station
 | D. | It requests a change in transmitting protocol
Signals and Emissions
Group G8C

## Slide 409
 | G8C08 ~ Which of the following statements is true about PSK31? | 
 |  | Upper case letters make the signal stronger
 |  | Upper case letters use longer Varicode signals and thus slow down transmission
 |  | Varicode Error Correction is used to ensure accurate message reception
 |  | Higher power is needed as compared to RTTY for similar error rates
 | G8C08 ~ Which of the following statements is true about PSK31? | 
 |  | Upper case letters make the signal stronger
 |  | Varicode Error Correction is used to ensure accurate message reception
 |  | Higher power is needed as compared to RTTY for similar error rates
 | G8C08 ~ Which of the following statements is true about PSK31? | 
 | A. | Upper case letters make the signal stronger
 | B. | Upper case letters use longer Varicode signals and thus slow down transmission
 | C. | Varicode Error Correction is used to ensure accurate message reception
 | D. | Higher power is needed as compared to RTTY for similar error rates
Signals and Emissions
Group G8C

## Slide 410
 | G8C09 ~ What does the number 31 represent in "PSK31"? | 
 |  | The approximate transmitted symbol rate
 |  | The version of the PSK protocol
 |  | The year in which PSK31 was invented
 |  | The number of characters that can be represented by PSK31
 | G8C09 ~ What does the number 31 represent in "PSK31"? | 
 |  | The version of the PSK protocol
 |  | The year in which PSK31 was invented
 |  | The number of characters that can be represented by PSK31
 | G8C09 ~ What does the number 31 represent in "PSK31"? | 
 | A. | The approximate transmitted symbol rate
 | B. | The version of the PSK protocol
 | C. | The year in which PSK31 was invented
 | D. | The number of characters that can be represented by PSK31
Signals and Emissions
Group G8C

## Slide 411
 | G8C10 ~ How does forward error correction (FEC) allow the receiver to correct errors in received data packets? | 
 |  | By controlling transmitter output power for optimum signal strength
 |  | By using the varicode character set
 |  | By transmitting redundant information with the data
 |  | By using a parity bit with each character
 | G8C10 ~ How does forward error correction (FEC) allow the receiver to correct errors in received data packets? | 
 |  | By controlling transmitter output power for optimum signal strength
 |  | By using the varicode character set
 |  | By using a parity bit with each character
 | G8C10 ~ How does forward error correction (FEC) allow the receiver to correct errors in received data packets? | 
 | A. | By controlling transmitter output power for optimum signal strength
 | B. | By using the varicode character set
 | C. | By transmitting redundant information with the data
 | D. | By using a parity bit with each character
Signals and Emissions
Group G8C

## Slide 412
 | G8C11 ~ How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified? | 
 |  | Dot and Dash
 |  | On and Off
 |  | High and Low
 |  | Mark and Space
 | G8C11 ~ How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified? | 
 |  | Dot and Dash
 |  | On and Off
 |  | High and Low
 | G8C11 ~ How are the two separate frequencies of a Frequency Shift Keyed (FSK) signal identified? | 
 | A. | Dot and Dash
 | B. | On and Off
 | C. | High and Low
 | D. | Mark and Space
Signals and Emissions
Group G8C

## Slide 413
 | G8C12 ~ Which type of code is used for sending characters in a PSK31 signal? | 
 |  | Varicode
 |  | Viterbi
 |  | Volumetric
 |  | Binary
 | G8C12 ~ Which type of code is used for sending characters in a PSK31 signal? | 
 |  | Viterbi
 |  | Volumetric
 |  | Binary
 | G8C12 ~ Which type of code is used for sending characters in a PSK31 signal? | 
 | A. | Varicode
 | B. | Viterbi
 | C. | Volumetric
 | D. | Binary
Signals and Emissions
Group G8C

## Slide 414
Group |  | Questions
G9A | Antenna feed lines: characteristic impedance, and attenuation; SWR calculation, measurement and effects; matching networks | 15
G9B | Basic antennas | 12
G9C | Directional antennas | 20
G9D | Specialized antennas | 11
4 | Total | 58
Subelement G9 Antennas and Feed Lines
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 415
G9A01 | G9A15
G9A02 | 
G9A03 | 
G9A04 | 
G9A05 | 
G9A06 | 
G9A07 | 
G9A08 | 
G9A09 | 
G9A10 | 
G9A11 | 
G9A12 | 
G9A13 | 
G9A14 | 
Antennas and Feed Lines
Group G9A (15 Questions)
Antenna feed lines: characteristic impedance, and attenuation; SWR calculation, measurement and effects; matching networks
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 416
 | G9A01 ~ Which of the following factors determine the characteristic impedance of a parallel conductor antenna feed line? | 
 |  | The distance between the centers of the conductors and the radius of the conductors
 |  | The distance between the centers of the conductors and the length of the line
 |  | The radius of the conductors and the frequency of the signal
 |  | The frequency of the signal and the length of the line
 | G9A01 ~ Which of the following factors determine the characteristic impedance of a parallel conductor antenna feed line? | 
 |  | The distance between the centers of the conductors and the length of the line
 |  | The radius of the conductors and the frequency of the signal
 |  | The frequency of the signal and the length of the line
 | G9A01 ~ Which of the following factors determine the characteristic impedance of a parallel conductor antenna feed line? | 
 | A. | The distance between the centers of the conductors and the radius of the conductors
 | B. | The distance between the centers of the conductors and the length of the line
 | C. | The radius of the conductors and the frequency of the signal
 | D. | The frequency of the signal and the length of the line
Antennas and Feed Lines
Group G9A

## Slide 417
 | G9A02 ~ What are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations? | 
 |  | 25 and 30 ohms
 |  | 50 and 75 ohms
 |  | 80 and 100 ohms
 |  | 500 and 750 ohms
 | G9A02 ~ What are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations? | 
 |  | 25 and 30 ohms
 |  | 80 and 100 ohms
 |  | 500 and 750 ohms
 | G9A02 ~ What are the typical characteristic impedances of coaxial cables used for antenna feed lines at amateur stations? | 
 | A. | 25 and 30 ohms
 | B. | 50 and 75 ohms
 | C. | 80 and 100 ohms
 | D. | 500 and 750 ohms
Antennas and Feed Lines
Group G9A

## Slide 418
 | G9A03 ~ What is the characteristic impedance of flat ribbon TV type twinlead? | 
 |  | 50 ohms
 |  | 75 ohms
 |  | 100 ohms
 |  | 300 ohms
 | G9A03 ~ What is the characteristic impedance of flat ribbon TV type twinlead? | 
 |  | 50 ohms
 |  | 75 ohms
 |  | 100 ohms
 | G9A03 ~ What is the characteristic impedance of flat ribbon TV type twinlead? | 
 | A. | 50 ohms
 | B. | 75 ohms
 | C. | 100 ohms
 | D. | 300 ohms
Antennas and Feed Lines
Group G9A

## Slide 419
 | G9A04 ~ What might cause reflected power at the point where a feed line connects to an antenna? | 
 |  | Operating an antenna at its resonant frequency
 |  | Using more transmitter power than the antenna can handle
 |  | A difference between feed line impedance and antenna feed point impedance
 |  | Feeding the antenna with unbalanced feed line
 | G9A04 ~ What might cause reflected power at the point where a feed line connects to an antenna? | 
 |  | Operating an antenna at its resonant frequency
 |  | Using more transmitter power than the antenna can handle
 |  | Feeding the antenna with unbalanced feed line
 | G9A04 ~ What might cause reflected power at the point where a feed line connects to an antenna? | 
 | A. | Operating an antenna at its resonant frequency
 | B. | Using more transmitter power than the antenna can handle
 | C. | A difference between feed line impedance and antenna feed point impedance
 | D. | Feeding the antenna with unbalanced feed line
Antennas and Feed Lines
Group G9A

## Slide 420
 | G9A05 ~ How does the attenuation of coaxial cable change as the frequency of the signal it is carrying increases? | 
 |  | Attenuation is independent of frequency
 |  | Attenuation increases
 |  | Attenuation decreases
 |  | Attenuation reaches a maximum at approximately 18 MHz
 | G9A05 ~ How does the attenuation of coaxial cable change as the frequency of the signal it is carrying increases? | 
 |  | Attenuation is independent of frequency
 |  | Attenuation decreases
 |  | Attenuation reaches a maximum at approximately 18 MHz
 | G9A05 ~ How does the attenuation of coaxial cable change as the frequency of the signal it is carrying increases? | 
 | A. | Attenuation is independent of frequency
 | B. | Attenuation increases
 | C. | Attenuation decreases
 | D. | Attenuation reaches a maximum at approximately 18 MHz
Antennas and Feed Lines
Group G9A

## Slide 421
 | G9A06 ~ In what units is RF feed line loss usually expressed? | 
 |  | Ohms per 1000 feet
 |  | Decibels per 1000 feet
 |  | Ohms per 100 feet
 |  | Decibels per 100 feet
 | G9A06 ~ In what units is RF feed line loss usually expressed? | 
 |  | Ohms per 1000 feet
 |  | Decibels per 1000 feet
 |  | Ohms per 100 feet
 | G9A06 ~ In what units is RF feed line loss usually expressed? | 
 | A. | Ohms per 1000 feet
 | B. | Decibels per 1000 feet
 | C. | Ohms per 100 feet
 | D. | Decibels per 100 feet
Antennas and Feed Lines
Group G9A

## Slide 422
 | G9A07 ~ What must be done to prevent standing waves on an antenna feed line? | 
 |  | The antenna feed point must be at DC ground potential
 |  | The feed line must be cut to a length equal to an odd number of electrical quarter wavelengths
 |  | The feed line must be cut to a length equal to an even number of physical half wavelengths
 |  | The antenna feed point impedance must be matched to the characteristic impedance of the feed line
 | G9A07 ~ What must be done to prevent standing waves on an antenna feed line? | 
 |  | The antenna feed point must be at DC ground potential
 |  | The feed line must be cut to a length equal to an odd number of electrical quarter wavelengths
 |  | The feed line must be cut to a length equal to an even number of physical half wavelengths
 | G9A07 ~ What must be done to prevent standing waves on an antenna feed line? | 
 | A. | The antenna feed point must be at DC ground potential
 | B. | The feed line must be cut to a length equal to an odd number of electrical quarter wavelengths
 | C. | The feed line must be cut to a length equal to an even number of physical half wavelengths
 | D. | The antenna feed point impedance must be matched to the characteristic impedance of the feed line
Antennas and Feed Lines
Group G9A

## Slide 423
 | G9A08 ~ If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, what is the resulting SWR on the feed line? | 
 |  | 1 to 1
 |  | 5 to 1
 |  | Between 1 to 1 and 5 to 1 depending on the characteristic impedance of the line
 |  | Between 1 to 1 and 5 to 1 depending on the reflected power at the transmitter
 | G9A08 ~ If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, what is the resulting SWR on the feed line? | 
 |  | 1 to 1
 |  | Between 1 to 1 and 5 to 1 depending on the characteristic impedance of the line
 |  | Between 1 to 1 and 5 to 1 depending on the reflected power at the transmitter
 | G9A08 ~ If the SWR on an antenna feed line is 5 to 1, and a matching network at the transmitter end of the feed line is adjusted to 1 to 1 SWR, what is the resulting SWR on the feed line? | 
 | A. | 1 to 1
 | B. | 5 to 1
 | C. | Between 1 to 1 and 5 to 1 depending on the characteristic impedance of the line
 | D. | Between 1 to 1 and 5 to 1 depending on the reflected power at the transmitter
Antennas and Feed Lines
Group G9A

## Slide 424
 | G9A09 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance? | 
 |  | 4:1
 |  | 1:4
 |  | 2:1
 |  | 1:2
 | G9A09 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance? | 
 |  | 1:4
 |  | 2:1
 |  | 1:2
 | G9A09 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 200 ohm impedance? | 
 | A. | 4:1
 | B. | 1:4
 | C. | 2:1
 | D. | 1:2
Antennas and Feed Lines
Group G9A

## Slide 425
 | G9A10 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 10 ohm impedance? | 
 |  | 2:1
 |  | 50:1
 |  | 1:5
 |  | 5:1
 | G9A10 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 10 ohm impedance? | 
 |  | 2:1
 |  | 50:1
 |  | 1:5
 | G9A10 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 10 ohm impedance? | 
 | A. | 2:1
 | B. | 50:1
 | C. | 1:5
 | D. | 5:1
Antennas and Feed Lines
Group G9A

## Slide 426
 | G9A11 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 50 ohm impedance? | 
 |  | 2:1
 |  | 1:1
 |  | 50:50
 |  | 0:0
 | G9A11 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 50 ohm impedance? | 
 |  | 2:1
 |  | 50:50
 |  | 0:0
 | G9A11 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 50 ohm impedance? | 
 | A. | 2:1
 | B. | 1:1
 | C. | 50:50
 | D. | 0:0
Antennas and Feed Lines
Group G9A

## Slide 427
 | G9A12 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 25 ohm impedance? | 
 |  | 2:1
 |  | 2.5:1
 |  | 1.25:1
 |  | You cannot determine SWR from impedance values
 | G9A12 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 25 ohm impedance? | 
 |  | 2.5:1
 |  | 1.25:1
 |  | You cannot determine SWR from impedance values
 | G9A12 ~ What standing wave ratio will result when connecting a 50 ohm feed line to a non-reactive load having 25 ohm impedance? | 
 | A. | 2:1
 | B. | 2.5:1
 | C. | 1.25:1
 | D. | You cannot determine SWR from impedance values
Antennas and Feed Lines
Group G9A

## Slide 428
 | G9A13 ~ What standing wave ratio will result when connecting a 50 ohm feed line to an antenna that has a purely resistive 300 ohm feed point impedance? | 
 |  | 1.5:1
 |  | 3:1
 |  | 6:1
 |  | You cannot determine SWR from impedance values
 | G9A13 ~ What standing wave ratio will result when connecting a 50 ohm feed line to an antenna that has a purely resistive 300 ohm feed point impedance? | 
 |  | 1.5:1
 |  | 3:1
 |  | You cannot determine SWR from impedance values
 | G9A13 ~ What standing wave ratio will result when connecting a 50 ohm feed line to an antenna that has a purely resistive 300 ohm feed point impedance? | 
 | A. | 1.5:1
 | B. | 3:1
 | C. | 6:1
 | D. | You cannot determine SWR from impedance values
Antennas and Feed Lines
Group G9A

## Slide 429
 | G9A14 ~ What is the interaction between high standing wave ratio (SWR) and transmission line loss? | 
 |  | There is no interaction between transmission line loss and SWR
 |  | If a transmission line is lossy, high SWR will increase the loss
 |  | High SWR makes it difficult to measure transmission line loss
 |  | High SWR reduces the relative effect of transmission line loss
 | G9A14 ~ What is the interaction between high standing wave ratio (SWR) and transmission line loss? | 
 |  | There is no interaction between transmission line loss and SWR
 |  | High SWR makes it difficult to measure transmission line loss
 |  | High SWR reduces the relative effect of transmission line loss
 | G9A14 ~ What is the interaction between high standing wave ratio (SWR) and transmission line loss? | 
 | A. | There is no interaction between transmission line loss and SWR
 | B. | If a transmission line is lossy, high SWR will increase the loss
 | C. | High SWR makes it difficult to measure transmission line loss
 | D. | High SWR reduces the relative effect of transmission line loss
Antennas and Feed Lines
Group G9A

## Slide 430
 | G9A15 ~ What is the effect of transmission line loss on SWR measured at the input to the line? | 
 |  | The higher the transmission line loss, the more the SWR will read artificially low
 |  | The higher the transmission line loss, the more the SWR will read artificially high
 |  | The higher the transmission line loss, the more accurate the SWR measurement will be
 |  | Transmission line loss does not affect the SWR measurement
 | G9A15 ~ What is the effect of transmission line loss on SWR measured at the input to the line? | 
 |  | The higher the transmission line loss, the more the SWR will read artificially high
 |  | The higher the transmission line loss, the more accurate the SWR measurement will be
 |  | Transmission line loss does not affect the SWR measurement
 | G9A15 ~ What is the effect of transmission line loss on SWR measured at the input to the line? | 
 | A. | The higher the transmission line loss, the more the SWR will read artificially low
 | B. | The higher the transmission line loss, the more the SWR will read artificially high
 | C. | The higher the transmission line loss, the more accurate the SWR measurement will be
 | D. | Transmission line loss does not affect the SWR measurement
Antennas and Feed Lines
Group G9A

## Slide 431
G9B01
G9B02
G9B03
G9B04
G9B05
G9B06
G9B07
G9B08
G9B09
G9B10
G9B11
G9B12
Antennas and Feed Lines
Group G9B (12 Questions)
Basic antennas
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 432
 | G9B01 ~ What is one disadvantage of a directly fed random-wire HF antenna? | 
 |  | It must be longer than 1 wavelength
 |  | You may experience RF burns when touching metal objects in your station
 |  | It produces only vertically polarized radiation
 |  | It is more effective on the lower HF bands than on the higher bands
 | G9B01 ~ What is one disadvantage of a directly fed random-wire HF antenna? | 
 |  | It must be longer than 1 wavelength
 |  | It produces only vertically polarized radiation
 |  | It is more effective on the lower HF bands than on the higher bands
 | G9B01 ~ What is one disadvantage of a directly fed random-wire HF antenna? | 
 | A. | It must be longer than 1 wavelength
 | B. | You may experience RF burns when touching metal objects in your station
 | C. | It produces only vertically polarized radiation
 | D. | It is more effective on the lower HF bands than on the higher bands
Antennas and Feed Lines
Group G9B

## Slide 433
 | G9B02 ~ Which of the following is a common way to adjust the feed point impedance of a quarter wave ground plane vertical antenna to be approximately 50 ohms? | 
 |  | Slope the radials upward
 |  | Slope the radials downward
 |  | Lengthen the radials
 |  | Shorten the radials
 | G9B02 ~ Which of the following is a common way to adjust the feed point impedance of a quarter wave ground plane vertical antenna to be approximately 50 ohms? | 
 |  | Slope the radials upward
 |  | Lengthen the radials
 |  | Shorten the radials
 | G9B02 ~ Which of the following is a common way to adjust the feed point impedance of a quarter wave ground plane vertical antenna to be approximately 50 ohms? | 
 | A. | Slope the radials upward
 | B. | Slope the radials downward
 | C. | Lengthen the radials
 | D. | Shorten the radials
Antennas and Feed Lines
Group G9B

## Slide 434
 | G9B03 ~ What happens to the feed point impedance of a ground plane antenna when its radials are changed from horizontal to sloping downward? | 
 |  | It decreases
 |  | It increases
 |  | It stays the same
 |  | It reaches a maximum at an angle of 45 degrees
 | G9B03 ~ What happens to the feed point impedance of a ground plane antenna when its radials are changed from horizontal to sloping downward? | 
 |  | It decreases
 |  | It stays the same
 |  | It reaches a maximum at an angle of 45 degrees
 | G9B03 ~ What happens to the feed point impedance of a ground plane antenna when its radials are changed from horizontal to sloping downward? | 
 | A. | It decreases
 | B. | It increases
 | C. | It stays the same
 | D. | It reaches a maximum at an angle of 45 degrees
Antennas and Feed Lines
Group G9B

## Slide 435
 | G9B04 ~ What is the radiation pattern of a dipole antenna in free space in the plane of the conductor? | 
 |  | It is a figure-eight at right angles to the antenna
 |  | It is a figure-eight off both ends of the antenna
 |  | It is a circle (equal radiation in all directions)
 |  | It has a pair of lobes on one side of the antenna and a single lobe on the other side
 | G9B04 ~ What is the radiation pattern of a dipole antenna in free space in the plane of the conductor? | 
 |  | It is a figure-eight off both ends of the antenna
 |  | It is a circle (equal radiation in all directions)
 |  | It has a pair of lobes on one side of the antenna and a single lobe on the other side
 | G9B04 ~ What is the radiation pattern of a dipole antenna in free space in the plane of the conductor? | 
 | A. | It is a figure-eight at right angles to the antenna
 | B. | It is a figure-eight off both ends of the antenna
 | C. | It is a circle (equal radiation in all directions)
 | D. | It has a pair of lobes on one side of the antenna and a single lobe on the other side
Antennas and Feed Lines
Group G9B

## Slide 436
 | G9B05 ~ How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna? | 
 |  | If the antenna is too high, the pattern becomes unpredictable
 |  | Antenna height has no effect on the pattern
 |  | If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional
 |  | If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated
 | G9B05 ~ How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna? | 
 |  | If the antenna is too high, the pattern becomes unpredictable
 |  | Antenna height has no effect on the pattern
 |  | If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated
 | G9B05 ~ How does antenna height affect the horizontal (azimuthal) radiation pattern of a horizontal dipole HF antenna? | 
 | A. | If the antenna is too high, the pattern becomes unpredictable
 | B. | Antenna height has no effect on the pattern
 | C. | If the antenna is less than 1/2 wavelength high, the azimuthal pattern is almost omnidirectional
 | D. | If the antenna is less than 1/2 wavelength high, radiation off the ends of the wire is eliminated
Antennas and Feed Lines
Group G9B

## Slide 437
 | G9B06 ~ Where should the radial wires of a ground-mounted vertical antenna system be placed? | 
 |  | As high as possible above the ground
 |  | Parallel to the antenna element
 |  | On the surface of the Earth or buried a few inches below the ground
 |  | At the center of the antenna
 | G9B06 ~ Where should the radial wires of a ground-mounted vertical antenna system be placed? | 
 |  | As high as possible above the ground
 |  | Parallel to the antenna element
 |  | At the center of the antenna
 | G9B06 ~ Where should the radial wires of a ground-mounted vertical antenna system be placed? | 
 | A. | As high as possible above the ground
 | B. | Parallel to the antenna element
 | C. | On the surface of the Earth or buried a few inches below the ground
 | D. | At the center of the antenna
Antennas and Feed Lines
Group G9B

## Slide 438
 | G9B07 ~ How does the feed point impedance of a 1/2 wave dipole antenna change as the antenna is lowered below 1/4 wave above ground? | 
 |  | It steadily increases
 |  | It steadily decreases
 |  | It peaks at about 1/8 wavelength above ground
 |  | It is unaffected by the height above ground
 | G9B07 ~ How does the feed point impedance of a 1/2 wave dipole antenna change as the antenna is lowered below 1/4 wave above ground? | 
 |  | It steadily increases
 |  | It peaks at about 1/8 wavelength above ground
 |  | It is unaffected by the height above ground
 | G9B07 ~ How does the feed point impedance of a 1/2 wave dipole antenna change as the antenna is lowered below 1/4 wave above ground? | 
 | A. | It steadily increases
 | B. | It steadily decreases
 | C. | It peaks at about 1/8 wavelength above ground
 | D. | It is unaffected by the height above ground
Antennas and Feed Lines
Group G9B

## Slide 439
 | G9B08 ~ How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends? | 
 |  | It steadily increases
 |  | It steadily decreases
 |  | It peaks at about 1/8 wavelength from the end
 |  | It is unaffected by the location of the feed point
 | G9B08 ~ How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends? | 
 |  | It steadily decreases
 |  | It peaks at about 1/8 wavelength from the end
 |  | It is unaffected by the location of the feed point
 | G9B08 ~ How does the feed point impedance of a 1/2 wave dipole change as the feed point is moved from the center toward the ends? | 
 | A. | It steadily increases
 | B. | It steadily decreases
 | C. | It peaks at about 1/8 wavelength from the end
 | D. | It is unaffected by the location of the feed point
Antennas and Feed Lines
Group G9B

## Slide 440
 | G9B09 ~ Which of the following is an advantage of a horizontally polarized as compared to a vertically polarized HF antenna? | 
 |  | Lower ground reflection losses
 |  | Lower feed point impedance
 |  | Shorter Radials
 |  | Lower radiation resistance
 | G9B09 ~ Which of the following is an advantage of a horizontally polarized as compared to a vertically polarized HF antenna? | 
 |  | Lower feed point impedance
 |  | Shorter Radials
 |  | Lower radiation resistance
 | G9B09 ~ Which of the following is an advantage of a horizontally polarized as compared to a vertically polarized HF antenna? | 
 | A. | Lower ground reflection losses
 | B. | Lower feed point impedance
 | C. | Shorter Radials
 | D. | Lower radiation resistance
Antennas and Feed Lines
Group G9B

## Slide 441
 | G9B10 ~ What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz? | 
 |  | 8 feet
 |  | 16 feet
 |  | 24 feet
 |  | 32 feet
 | G9B10 ~ What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz? | 
 |  | 8 feet
 |  | 16 feet
 |  | 24 feet
 | G9B10 ~ What is the approximate length for a 1/2 wave dipole antenna cut for 14.250 MHz? | 
 | A. | 8 feet
 | B. | 16 feet
 | C. | 24 feet
 | D. | 32 feet
Antennas and Feed Lines
Group G9B

## Slide 442
 | G9B11 ~ What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz? | 
 |  | 42 feet
 |  | 84 feet
 |  | 131 feet
 |  | 263 feet
 | G9B11 ~ What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz? | 
 |  | 42 feet
 |  | 84 feet
 |  | 263 feet
 | G9B11 ~ What is the approximate length for a 1/2 wave dipole antenna cut for 3.550 MHz? | 
 | A. | 42 feet
 | B. | 84 feet
 | C. | 131 feet
 | D. | 263 feet
Antennas and Feed Lines
Group G9B

## Slide 443
 | G9B12 ~ What is the approximate length for a 1/4 wave vertical antenna cut for 28.5 MHz? | 
 |  | 8 feet
 |  | 11 feet
 |  | 16 feet
 |  | 21 feet
 | G9B12 ~ What is the approximate length for a 1/4 wave vertical antenna cut for 28.5 MHz? | 
 |  | 11 feet
 |  | 16 feet
 |  | 21 feet
 | G9B12 ~ What is the approximate length for a 1/4 wave vertical antenna cut for 28.5 MHz? | 
 | A. | 8 feet
 | B. | 11 feet
 | C. | 16 feet
 | D. | 21 feet
Antennas and Feed Lines
Group G9B

## Slide 444
G9C01 | G9C15
G9C02 | G9C16
G9C03 | G9C17
G9C04 | G9C18
G9C05 | G9C19
G9C06 | G9C20
G9C07 | 
G9C08 | 
G9C09 | 
G9C10 | 
G9C11 | 
G9C12 | 
G9C13 | 
G9C14 | 
Antennas and Feed Lines
Group G9C (20 Questions)
Directional antennas
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 445
 | G9C01 ~ Which of the following would increase the bandwidth of a Yagi antenna? | 
 |  | Larger diameter elements
 |  | Closer element spacing
 |  | Loading coils in series with the element
 |  | Tapered-diameter elements
 | G9C01 ~ Which of the following would increase the bandwidth of a Yagi antenna? | 
 |  | Closer element spacing
 |  | Loading coils in series with the element
 |  | Tapered-diameter elements
 | G9C01 ~ Which of the following would increase the bandwidth of a Yagi antenna? | 
 | A. | Larger diameter elements
 | B. | Closer element spacing
 | C. | Loading coils in series with the element
 | D. | Tapered-diameter elements
Antennas and Feed Lines
Group G9C

## Slide 446
 | G9C02 ~ What is the approximate length of the driven element of a Yagi antenna? | 
 |  | 1/4 wavelength
 |  | 1/2 wavelength
 |  | 3/4 wavelength
 |  | 1 wavelength
 | G9C02 ~ What is the approximate length of the driven element of a Yagi antenna? | 
 |  | 1/4 wavelength
 |  | 3/4 wavelength
 |  | 1 wavelength
 | G9C02 ~ What is the approximate length of the driven element of a Yagi antenna? | 
 | A. | 1/4 wavelength
 | B. | 1/2 wavelength
 | C. | 3/4 wavelength
 | D. | 1 wavelength
Antennas and Feed Lines
Group G9C

## Slide 447
 | G9C03 ~ Which statement about a three-element, single-band Yagi antenna is true? | 
 |  | The reflector is normally the shortest element
 |  | The director is normally the shortest element
 |  | The driven element is the longest element
 |  | Low feed point impedance increases bandwidth
 | G9C03 ~ Which statement about a three-element, single-band Yagi antenna is true? | 
 |  | The reflector is normally the shortest element
 |  | The driven element is the longest element
 |  | Low feed point impedance increases bandwidth
 | G9C03 ~ Which statement about a three-element, single-band Yagi antenna is true? | 
 | A. | The reflector is normally the shortest element
 | B. | The director is normally the shortest element
 | C. | The driven element is the longest element
 | D. | Low feed point impedance increases bandwidth
Antennas and Feed Lines
Group G9C

## Slide 448
 | G9C04 ~ Which statement about a three-element, single-band Yagi antenna is true? | 
 |  | The reflector is normally the longest element
 |  | The director is normally the longest element
 |  | The reflector is normally the shortest element
 |  | All of the elements must be the same length
 | G9C04 ~ Which statement about a three-element, single-band Yagi antenna is true? | 
 |  | The director is normally the longest element
 |  | The reflector is normally the shortest element
 |  | All of the elements must be the same length
 | G9C04 ~ Which statement about a three-element, single-band Yagi antenna is true? | 
 | A. | The reflector is normally the longest element
 | B. | The director is normally the longest element
 | C. | The reflector is normally the shortest element
 | D. | All of the elements must be the same length
Antennas and Feed Lines
Group G9C

## Slide 449
 | G9C05 ~ How does increasing boom length and adding directors affect a Yagi antenna? | 
 |  | Gain increases
 |  | Beamwidth increases
 |  | Front to back ratio decreases
 |  | Front to side ratio decreases
 | G9C05 ~ How does increasing boom length and adding directors affect a Yagi antenna? | 
 |  | Beamwidth increases
 |  | Front to back ratio decreases
 |  | Front to side ratio decreases
 | G9C05 ~ How does increasing boom length and adding directors affect a Yagi antenna? | 
 | A. | Gain increases
 | B. | Beamwidth increases
 | C. | Front to back ratio decreases
 | D. | Front to side ratio decreases
Antennas and Feed Lines
Group G9C

## Slide 450
 | G9C06 ~ What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector? | 
 |  | The driven element must be fed with a balun transformer
 |  | There must be an open circuit in the driven element at the point opposite the feed point
 |  | The reflector element must be approximately 5 percent shorter than the driven element
 |  | The reflector element must be approximately 5 percent longer than the driven element
 | G9C06 ~ What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector? | 
 |  | The driven element must be fed with a balun transformer
 |  | There must be an open circuit in the driven element at the point opposite the feed point
 |  | The reflector element must be approximately 5 percent shorter than the driven element
 | G9C06 ~ What configuration of the loops of a two-element quad antenna must be used for the antenna to operate as a beam antenna, assuming one of the elements is used as a reflector? | 
 | A. | The driven element must be fed with a balun transformer
 | B. | There must be an open circuit in the driven element at the point opposite the feed point
 | C. | The reflector element must be approximately 5 percent shorter than the driven element
 | D. | The reflector element must be approximately 5 percent longer than the driven element
Antennas and Feed Lines
Group G9C

## Slide 451
 | G9C07 ~ What does "front-to-back ratio" mean in reference to a Yagi antenna? | 
 |  | The number of directors versus the number of reflectors
 |  | The relative position of the driven element with respect to the reflectors and directors
 |  | The power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction
 |  | The ratio of forward gain to dipole gain
 | G9C07 ~ What does "front-to-back ratio" mean in reference to a Yagi antenna? | 
 |  | The number of directors versus the number of reflectors
 |  | The relative position of the driven element with respect to the reflectors and directors
 |  | The ratio of forward gain to dipole gain
 | G9C07 ~ What does "front-to-back ratio" mean in reference to a Yagi antenna? | 
 | A. | The number of directors versus the number of reflectors
 | B. | The relative position of the driven element with respect to the reflectors and directors
 | C. | The power radiated in the major radiation lobe compared to the power radiated in exactly the opposite direction
 | D. | The ratio of forward gain to dipole gain
Antennas and Feed Lines
Group G9C

## Slide 452
 | G9C08 ~ What is meant by the "main lobe" of a directive antenna? | 
 |  | The magnitude of the maximum vertical angle of radiation
 |  | The point of maximum current in a radiating antenna element
 |  | The maximum voltage standing wave point on a radiating element
 |  | The direction of maximum radiated field strength from the antenna
 | G9C08 ~ What is meant by the "main lobe" of a directive antenna? | 
 |  | The magnitude of the maximum vertical angle of radiation
 |  | The point of maximum current in a radiating antenna element
 |  | The maximum voltage standing wave point on a radiating element
 | G9C08 ~ What is meant by the "main lobe" of a directive antenna? | 
 | A. | The magnitude of the maximum vertical angle of radiation
 | B. | The point of maximum current in a radiating antenna element
 | C. | The maximum voltage standing wave point on a radiating element
 | D. | The direction of maximum radiated field strength from the antenna
Antennas and Feed Lines
Group G9C

## Slide 453
 | G9C09 ~ How does the gain of two 3-element horizontally polarized Yagi antennas spaced vertically 1/2 wavelength apart typically compare to the gain of a single 3-element Yagi? | 
 |  | Approximately 1.5 dB higher
 |  | Approximately 3 dB higher
 |  | Approximately 6 dB higher
 |  | Approximately 9 dB higher
 | G9C09 ~ How does the gain of two 3-element horizontally polarized Yagi antennas spaced vertically 1/2 wavelength apart typically compare to the gain of a single 3-element Yagi? | 
 |  | Approximately 1.5 dB higher
 |  | Approximately 6 dB higher
 |  | Approximately 9 dB higher
 | G9C09 ~ How does the gain of two 3-element horizontally polarized Yagi antennas spaced vertically 1/2 wavelength apart typically compare to the gain of a single 3-element Yagi? | 
 | A. | Approximately 1.5 dB higher
 | B. | Approximately 3 dB higher
 | C. | Approximately 6 dB higher
 | D. | Approximately 9 dB higher
Antennas and Feed Lines
Group G9C

## Slide 454
 | G9C10 ~ Which of the following is a Yagi antenna design variable that could be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth? | 
 |  | The physical length of the boom
 |  | The number of elements on the boom
 |  | The spacing of each element along the boom
 |  | All of these choices are correct
 | G9C10 ~ Which of the following is a Yagi antenna design variable that could be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth? | 
 |  | The physical length of the boom
 |  | The number of elements on the boom
 |  | The spacing of each element along the boom
 | G9C10 ~ Which of the following is a Yagi antenna design variable that could be adjusted to optimize forward gain, front-to-back ratio, or SWR bandwidth? | 
 | A. | The physical length of the boom
 | B. | The number of elements on the boom
 | C. | The spacing of each element along the boom
 | D. | All of these choices are correct
Antennas and Feed Lines
Group G9C

## Slide 455
 | G9C11 ~ What is the purpose of a gamma match used with Yagi antennas? | 
 |  | To match the relatively low feed point impedance to 50 ohms
 |  | To match the relatively high feed point impedance to 50 ohms
 |  | To increase the front-to-back ratio
 |  | To increase the main lobe gain
 | G9C11 ~ What is the purpose of a gamma match used with Yagi antennas? | 
 |  | To match the relatively high feed point impedance to 50 ohms
 |  | To increase the front-to-back ratio
 |  | To increase the main lobe gain
 | G9C11 ~ What is the purpose of a gamma match used with Yagi antennas? | 
 | A. | To match the relatively low feed point impedance to 50 ohms
 | B. | To match the relatively high feed point impedance to 50 ohms
 | C. | To increase the front-to-back ratio
 | D. | To increase the main lobe gain
Antennas and Feed Lines
Group G9C

## Slide 456
 | G9C12 ~ Which of the following is an advantage of using a gamma match for impedance matching of a Yagi antenna to 50 ohm coax feed line? | 
 |  | It does not require that the elements be insulated from the boom
 |  | It does not require any inductors or capacitors
 |  | It is useful for matching multiband antennas
 |  | All of these choices are correct
 | G9C12 ~ Which of the following is an advantage of using a gamma match for impedance matching of a Yagi antenna to 50 ohm coax feed line? | 
 |  | It does not require any inductors or capacitors
 |  | It is useful for matching multiband antennas
 |  | All of these choices are correct
 | G9C12 ~ Which of the following is an advantage of using a gamma match for impedance matching of a Yagi antenna to 50 ohm coax feed line? | 
 | A. | It does not require that the elements be insulated from the boom
 | B. | It does not require any inductors or capacitors
 | C. | It is useful for matching multiband antennas
 | D. | All of these choices are correct
Antennas and Feed Lines
Group G9C

## Slide 457
 | G9C13 ~ Approximately how long is each side of the driven element of a quad antenna? | 
 |  | 1/4 wavelength
 |  | 1/2 wavelength
 |  | 3/4 wavelength
 |  | 1 wavelength
 | G9C13 ~ Approximately how long is each side of the driven element of a quad antenna? | 
 |  | 1/2 wavelength
 |  | 3/4 wavelength
 |  | 1 wavelength
 | G9C13 ~ Approximately how long is each side of the driven element of a quad antenna? | 
 | A. | 1/4 wavelength
 | B. | 1/2 wavelength
 | C. | 3/4 wavelength
 | D. | 1 wavelength
Antennas and Feed Lines
Group G9C

## Slide 458
 | G9C14 ~ How does the forward gain of a two-element quad antenna compare to the forward gain of a three-element Yagi antenna? | 
 |  | About 2/3 as much
 |  | About the same
 |  | About 1.5 times as much
 |  | About twice as much
 | G9C14 ~ How does the forward gain of a two-element quad antenna compare to the forward gain of a three-element Yagi antenna? | 
 |  | About 2/3 as much
 |  | About 1.5 times as much
 |  | About twice as much
 | G9C14 ~ How does the forward gain of a two-element quad antenna compare to the forward gain of a three-element Yagi antenna? | 
 | A. | About 2/3 as much
 | B. | About the same
 | C. | About 1.5 times as much
 | D. | About twice as much
Antennas and Feed Lines
Group G9C

## Slide 459
 | G9C15 ~ Approximately how long is each side of the reflector element of a quad antenna? | 
 |  | Slightly less than 1/4 wavelength
 |  | Slightly more than 1/4 wavelength
 |  | Slightly less than 1/2 wavelength
 |  | Slightly more than 1/2 wavelength
 | G9C15 ~ Approximately how long is each side of the reflector element of a quad antenna? | 
 |  | Slightly less than 1/4 wavelength
 |  | Slightly less than 1/2 wavelength
 |  | Slightly more than 1/2 wavelength
 | G9C15 ~ Approximately how long is each side of the reflector element of a quad antenna? | 
 | A. | Slightly less than 1/4 wavelength
 | B. | Slightly more than 1/4 wavelength
 | C. | Slightly less than 1/2 wavelength
 | D. | Slightly more than 1/2 wavelength
Antennas and Feed Lines
Group G9C

## Slide 460
 | G9C16 ~ How does the gain of a two-element delta-loop beam compare to the gain of a two-element quad antenna? | 
 |  | 3 dB higher
 |  | 3 dB lower
 |  | 2.54 dB higher
 |  | About the same
 | G9C16 ~ How does the gain of a two-element delta-loop beam compare to the gain of a two-element quad antenna? | 
 |  | 3 dB higher
 |  | 3 dB lower
 |  | 2.54 dB higher
 | G9C16 ~ How does the gain of a two-element delta-loop beam compare to the gain of a two-element quad antenna? | 
 | A. | 3 dB higher
 | B. | 3 dB lower
 | C. | 2.54 dB higher
 | D. | About the same
Antennas and Feed Lines
Group G9C

## Slide 461
 | G9C17 ~ Approximately how long is each leg of a symmetrical delta-loop antenna? | 
 |  | 1/4 wavelength
 |  | 1/3 wavelength
 |  | 1/2 wavelength
 |  | 2/3 wavelength
 | G9C17 ~ Approximately how long is each leg of a symmetrical delta-loop antenna? | 
 |  | 1/4 wavelength
 |  | 1/2 wavelength
 |  | 2/3 wavelength
 | G9C17 ~ Approximately how long is each leg of a symmetrical delta-loop antenna? | 
 | A. | 1/4 wavelength
 | B. | 1/3 wavelength
 | C. | 1/2 wavelength
 | D. | 2/3 wavelength
Antennas and Feed Lines
Group G9C

## Slide 462
 | G9C18 ~ What happens when the feed point of a quad antenna of any shape is moved from the midpoint of the top or bottom to the midpoint of either side? | 
 |  | The polarization of the radiated signal changes from horizontal to vertical
 |  | The polarization of the radiated signal changes from vertical to horizontal
 |  | There is no change in polarization
 |  | The radiated signal becomes circularly polarized
 | G9C18 ~ What happens when the feed point of a quad antenna of any shape is moved from the midpoint of the top or bottom to the midpoint of either side? | 
 |  | The polarization of the radiated signal changes from vertical to horizontal
 |  | There is no change in polarization
 |  | The radiated signal becomes circularly polarized
 | G9C18 ~ What happens when the feed point of a quad antenna of any shape is moved from the midpoint of the top or bottom to the midpoint of either side? | 
 | A. | The polarization of the radiated signal changes from horizontal to vertical
 | B. | The polarization of the radiated signal changes from vertical to horizontal
 | C. | There is no change in polarization
 | D. | The radiated signal becomes circularly polarized
Antennas and Feed Lines
Group G9C

## Slide 463
 | G9C19 ~ How does antenna gain stated in dBi compare to gain stated in dBd for the same antenna? | 
 |  | dBi gain figures are 2.15 dB lower then dBd gain figures
 |  | dBi gain figures are 2.15 dB higher than dBd gain figures
 |  | dBi gain figures are the same as the square root of dBd gain figures multiplied by 2.15
 |  | dBi gain figures are the reciprocal of dBd gain figures + 2.15 dB
 | G9C19 ~ How does antenna gain stated in dBi compare to gain stated in dBd for the same antenna? | 
 |  | dBi gain figures are 2.15 dB lower then dBd gain figures
 |  | dBi gain figures are the same as the square root of dBd gain figures multiplied by 2.15
 |  | dBi gain figures are the reciprocal of dBd gain figures + 2.15 dB
 | G9C19 ~ How does antenna gain stated in dBi compare to gain stated in dBd for the same antenna? | 
 | A. | dBi gain figures are 2.15 dB lower then dBd gain figures
 | B. | dBi gain figures are 2.15 dB higher than dBd gain figures
 | C. | dBi gain figures are the same as the square root of dBd gain figures multiplied by 2.15
 | D. | dBi gain figures are the reciprocal of dBd gain figures + 2.15 dB
Antennas and Feed Lines
Group G9C

## Slide 464
 | G9C20 ~ What is meant by the terms dBi and dBd when referring to antenna gain? | 
 |  | dBi refers to an isotropic antenna, dBd refers to a dipole antenna
 |  | dBi refers to an ionospheric reflecting antenna, dBd refers to a dissipative antenna
 |  | dBi refers to an inverted-vee antenna, dBd refers to a downward reflecting antenna
 |  | dBi refers to an isometric antenna, dBd refers to a discone antenna
 | G9C20 ~ What is meant by the terms dBi and dBd when referring to antenna gain? | 
 |  | dBi refers to an ionospheric reflecting antenna, dBd refers to a dissipative antenna
 |  | dBi refers to an inverted-vee antenna, dBd refers to a downward reflecting antenna
 |  | dBi refers to an isometric antenna, dBd refers to a discone antenna
 | G9C20 ~ What is meant by the terms dBi and dBd when referring to antenna gain? | 
 | A. | dBi refers to an isotropic antenna, dBd refers to a dipole antenna
 | B. | dBi refers to an ionospheric reflecting antenna, dBd refers to a dissipative antenna
 | C. | dBi refers to an inverted-vee antenna, dBd refers to a downward reflecting antenna
 | D. | dBi refers to an isometric antenna, dBd refers to a discone antenna
Antennas and Feed Lines
Group G9C

## Slide 465
G9D01
G9D02
G9D03
G9D04
G9D05
G9D06
G9D07
G9D08
G9D09
G9D10
G9D11
Antennas and Feed Lines
Group G9D (11 Questions)
Specialized antennas
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 466
 | G9D01 ~ What does the term NVIS mean as related to antennas? | 
 |  | Nearly Vertical Inductance System
 |  | Non-Varying Indicated SWR
 |  | Non-Varying Impedance Smoothing
 |  | Near Vertical Incidence sky-wave
 | G9D01 ~ What does the term NVIS mean as related to antennas? | 
 |  | Nearly Vertical Inductance System
 |  | Non-Varying Indicated SWR
 |  | Non-Varying Impedance Smoothing
 | G9D01 ~ What does the term NVIS mean as related to antennas? | 
 | A. | Nearly Vertical Inductance System
 | B. | Non-Varying Indicated SWR
 | C. | Non-Varying Impedance Smoothing
 | D. | Near Vertical Incidence sky-wave
Antennas and Feed Lines
Group G9D

## Slide 467
 | G9D02 ~ Which of the following is an advantage of an NVIS antenna? | 
 |  | Low vertical angle radiation for working stations out to ranges of several thousand kilometers
 |  | High vertical angle radiation for working stations within a radius of a few hundred kilometers
 |  | High forward gain
 |  | All of these choices are correct
 | G9D02 ~ Which of the following is an advantage of an NVIS antenna? | 
 |  | Low vertical angle radiation for working stations out to ranges of several thousand kilometers
 |  | High forward gain
 |  | All of these choices are correct
 | G9D02 ~ Which of the following is an advantage of an NVIS antenna? | 
 | A. | Low vertical angle radiation for working stations out to ranges of several thousand kilometers
 | B. | High vertical angle radiation for working stations within a radius of a few hundred kilometers
 | C. | High forward gain
 | D. | All of these choices are correct
Antennas and Feed Lines
Group G9D

## Slide 468
 | G9D03 ~ At what height above ground is an NVIS antenna typically installed? | 
 |  | As close to 1/2 wavelength as possible
 |  | As close to one wavelength as possible
 |  | Height is not critical as long as it is significantly more than 1/2 wavelength
 |  | Between 1/10 and 1/4 wavelength
 | G9D03 ~ At what height above ground is an NVIS antenna typically installed? | 
 |  | As close to 1/2 wavelength as possible
 |  | As close to one wavelength as possible
 |  | Height is not critical as long as it is significantly more than 1/2 wavelength
 | G9D03 ~ At what height above ground is an NVIS antenna typically installed? | 
 | A. | As close to 1/2 wavelength as possible
 | B. | As close to one wavelength as possible
 | C. | Height is not critical as long as it is significantly more than 1/2 wavelength
 | D. | Between 1/10 and 1/4 wavelength
Antennas and Feed Lines
Group G9D

## Slide 469
 | G9D04 ~ What is the primary purpose of antenna traps? | 
 |  | To permit multiband operation
 |  | To notch spurious frequencies
 |  | To provide balanced feed point impedance
 |  | To prevent out of band operation
 | G9D04 ~ What is the primary purpose of antenna traps? | 
 |  | To notch spurious frequencies
 |  | To provide balanced feed point impedance
 |  | To prevent out of band operation
 | G9D04 ~ What is the primary purpose of antenna traps? | 
 | A. | To permit multiband operation
 | B. | To notch spurious frequencies
 | C. | To provide balanced feed point impedance
 | D. | To prevent out of band operation
Antennas and Feed Lines
Group G9D

## Slide 470
 | G9D05 ~ What is an advantage of vertical stacking of horizontally polarized Yagi antennas? | 
 |  | It allows quick selection of vertical or horizontal polarization
 |  | It allows simultaneous vertical and horizontal polarization
 |  | It narrows the main lobe in azimuth
 |  | It narrows the main lobe in elevation
 | G9D05 ~ What is an advantage of vertical stacking of horizontally polarized Yagi antennas? | 
 |  | It allows quick selection of vertical or horizontal polarization
 |  | It allows simultaneous vertical and horizontal polarization
 |  | It narrows the main lobe in azimuth
 | G9D05 ~ What is an advantage of vertical stacking of horizontally polarized Yagi antennas? | 
 | A. | It allows quick selection of vertical or horizontal polarization
 | B. | It allows simultaneous vertical and horizontal polarization
 | C. | It narrows the main lobe in azimuth
 | D. | It narrows the main lobe in elevation
Antennas and Feed Lines
Group G9D

## Slide 471
 | G9D06 ~ Which of the following is an advantage of a log periodic antenna? | 
 |  | Wide bandwidth
 |  | Higher gain per element than a Yagi antenna
 |  | Harmonic suppression
 |  | Polarization diversity
 | G9D06 ~ Which of the following is an advantage of a log periodic antenna? | 
 |  | Higher gain per element than a Yagi antenna
 |  | Harmonic suppression
 |  | Polarization diversity
 | G9D06 ~ Which of the following is an advantage of a log periodic antenna? | 
 | A. | Wide bandwidth
 | B. | Higher gain per element than a Yagi antenna
 | C. | Harmonic suppression
 | D. | Polarization diversity
Antennas and Feed Lines
Group G9D

## Slide 472
 | G9D07 ~ Which of the following describes a log periodic antenna? | 
 |  | Length and spacing of the elements increase logarithmically from one end of the boom to the other
 |  | Impedance varies periodically as a function of frequency
 |  | Gain varies logarithmically as a function of frequency
 |  | SWR varies periodically as a function of boom length
 | G9D07 ~ Which of the following describes a log periodic antenna? | 
 |  | Impedance varies periodically as a function of frequency
 |  | Gain varies logarithmically as a function of frequency
 |  | SWR varies periodically as a function of boom length
 | G9D07 ~ Which of the following describes a log periodic antenna? | 
 | A. | Length and spacing of the elements increase logarithmically from one end of the boom to the other
 | B. | Impedance varies periodically as a function of frequency
 | C. | Gain varies logarithmically as a function of frequency
 | D. | SWR varies periodically as a function of boom length
Antennas and Feed Lines
Group G9D

## Slide 473
 | G9D08 ~ Why is a Beverage antenna not used for transmitting? | 
 |  | Its impedance is too low for effective matching
 |  | It has high losses compared to other types of antennas
 |  | It has poor directivity
 |  | All of these choices are correct
 | G9D08 ~ Why is a Beverage antenna not used for transmitting? | 
 |  | Its impedance is too low for effective matching
 |  | It has poor directivity
 |  | All of these choices are correct
 | G9D08 ~ Why is a Beverage antenna not used for transmitting? | 
 | A. | Its impedance is too low for effective matching
 | B. | It has high losses compared to other types of antennas
 | C. | It has poor directivity
 | D. | All of these choices are correct
Antennas and Feed Lines
Group G9D

## Slide 474
 | G9D09 ~ Which of the following is an application for a Beverage antenna? | 
 |  | Directional transmitting for low HF bands
 |  | Directional receiving for low HF bands
 |  | Portable direction finding at higher HF frequencies
 |  | Portable direction finding at lower HF frequencies
 | G9D09 ~ Which of the following is an application for a Beverage antenna? | 
 |  | Directional transmitting for low HF bands
 |  | Portable direction finding at higher HF frequencies
 |  | Portable direction finding at lower HF frequencies
 | G9D09 ~ Which of the following is an application for a Beverage antenna? | 
 | A. | Directional transmitting for low HF bands
 | B. | Directional receiving for low HF bands
 | C. | Portable direction finding at higher HF frequencies
 | D. | Portable direction finding at lower HF frequencies
Antennas and Feed Lines
Group G9D

## Slide 475
 | G9D10 ~ Which of the following describes a Beverage antenna? | 
 |  | A vertical antenna
 |  | A broad-band mobile antenna
 |  | A helical antenna for space reception
 |  | A very long and low directional receiving antenna
 | G9D10 ~ Which of the following describes a Beverage antenna? | 
 |  | A vertical antenna
 |  | A broad-band mobile antenna
 |  | A helical antenna for space reception
 | G9D10 ~ Which of the following describes a Beverage antenna? | 
 | A. | A vertical antenna
 | B. | A broad-band mobile antenna
 | C. | A helical antenna for space reception
 | D. | A very long and low directional receiving antenna
Antennas and Feed Lines
Group G9D

## Slide 476
 | G9D11 ~ Which of the following is a disadvantage of multiband antennas? | 
 |  | They present low impedance on all design frequencies
 |  | They must be used with an antenna tuner
 |  | They must be fed with open wire line
 |  | They have poor harmonic rejection
 | G9D11 ~ Which of the following is a disadvantage of multiband antennas? | 
 |  | They present low impedance on all design frequencies
 |  | They must be used with an antenna tuner
 |  | They must be fed with open wire line
 | G9D11 ~ Which of the following is a disadvantage of multiband antennas? | 
 | A. | They present low impedance on all design frequencies
 | B. | They must be used with an antenna tuner
 | C. | They must be fed with open wire line
 | D. | They have poor harmonic rejection
Antennas and Feed Lines
Group G9D

## Slide 477
Group |  | Questions
G0A | RF safety principles, rules and guidelines; routine station evaluation | 12
G0B | Safety in the ham shack: electrical shock and treatment, safety grounding, fusing, interlocks, wiring, antenna and tower safety | 15
2 | Total | 27
Subelement G0 Electrical and RF Safety
Notes: This slide lists all Groups in the current Subelement. The first column contains clickable hyperlinks for easy access to each Group.

## Slide 478
G0A01
G0A02
G0A03
G0A04
G0A05
G0A06
G0A07
G0A08
G0A09
G0A10
G0A11
G0A12
Electrical and RF Safety
Group G0A (12 Questions)
RF safety principles, rules and guidelines; routine station evaluation
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 479
 | G0A01 ~ What is one way that RF energy can affect human body tissue? | 
 |  | It heats body tissue
 |  | It causes radiation poisoning
 |  | It causes the blood count to reach a dangerously low level
 |  | It cools body tissue
 | G0A01 ~ What is one way that RF energy can affect human body tissue? | 
 |  | It causes radiation poisoning
 |  | It causes the blood count to reach a dangerously low level
 |  | It cools body tissue
 | G0A01 ~ What is one way that RF energy can affect human body tissue? | 
 | A. | It heats body tissue
 | B. | It causes radiation poisoning
 | C. | It causes the blood count to reach a dangerously low level
 | D. | It cools body tissue
Electrical and RF Safety
Group G0A

## Slide 480
 | G0A02 ~ Which of the following properties is important in estimating whether an RF signal exceeds the maximum permissible exposure (MPE)? | 
 |  | Its duty cycle
 |  | Its frequency
 |  | Its power density
 |  | All of these choices are correct
 | G0A02 ~ Which of the following properties is important in estimating whether an RF signal exceeds the maximum permissible exposure (MPE)? | 
 |  | Its duty cycle
 |  | Its frequency
 |  | Its power density
 | G0A02 ~ Which of the following properties is important in estimating whether an RF signal exceeds the maximum permissible exposure (MPE)? | 
 | A. | Its duty cycle
 | B. | Its frequency
 | C. | Its power density
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0A

## Slide 481
 | G0A03 ~ How can you determine that your station complies with FCC RF exposure regulations? | 
 |  | By calculation based on FCC OET Bulletin 65
 |  | By calculation based on computer modeling
 |  | By measurement of field strength using calibrated equipment
 |  | All of these choices are correct
 | FCC | 97.13(c)(1)
 | G0A03 ~ How can you determine that your station complies with FCC RF exposure regulations? | 
 |  | By calculation based on FCC OET Bulletin 65
 |  | By calculation based on computer modeling
 |  | By measurement of field strength using calibrated equipment
 | G0A03 ~ How can you determine that your station complies with FCC RF exposure regulations? | 
 | A. | By calculation based on FCC OET Bulletin 65
 | B. | By calculation based on computer modeling
 | C. | By measurement of field strength using calibrated equipment
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0A

## Slide 482
 | G0A04 ~ What does "time averaging" mean in reference to RF radiation exposure? | 
 |  | The average amount of power developed by the transmitter over a specific 24 hour period
 |  | The average time it takes RF radiation to have any long-term effect on the body
 |  | The total time of the exposure
 |  | The total RF exposure averaged over a certain time
 | G0A04 ~ What does "time averaging" mean in reference to RF radiation exposure? | 
 |  | The average amount of power developed by the transmitter over a specific 24 hour period
 |  | The average time it takes RF radiation to have any long-term effect on the body
 |  | The total time of the exposure
 | G0A04 ~ What does "time averaging" mean in reference to RF radiation exposure? | 
 | A. | The average amount of power developed by the transmitter over a specific 24 hour period
 | B. | The average time it takes RF radiation to have any long-term effect on the body
 | C. | The total time of the exposure
 | D. | The total RF exposure averaged over a certain time
Electrical and RF Safety
Group G0A

## Slide 483
 | G0A05 ~ What must you do if an evaluation of your station shows RF energy radiated from your station exceeds permissible limits? | 
 |  | Take action to prevent human exposure to the excessive RF fields
 |  | File an Environmental Impact Statement (EIS-97) with the FCC
 |  | Secure written permission from your neighbors to operate above the controlled MPE limits
 |  | All of these choices are correct
 | G0A05 ~ What must you do if an evaluation of your station shows RF energy radiated from your station exceeds permissible limits? | 
 |  | File an Environmental Impact Statement (EIS-97) with the FCC
 |  | Secure written permission from your neighbors to operate above the controlled MPE limits
 |  | All of these choices are correct
 | G0A05 ~ What must you do if an evaluation of your station shows RF energy radiated from your station exceeds permissible limits? | 
 | A. | Take action to prevent human exposure to the excessive RF fields
 | B. | File an Environmental Impact Statement (EIS-97) with the FCC
 | C. | Secure written permission from your neighbors to operate above the controlled MPE limits
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0A

## Slide 484
 | G0A06 ~ What precaution should be taken when installing a ground-mounted antenna? | 
 |  | It should not be installed higher than you can reach
 |  | It should not be installed in a wet area
 |  | It should limited to 10 feet in height
 |  | It should be installed such that it is protected against unauthorized access
 | G0A06 ~ What precaution should be taken when installing a ground-mounted antenna? | 
 |  | It should not be installed higher than you can reach
 |  | It should not be installed in a wet area
 |  | It should limited to 10 feet in height
 | G0A06 ~ What precaution should be taken when installing a ground-mounted antenna? | 
 | A. | It should not be installed higher than you can reach
 | B. | It should not be installed in a wet area
 | C. | It should limited to 10 feet in height
 | D. | It should be installed such that it is protected against unauthorized access
Electrical and RF Safety
Group G0A

## Slide 485
 | G0A07 ~ What effect does transmitter duty cycle have when evaluating RF exposure? | 
 |  | A lower transmitter duty cycle permits greater short-term exposure levels
 |  | A higher transmitter duty cycle permits greater short-term exposure levels
 |  | Low duty cycle transmitters are exempt from RF exposure evaluation requirements
 |  | High duty cycle transmitters are exempt from RF exposure requirements
 | G0A07 ~ What effect does transmitter duty cycle have when evaluating RF exposure? | 
 |  | A higher transmitter duty cycle permits greater short-term exposure levels
 |  | Low duty cycle transmitters are exempt from RF exposure evaluation requirements
 |  | High duty cycle transmitters are exempt from RF exposure requirements
 | G0A07 ~ What effect does transmitter duty cycle have when evaluating RF exposure? | 
 | A. | A lower transmitter duty cycle permits greater short-term exposure levels
 | B. | A higher transmitter duty cycle permits greater short-term exposure levels
 | C. | Low duty cycle transmitters are exempt from RF exposure evaluation requirements
 | D. | High duty cycle transmitters are exempt from RF exposure requirements
Electrical and RF Safety
Group G0A

## Slide 486
 | G0A08 ~ Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations when transmitter power exceeds levels specified in FCC Part 97.13? | 
 |  | Post a copy of FCC Part 97.13 in the station
 |  | Post a copy of OET Bulletin 65 in the station
 |  | Perform a routine RF exposure evaluation
 |  | All of these choices are correct
 | G0A08 ~ Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations when transmitter power exceeds levels specified in FCC Part 97.13? | 
 |  | Post a copy of FCC Part 97.13 in the station
 |  | Post a copy of OET Bulletin 65 in the station
 |  | All of these choices are correct
 | G0A08 ~ Which of the following steps must an amateur operator take to ensure compliance with RF safety regulations when transmitter power exceeds levels specified in FCC Part 97.13? | 
 | A. | Post a copy of FCC Part 97.13 in the station
 | B. | Post a copy of OET Bulletin 65 in the station
 | C. | Perform a routine RF exposure evaluation
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0A

## Slide 487
 | G0A09 ~ What type of instrument can be used to accurately measure an RF field? | 
 |  | A receiver with an S meter
 |  | A calibrated field strength meter with a calibrated antenna
 |  | An SWR meter with a peak-reading function
 |  | An oscilloscope with a high-stability crystal marker generator
 | G0A09 ~ What type of instrument can be used to accurately measure an RF field? | 
 |  | A receiver with an S meter
 |  | An SWR meter with a peak-reading function
 |  | An oscilloscope with a high-stability crystal marker generator
 | G0A09 ~ What type of instrument can be used to accurately measure an RF field? | 
 | A. | A receiver with an S meter
 | B. | A calibrated field strength meter with a calibrated antenna
 | C. | An SWR meter with a peak-reading function
 | D. | An oscilloscope with a high-stability crystal marker generator
Electrical and RF Safety
Group G0A

## Slide 488
 | G0A10 ~ What is one thing that can be done if evaluation shows that a neighbor might receive more than the allowable limit of RF exposure from the main lobe of a directional antenna? | 
 |  | Change to a non-polarized antenna with higher gain
 |  | Post a warning sign that is clearly visible to the neighbor
 |  | Use an antenna with a higher front-to-back ratio
 |  | Take precautions to ensure that the antenna cannot be pointed in their direction
 | G0A10 ~ What is one thing that can be done if evaluation shows that a neighbor might receive more than the allowable limit of RF exposure from the main lobe of a directional antenna? | 
 |  | Change to a non-polarized antenna with higher gain
 |  | Post a warning sign that is clearly visible to the neighbor
 |  | Use an antenna with a higher front-to-back ratio
 | G0A10 ~ What is one thing that can be done if evaluation shows that a neighbor might receive more than the allowable limit of RF exposure from the main lobe of a directional antenna? | 
 | A. | Change to a non-polarized antenna with higher gain
 | B. | Post a warning sign that is clearly visible to the neighbor
 | C. | Use an antenna with a higher front-to-back ratio
 | D. | Take precautions to ensure that the antenna cannot be pointed in their direction
Electrical and RF Safety
Group G0A

## Slide 489
 | G0A11 ~ What precaution should you take if you install an indoor transmitting antenna? | 
 |  | Locate the antenna close to your operating position to minimize feed line radiation
 |  | Position the antenna along the edge of a wall to reduce parasitic radiation
 |  | Make sure that MPE limits are not exceeded in occupied areas
 |  | Make sure the antenna is properly shielded
 | G0A11 ~ What precaution should you take if you install an indoor transmitting antenna? | 
 |  | Locate the antenna close to your operating position to minimize feed line radiation
 |  | Position the antenna along the edge of a wall to reduce parasitic radiation
 |  | Make sure the antenna is properly shielded
 | G0A11 ~ What precaution should you take if you install an indoor transmitting antenna? | 
 | A. | Locate the antenna close to your operating position to minimize feed line radiation
 | B. | Position the antenna along the edge of a wall to reduce parasitic radiation
 | C. | Make sure that MPE limits are not exceeded in occupied areas
 | D. | Make sure the antenna is properly shielded
Electrical and RF Safety
Group G0A

## Slide 490
 | G0A12 ~ What precaution should you take whenever you make adjustments or repairs to an antenna? | 
 |  | Ensure that you and the antenna structure are grounded
 |  | Turn off the transmitter and disconnect the feed line
 |  | Wear a radiation badge
 |  | All of these choices are correct
 | G0A12 ~ What precaution should you take whenever you make adjustments or repairs to an antenna? | 
 |  | Ensure that you and the antenna structure are grounded
 |  | Wear a radiation badge
 |  | All of these choices are correct
 | G0A12 ~ What precaution should you take whenever you make adjustments or repairs to an antenna? | 
 | A. | Ensure that you and the antenna structure are grounded
 | B. | Turn off the transmitter and disconnect the feed line
 | C. | Wear a radiation badge
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0A

## Slide 491
G0B01 | G0B15
G0B02 | 
G0B03 | 
G0B04 | 
G0B05 | 
G0B06 | 
G0B07 | 
G0B08 | 
G0B09 | 
G0B10 | 
G0B11 | 
G0B12 | 
G0B13 | 
G0B14 | 
Electrical and RF Safety
Group G0B (15 Questions)
Safety in the ham shack: electrical shock and treatment, safety grounding, fusing, interlocks, wiring, antenna and tower safety
Notes: This slide summarizes the current Group. On the right is a list of hyperlinks to each question in the current Group.

## Slide 492
 | G0B01 ~ Which wire or wires in a four-conductor connection should be attached to fuses or circuit breakers in a device operated from a 240 VAC single phase source? | 
 |  | Only the two wires carrying voltage
 |  | Only the neutral wire
 |  | Only the ground wire
 |  | All wires
 | G0B01 ~ Which wire or wires in a four-conductor connection should be attached to fuses or circuit breakers in a device operated from a 240 VAC single phase source? | 
 |  | Only the neutral wire
 |  | Only the ground wire
 |  | All wires
 | G0B01 ~ Which wire or wires in a four-conductor connection should be attached to fuses or circuit breakers in a device operated from a 240 VAC single phase source? | 
 | A. | Only the two wires carrying voltage
 | B. | Only the neutral wire
 | C. | Only the ground wire
 | D. | All wires
Electrical and RF Safety
Group G0B

## Slide 493
 | G0B02 ~ What is the minimum wire size that may be safely used for a circuit that draws up to 20 amperes of continuous current? | 
 |  | AWG number 20
 |  | AWG number 16
 |  | AWG number 12
 |  | AWG number 8
 | G0B02 ~ What is the minimum wire size that may be safely used for a circuit that draws up to 20 amperes of continuous current? | 
 |  | AWG number 20
 |  | AWG number 16
 |  | AWG number 8
 | G0B02 ~ What is the minimum wire size that may be safely used for a circuit that draws up to 20 amperes of continuous current? | 
 | A. | AWG number 20
 | B. | AWG number 16
 | C. | AWG number 12
 | D. | AWG number 8
Electrical and RF Safety
Group G0B

## Slide 494
 | G0B03 ~ Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring? | 
 |  | 100 amperes
 |  | 60 amperes
 |  | 30 amperes
 |  | 15 amperes
 | G0B03 ~ Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring? | 
 |  | 100 amperes
 |  | 60 amperes
 |  | 30 amperes
 | G0B03 ~ Which size of fuse or circuit breaker would be appropriate to use with a circuit that uses AWG number 14 wiring? | 
 | A. | 100 amperes
 | B. | 60 amperes
 | C. | 30 amperes
 | D. | 15 amperes
Electrical and RF Safety
Group G0B

## Slide 495
 | G0B04 ~ Which of the following is a primary reason for not placing a gasoline-fueled generator inside an occupied area? | 
 |  | Danger of carbon monoxide poisoning
 |  | Danger of engine over torque
 |  | Lack of oxygen for adequate combustion
 |  | Lack of nitrogen for adequate combustion
 | G0B04 ~ Which of the following is a primary reason for not placing a gasoline-fueled generator inside an occupied area? | 
 |  | Danger of engine over torque
 |  | Lack of oxygen for adequate combustion
 |  | Lack of nitrogen for adequate combustion
 | G0B04 ~ Which of the following is a primary reason for not placing a gasoline-fueled generator inside an occupied area? | 
 | A. | Danger of carbon monoxide poisoning
 | B. | Danger of engine over torque
 | C. | Lack of oxygen for adequate combustion
 | D. | Lack of nitrogen for adequate combustion
Electrical and RF Safety
Group G0B

## Slide 496
 | G0B05 ~ Which of the following conditions will cause a Ground Fault Circuit Interrupter (GFCI) to disconnect the 120 or 240 Volt AC line power to a device? | 
 |  | Current flowing from one or more of the voltage-carrying wires to the neutral wire
 |  | Current flowing from one or more of the voltage-carrying wires directly to ground
 |  | Overvoltage on the voltage-carrying wires
 |  | All of these choices are correct
 | G0B05 ~ Which of the following conditions will cause a Ground Fault Circuit Interrupter (GFCI) to disconnect the 120 or 240 Volt AC line power to a device? | 
 |  | Current flowing from one or more of the voltage-carrying wires to the neutral wire
 |  | Overvoltage on the voltage-carrying wires
 |  | All of these choices are correct
 | G0B05 ~ Which of the following conditions will cause a Ground Fault Circuit Interrupter (GFCI) to disconnect the 120 or 240 Volt AC line power to a device? | 
 | A. | Current flowing from one or more of the voltage-carrying wires to the neutral wire
 | B. | Current flowing from one or more of the voltage-carrying wires directly to ground
 | C. | Overvoltage on the voltage-carrying wires
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0B

## Slide 497
 | G0B06 ~ Why must the metal enclosure of every item of station equipment be grounded? | 
 |  | It prevents a blown fuse in the event of an internal short circuit
 |  | It prevents signal overload
 |  | It ensures that the neutral wire is grounded
 |  | It ensures that hazardous voltages cannot appear on the chassis
 | G0B06 ~ Why must the metal enclosure of every item of station equipment be grounded? | 
 |  | It prevents a blown fuse in the event of an internal short circuit
 |  | It prevents signal overload
 |  | It ensures that the neutral wire is grounded
 | G0B06 ~ Why must the metal enclosure of every item of station equipment be grounded? | 
 | A. | It prevents a blown fuse in the event of an internal short circuit
 | B. | It prevents signal overload
 | C. | It ensures that the neutral wire is grounded
 | D. | It ensures that hazardous voltages cannot appear on the chassis
Electrical and RF Safety
Group G0B

## Slide 498
 | G0B07 ~ Which of these choices should be observed when climbing a tower using a safety belt or harness? | 
 |  | Never lean back and rely on the belt alone to support your weight
 |  | Confirm that the belt is rated for the weight of the climber and that it is within its allowable service life
 |  | Ensure that all heavy tools are securely fastened to the belt D-ring
 |  | All of these choices are correct
 | G0B07 ~ Which of these choices should be observed when climbing a tower using a safety belt or harness? | 
 |  | Never lean back and rely on the belt alone to support your weight
 |  | Ensure that all heavy tools are securely fastened to the belt D-ring
 |  | All of these choices are correct
 | G0B07 ~ Which of these choices should be observed when climbing a tower using a safety belt or harness? | 
 | A. | Never lean back and rely on the belt alone to support your weight
 | B. | Confirm that the belt is rated for the weight of the climber and that it is within its allowable service life
 | C. | Ensure that all heavy tools are securely fastened to the belt D-ring
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0B

## Slide 499
 | G0B08 ~ What should be done by any person preparing to climb a tower that supports electrically powered devices? | 
 |  | Notify the electric company that a person will be working on the tower
 |  | Make sure all circuits that supply power to the tower are locked out and tagged
 |  | Unground the base of the tower
 |  | All of these choices are correct
 | G0B08 ~ What should be done by any person preparing to climb a tower that supports electrically powered devices? | 
 |  | Notify the electric company that a person will be working on the tower
 |  | Unground the base of the tower
 |  | All of these choices are correct
 | G0B08 ~ What should be done by any person preparing to climb a tower that supports electrically powered devices? | 
 | A. | Notify the electric company that a person will be working on the tower
 | B. | Make sure all circuits that supply power to the tower are locked out and tagged
 | C. | Unground the base of the tower
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0B

## Slide 500
 | G0B09 ~ Why should soldered joints not be used with the wires that connect the base of a tower to a system of ground rods? | 
 |  | The resistance of solder is too high
 |  | Solder flux will prevent a low conductivity connection
 |  | Solder has too high a dielectric constant to provide adequate lightning protection
 |  | A soldered joint will likely be destroyed by the heat of a lightning strike
 | G0B09 ~ Why should soldered joints not be used with the wires that connect the base of a tower to a system of ground rods? | 
 |  | The resistance of solder is too high
 |  | Solder flux will prevent a low conductivity connection
 |  | Solder has too high a dielectric constant to provide adequate lightning protection
 | G0B09 ~ Why should soldered joints not be used with the wires that connect the base of a tower to a system of ground rods? | 
 | A. | The resistance of solder is too high
 | B. | Solder flux will prevent a low conductivity connection
 | C. | Solder has too high a dielectric constant to provide adequate lightning protection
 | D. | A soldered joint will likely be destroyed by the heat of a lightning strike
Electrical and RF Safety
Group G0B

## Slide 501
 | G0B10 ~ Which of the following is a danger from lead-tin solder? | 
 |  | Lead can contaminate food if hands are not washed carefully after handling the solder
 |  | High voltages can cause lead-tin solder to disintegrate suddenly
 |  | Tin in the solder can "cold flow" causing shorts in the circuit
 |  | RF energy can convert the lead into a poisonous gas
 | G0B10 ~ Which of the following is a danger from lead-tin solder? | 
 |  | High voltages can cause lead-tin solder to disintegrate suddenly
 |  | Tin in the solder can "cold flow" causing shorts in the circuit
 |  | RF energy can convert the lead into a poisonous gas
 | G0B10 ~ Which of the following is a danger from lead-tin solder? | 
 | A. | Lead can contaminate food if hands are not washed carefully after handling the solder
 | B. | High voltages can cause lead-tin solder to disintegrate suddenly
 | C. | Tin in the solder can "cold flow" causing shorts in the circuit
 | D. | RF energy can convert the lead into a poisonous gas
Electrical and RF Safety
Group G0B

## Slide 502
 | G0B11 ~ Which of the following is good practice for lightning protection grounds? | 
 |  | They must be bonded to all buried water and gas lines
 |  | Bends in ground wires must be made as close as possible to a right angle
 |  | Lightning grounds must be connected to all ungrounded wiring
 |  | They must be bonded together with all other grounds
 | G0B11 ~ Which of the following is good practice for lightning protection grounds? | 
 |  | They must be bonded to all buried water and gas lines
 |  | Bends in ground wires must be made as close as possible to a right angle
 |  | Lightning grounds must be connected to all ungrounded wiring
 | G0B11 ~ Which of the following is good practice for lightning protection grounds? | 
 | A. | They must be bonded to all buried water and gas lines
 | B. | Bends in ground wires must be made as close as possible to a right angle
 | C. | Lightning grounds must be connected to all ungrounded wiring
 | D. | They must be bonded together with all other grounds
Electrical and RF Safety
Group G0B

## Slide 503
 | G0B12 ~ What is the purpose of a power supply interlock? | 
 |  | To prevent unauthorized changes to the circuit that would void the manufacturer's warranty
 |  | To shut down the unit if it becomes too hot
 |  | To ensure that dangerous voltages are removed if the cabinet is opened
 |  | To shut off the power supply if too much voltage is produced
 | G0B12 ~ What is the purpose of a power supply interlock? | 
 |  | To prevent unauthorized changes to the circuit that would void the manufacturer's warranty
 |  | To shut down the unit if it becomes too hot
 |  | To shut off the power supply if too much voltage is produced
 | G0B12 ~ What is the purpose of a power supply interlock? | 
 | A. | To prevent unauthorized changes to the circuit that would void the manufacturer's warranty
 | B. | To shut down the unit if it becomes too hot
 | C. | To ensure that dangerous voltages are removed if the cabinet is opened
 | D. | To shut off the power supply if too much voltage is produced
Electrical and RF Safety
Group G0B

## Slide 504
 | G0B13 ~ What must you do when powering your house from an emergency generator? | 
 |  | Disconnect the incoming utility power feed
 |  | Insure that the generator is not grounded
 |  | Insure that all lightning grounds are disconnected
 |  | All of these choices are correct
 | G0B13 ~ What must you do when powering your house from an emergency generator? | 
 |  | Insure that the generator is not grounded
 |  | Insure that all lightning grounds are disconnected
 |  | All of these choices are correct
 | G0B13 ~ What must you do when powering your house from an emergency generator? | 
 | A. | Disconnect the incoming utility power feed
 | B. | Insure that the generator is not grounded
 | C. | Insure that all lightning grounds are disconnected
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0B

## Slide 505
 | G0B14 ~ Which of the following is covered by the National Electrical Code? | 
 |  | Acceptable bandwidth limits
 |  | Acceptable modulation limits
 |  | Electrical safety inside the ham shack
 |  | RF exposure limits of the human body
 | G0B14 ~ Which of the following is covered by the National Electrical Code? | 
 |  | Acceptable bandwidth limits
 |  | Acceptable modulation limits
 |  | RF exposure limits of the human body
 | G0B14 ~ Which of the following is covered by the National Electrical Code? | 
 | A. | Acceptable bandwidth limits
 | B. | Acceptable modulation limits
 | C. | Electrical safety inside the ham shack
 | D. | RF exposure limits of the human body
Electrical and RF Safety
Group G0B

## Slide 506
 | G0B15 ~ Which of the following is true of an emergency generator installation? | 
 |  | The generator should be located in a well-ventilated area
 |  | The generator must be insulated from ground
 |  | Fuel should be stored near the generator for rapid refueling in case of an emergency
 |  | All of these choices are correct
 | G0B15 ~ Which of the following is true of an emergency generator installation? | 
 |  | The generator must be insulated from ground
 |  | Fuel should be stored near the generator for rapid refueling in case of an emergency
 |  | All of these choices are correct
 | G0B15 ~ Which of the following is true of an emergency generator installation? | 
 | A. | The generator should be located in a well-ventilated area
 | B. | The generator must be insulated from ground
 | C. | Fuel should be stored near the generator for rapid refueling in case of an emergency
 | D. | All of these choices are correct
Electrical and RF Safety
Group G0B

## Slide 507: The End Is your brain full yet?